## Slide 1
Material Handling Equipment
Module 3
Rigging Equipment
OSHA 1910.184 Slings: governs slings made from alloy steel chain, wire rope, metal mesh, natural or synthetic fiber rope, and synthetic web.
http://www.thefabricator.com/article/materialshandling/understanding-lift-magnet-compliance
0

## Slide 2
Material Handling and Storage
Module 3
To safely use slings take the following precautions:
A competent person should conduct inspections of slings before and during use
Remove damaged or defective slings from service
Source 1910.84(d)

## Slide 3
Material Handling and Storage
Module 3
To safely use slings take the following precautions:
 “Do not kink sling legs
 Do not load slings beyond their rated capacity
 Keep suspended loads clear of all obstructions
 Remain clear of loads about to be lifted and
suspended
 Do not engage in shock loading
 Avoid sudden crane acceleration and deceleration
when moving suspended loads”
 Do not use knots or bolts or other makeshift devices
to shorten slings
https://www.osha.gov/Publications/OSHA2236/osha2236.html

## Slide 4
Material Handling Equipment
Module 3
Chains
Overhead crane, chain, hook and hardware used
to move beams during fabrication

## Slide 5
Material Handling Equipment
Module 3
Chains
Inspect prior to use – each shift and during use
Discard defective equipment
Do not over load rigging
Specialized Hooks – clamps – should be proof tested
https://www.osha.gov/dsg/guidance/slings/alloy.html
Chain marking
Do not use because of different
Grade of material

## Slide 6
Material Handling Equipment
Module 3
ID tag attached
Listing -- size, grade, rated capacity & Mfg
Hook – ring – load rating not less than chain’s rating
No make shift equipment – hook, rods, bolts
When to discard chain?
Wear exceeds limits of 1910 Table N-184-1
Inspections based on:
  Frequency of use
  At least yearly
  Severity of service
Nature of lift
Use common sense
Document dates of inspection
5
ID Attached to hook

## Slide 7
Material Handling Equipment
Module 3 Chains
Job or shop hooks and links or makeshift fasteners are not allowed
Use the correct size pin for the job
6
Right
Wrong

## Slide 8
Material Handling Equipment
Module 3 Chains
AISC has a daily chain inspection form available at it’s website
http://www.aisc.org/content.aspx?id=31828
7

## Slide 9
Module 3 Wire rope
Cover/protect protruding ends of strands from splices
Lubricate – protect wire rope
Splice requirements
Use wire rope ‘U-bolt’ clamp
Check load capacity tables
End attachments need to be
proof tested
Wire rope end attachment
Material Handling Equipment

## Slide 10
Wire rope
Do not pull sling from under
loads
Do not use if:
  More than 10% of visible
  strands are broken
  Signs of excess wear,
  corrosion, or defect
  Protect slings from
  sharp edges
  Sling – wires are kinked
Material Handling Equipment
Module 3
Remove from service

## Slide 11
Wire rope
Crushing
If these happen, remove the wire rope sling from service
Kinking
Bird Caging

## Slide 12
Material Handling Equipment
Module 3 Wire Ropes
AISC has a wire rope inspection form posted at it’s website
http://www.aisc.org/content.aspx?id=31828
11

## Slide 13
Synthetic Web Slings Remove from service if any of these are present:
Acid or caustic burns
Melting or charring of any part
Snags, punctures, tears or cuts
Broken or worn stitches
Red core warning thread visible
Distortion of fittings
Material Handling Equipment
Module 3
Heat Damage
Red core waning thread visible
https://www.osha.gov/dsg/guidance/slings/synth-web.html
12

## Slide 14
Synthetic web
Mfg identification tag attached & legible
Tag list rated capacity for type of hitch used
Avoid sharp edges and high temperature with sling
Material Handling Equipment
Module 3
Look for sling ID tag
13
Pending photo approval

## Slide 15
Module 3
Synthetic Web Slings
Fittings must be:
At least as strong as that
of the sling
Free of sharp edges that could damage the webbing
https://www.osha.gov/dsg/guidance/slings/synth-web.html , 1910.184(i)
14
Material Handling and Storage

## Slide 16
15
Stitching
https://www.osha.gov/dsg/guidance/slings/synth-web.html , 1910.184(i)
Synthetic Web Sling Stitching
Stitching is the only method allowed to attach end fittings to webbing, or to form eyes
Material Handling and Storage
Module 3

## Slide 17
16
Nylon-Slings.com Erie, PA
Material Handling and Storage
Module 3

## Slide 18
Inspect slings:
Each day before use
Where service conditions warrant
Remove them from service if damaged or defective
or the red core warning thread is visible
https://www.osha.gov/dsg/guidance/slings/synth-web.html , 1910.184(i)
17
Material Handling and Storage
Module 3

## Slide 19
Module 3
AISC has a synthetic sling inspection form on its website
http://www.aisc.org/content.aspx?id=31828
Material Handling and Storage

## Slide 20
Questions on slings and rigging?
Material Handling and Storage
Module 3

## Slide 21: Material Handling and Storage Module 3
Movement at Ground or Floor Level
♦
♦
♦
♦
♦
♦
♦
♦
♦

## Slide 22
Movement at Floor or Ground Level-Key Topics
Powered Industrial Trucks-(Forklifts)
Material Handling and Storage
Module 3
Drawings from
https://www.osha.gov/SLTC/etools/pit/forklift/types/classes.html#class1

## Slide 23
Material Handling Equipment
Module 3
Powered Industrial Trucks (Forklifts)
Hazard: “Approximately 100 employees are fatally injured and approximately 95,000 employees are injured every year while operating powered industrial trucks.”
“Forklift turnover accounts
for a significant number of
these fatalities.”
https://www.osha.gov/Publications/OSHA3252/3252.html

## Slide 24
Material Handling and Storage
Module 3
https://www.osha.gov/Publications/OSHA3252/3252.html
Potential Hazards: Moving material within the shop-
Powered Industrial Trucks-(Forklifts)
Tipping, struck by caught between, wrong equipment for hazard classification
Hazard Avoidance:
Select proper equipment for application and hazard
Only qualified operators should use equipment
Check equipment before use
Do not overload
Center loads

## Slide 25
Material Handling and Storage
Module 3
https://www.osha.gov/Publications/OSHA3252/3252.html
Potential Hazards: Moving material within the shop-
Powered Industrial Trucks-(Forklifts)
Tipping, struck by caught between, wrong equipment for hazard classification
Hazard Avoidance:
Drive safely
No horseplay
Watch for obstructions
Do not leave unattended vehicles running
Proper maintenance

## Slide 26
Material Handling Equipment
Module 3
Powered Industrial Trucks (Forklifts)-Equipment
Powered industrial trucks (forklifts) must meet requirements of American National Standard for Powered Industrial Trucks, Part II ANSI B56.1-1969
Do not modify or make attachments without written approval from the manufacturer
Nameplates and markings must be in place and legible
Forklifts that are used in hazardous locations are required to be appropriately marked/approved for such use
https://www.osha.gov/Publications/OSHA2236/osha2236.html https://www.osha.gov/Publications/OSHA3252/3252.html

## Slide 27
Material Handling Equipment
https://www.osha.gov/Publications/OSHA3252/3252.html
Module 3
Powered Industrial Trucks (Forklifts)-Operator Qualifications
Train and certify all operators to ensure safe operation
Do not operate a forklift if under 18 years old
Must be competent
Trainees must be supervised by a competent person and not endanger others
Refresher training
Reevaluation every three years
Training requirements defined in 1910.178
https://www.osha.gov/Publications/OSHA2236/osha2236.html

## Slide 28
Material Handling Equipment
Module 3
Powered Industrial Trucks (Forklifts) Operation –before
you operate:
Check that rollover protective structure is in place
Check overhead guards are in place to protect from
falling objects
Reverse signal alarm should be operational
Check defects before using
Fill fuel tanks only when the engine is off
27
https://www.osha.gov/Publications/OSHA3252/3252.html

## Slide 29
Material Handling Equipment
Module 3
Powered Industrial Trucks (Forklifts) Operation-
Loads
Make sure loads are not heavier than the capacity of the industrial truck
Loads should be stable and safely arranged and within the
rated capacity of the truck
Follow safe operating procedures for picking up, moving, putting down and stacking loads
Center the load on the forks and as close to the mast as
possible to minimize tipping or load falling
Place the load at the lowest position for traveling
Don’t place extra weight on the rear of a counterbalanced forklift to allow an overload
Dock boards (bridge plates) are properly secured when
loading or unloading from loading docks
https://www.osha.gov/Publications/OSHA3252/3252.html

## Slide 30
Material Handling Equipment
Module 3
Powered Industrial Trucks (Forklifts) Operation-driving and operating
Drive safely-never over 5 mph- slow at congested areas
Always wear seat belts
Keep hands, arms legs and feet inside the truck
No riders unless there is an approved seat
Avoid traveling with elevated loads
Observe all traffic regulations and plant speed limits
Look in the direction of and keep a clear view of the path of travel
Run trucks at a safe speed that permits safe stopping
https://www.osha.gov/Publications/OSHA3252/3252.html

## Slide 31
Material Handling Equipment
Module 3
Powered Industrial Trucks (Forklifts) Operation-
Continued
Stunt driving and horseplay are prohibited
Check for headroom for the fork- lift under overhead installations, lights, pipes, etc
Operators maintain a safe distance from the edge of ramps or platforms while using forklifts on any elevated dock, platform or freight car
https://www.osha.gov/Publications/OSHA2236/osha2236.html https://www.osha.gov/Publications/warehousing.html https://www.osha.gov/SLTC/poweredindustrialtrucks/index.html
https://www.osha.gov/Publications/OSHA3252/3252.html

## Slide 32
Material Handling Equipment
Module 3
Powered Industrial Trucks (Forklifts) Source OSHA
Operation-Unattended vehicles
“Load engaging means should be fully lowered, with controls neutralized, power shut off and brakes set when a forklift is left unattended”
3220-10N 2004

## Slide 33
Material Handling Equipment
Module 3
Powered Industrial Trucks (Forklifts)-Maintenance
Properly maintain equipment, including tires and batteries
Remove defective forklifts from service
Handling batteries can be dangerous and requires special care and qualified personnel
Charge batteries in designated areas
.
3220-10N 2004
https://www.osha.gov/Publications/OSHA3252/3252.html

## Slide 34
Material Handling Equipment
Module 3
Powered Industrial
Trucks (Forklifts)
OSHA has a number
of helpful materials
available
https://www.osha.gov/SLTC/etools/pit/forklift/types/classes.html#class1

## Slide 35
Material Handling Equipment
Module 3
Powered Industrial trucks (Forklifts)
Forklift Safety
Safety and Health Topics: Powered Industrial Trucks OSHA website index links to specific requirements and other Federal agency requirements. https://www.osha.gov/SLTC/poweredindustrialtrucks/index.html
Sample Daily Checklists for Powered Industrial Trucks
https://www.osha.gov/dte/library/pit/daily_pit_checklist.html
3220-10N 2004
34

## Slide 36
Material Handling and Storage
Module 3
Movement at the Workstation-Key
Topics
♦
♦

## Slide 37
Movement at the Workstation-Key Topics
Jib Cranes
Carts
Hoist Balancers
Tool balancers
Material Handling and Storage
Module 3

## Slide 38
Material Handling and Storage
Module 3
Moving material at the work station
Steel may be moved at the work station or between work stations by:
Overhead cranes
Jib cranes
Rollers
Carts and dollies
Hoist balancers
Tool suspension devices
Workers or pairs of workers
Others in your shop?
Jib Crane
Roller system used to move material for fabrication

## Slide 39
Material Handling Equipment
Module 3
38
Lighten the Load- Use Material Handling Equipment
Photos from OSHA 3341-03N 2008
Hand carts for moving small materials in the shop
Pallet Jack

## Slide 40
Material Handling and Storage
Module 3
Potential Hazards: Moving material at the work station
Injuries from dropped work, pinches, cuts, scrapes,
burns from hot work, musculoskeletal injuries
Hazard Avoidance:
Use proper PPE for the task
Proper equipment use
Being aware
Being attentive of where your hands and feet are
Don’t work fatigued
Use proper lighting
Properly maintained equipment

## Slide 41
Material Handling Equipment
Module 3
Lighten the Load- Use Material Handling Equipment
Carts designed to transport and carry materials can reduce lifting, pushing, and pulling forces
Allow for heavy materials, tools, or equipment to be moved without carrying
Save time
Available in many shapes and sizes
Adapted from OSHA 3341-03N 2008

## Slide 42
Material Handling Equipment
Module 3
Carts
Hand cart for small loads Photo from CIANBRO
Drawing from: https://www.osha.gov/SLTC/etools/pit/forklift/types/classes.html#class1

## Slide 43
Material Handling Equipment
Module 3
Lighten the Load- Use Material Handling Equipment Points to Remember:
Motorized pallet jacks, if available, can be used for frequent or distant movement of materials. Handles should be located at the rear of the cart and positioned at waist level
Don’t obstruct view with the load
Balance loads and keep load within manufacturer’s recommended weight limits
Pushing is easier than pulling
Use proper wheels
Adapted from OSHA 3341-03N 2008

## Slide 44
Material Handling Equipment
Module 3
Jib Cranes
“Wall, floor, or pillar mounted I-beam with a rolling trolley/hoist used to lift and position equipment and material”
Jib cranes can be used near a work stations to help with tasks
Photo from OSHA 3341-03N 2008

## Slide 45
Material Handling Equipment
Module 3
Jib Cranes
AISC provides a useful pre-lift checklist. It is Included in the training packet.
http://www.aisc.org/content.aspx?id=31828

## Slide 46
Material Handling Equipment
Module 3
Jib Cranes
AISC pre-lift checklist continued
http://www.aisc.org/content.aspx?id=31828

## Slide 47
Material Handling Equipment
Module 3
Tool Balancers
Tool balancers help support tools comfortably for operators
Tools can be positioned over the work station
Can be used with a variety of
tools
Source CIANBRO

## Slide 48
Material Handling and Storage
Module 3
Storage and stacking of material
♦
♦
♦

## Slide 49
Storing Materials-Key Topics
Storing
Stacking
Housekeeping
48
Material Handling and Storage
Module 3
Fabricated beams and spandrel frames ready to be shipped to a construction site
Steel from the mill stored In the yard

## Slide 50
Material Handling and Storage
Module 3
Storing and stacking
Steel from the mill stored
Inside shop
Fabricated beams ready to be shipped
to construction site

## Slide 51
Material Handling Equipment
Module 3
Storage and stacking
Heavy steel shapes from the mill
Heavy plate from the mill

## Slide 52
Material Handling Equipment
Module 3
Hazard Potential: Stored materials
Improperly stored materials may fall, and injure workers
Improper manual lifting or carrying loads that are too large or heavy
Being struck by materials or being caught in pinch points
Incorrectly cutting ties or securing devices
Hazard Avoidance:
“Stack loads evenly and straight
Place heavier loads on lower or middle shelves and racks
Remove one object at a time from shelves and racks
Keep aisles and passageways clear and in good repair”
Non-compatible materials should not be stored together
51
Adapted from Source OSHA 3220-10N 2004

## Slide 53
Material Handling Equipment
Module 3
Materials Storage-Steel
American National Standard Z229.1-1982 lays out practices for steel fabrication and shops fabricating structural steel
Included in ANSI Z229.1- 1982 are practices for handling and storing steel material
Steel shapes stacked and nested
Adapted from source: ANSI Z229.1-1982
52

## Slide 54
Material Handling Equipment
Module 3
Store material in arrangements that allow for:
Easy movement
Easy access and movement
Materials and stacks to be stable
Racks used for storing plate and bar stock
53
Adapted from source: ANSI Z229.1-1982

## Slide 55
Material Handling Equipment
Module 3
Structural shapes received
from the mill
54
Can be nested or blocked
Optimize pile height for space and
stability
ANSI Z229.1-1982 suggested maximum pile heights for wide flange shapes 6-8” deep should be limited to 6’-0” in height for shapes 10-16”, 11’-0” in height and for 18- 36”, is 14 ‘-0” feet in height.
Under general industry standards If workers must work on loads higher than 4 feet, fall protection is
required
Nested wide flange shapes
Adapted from source: ANSI Z229.1-1982

## Slide 56
Material Handling Equipment
Adapted from source: ANSI Z229.1-1982
Module 3
Materials Storage - storage yards and storage areas
Store material on level surfaces free of trip hazards
Maintain walkways
Store on firm ground
In periods of freezing and thaws inspect areas for stability
Maintain approach aisles to piles
Use sound timber blocking for storing steel shapes to maintain pile stability
Do not extend blocking beyond piles interfering with walkways and adjacent lifts

## Slide 57
Material Handling Equipment
Module 3
Stacking
The variety of raw and fabricated steel shapes at the shop require planning and care when stacking

## Slide 58
Material Handling Equipment
Module 3
Use of wood blocking between beam material
Wood blocking used between shapes
Wood Blocking

## Slide 59
Material Handling Equipment
Module 3
Stacking Small steel items – angles

## Slide 60
Material Handling Equipment
Module 3
Stacking Steel Pipe
Round HSS steel shapes should be blocked,
placed in racks or cribbing or bundled and tied together
Blocking
Round HSS shapes stored for fabrication
–blocking is used to prevent shapes from rolling

## Slide 61
Material Handling Equipment
Module 3
60
String coils
Steel coils should be blocked to prevent movement
Steel coils weighing 10 tons are blocked to prevent rolling
Tapered Blocking

## Slide 62
Material Handling Equipment
Module 3
Materials Storage
Secure materials stored in tiers by stacking, racking, blocking, or interlocking to prevent them from falling
Post safe load limits of floors and shelves.
Source OSHA 3220-10N 2004

## Slide 63
Material Handling Equipment
Module 3
Materials Storage-Fuels
Store fuel in portable containers
Transportation of gasoline requires USDOT container
Tank size – 8 gallon or less
Approved OSHA can
Approved USDOT – (stamp-imprint)
Diesel fuel containers
Tank size – 119 gallons or less
Except from using specified container

## Slide 64
Material Handling Equipment
Module 3
Q and A
Storing
Materials

## Slide 65: Take a Stretch!
Material Handling Equipment
Module 3