## Slide 1: Fundamentals of Steel Bridge Engineering
Lesson 6 – Flexure Part 1
Fundamental Calculations
Notes: This presentation is part of the "Fundamentals of Steel Bridge Engineering" teaching aid, available at aisc.org/teachingaids. This set of (14) lessons was prepared by Frank Russo, PE, PhD and Michael Grubb, PE with support from the National Steel Bridge Alliance (NSBA) and AISC University Programs. For questions or comments on these presentations, please contact: AISC University Programs universityprograms@aisc.org

## Slide 2: Reference Materials
SBDH Vol 4
  Section 2.2 General I-Section Stringer Systems
  Section 6.3 I-Section Flexural Members
SBDH Vol 8
  Section 3.0 Behavior Considerations
SBDH Vol 20 – Design Example 1
Notes: The following references are companion to this lesson:
SBDH Vol 4 – Section 2.2, General I-Section Stringer Systems, Section 6.3, I-Section Flexural Members
SBDH Vol 8 – Section 3.0 – Behavior Considerations
SBDH Vol 20 – Design Example 1 – various sections

## Slide 3: Lesson 6 Roadmap – Flexure Part 1 Fundamental Calculations
Composite vs. Noncomposite
Elastic Section Properties
Elastic Stresses in Composite Sections
Plastic Section Properties
Flange Lateral Bending
Flange-Stress Reduction Factors
Tension Flanges with Holes
Notes: Lesson 6 is the first of five lessons dealing with the design of steel-bridge flexural members. The discussions in these lessons will focus primarily on the design of I-section flexural members. This first lesson deals with important fundamental calculations that are employed for the design of these members. These calculations and concepts will be employed throughout the remaining four lessons of this course dealing with the design of I-section flexural members.
Topics to be covered in this lesson include a discussion on the distinction between composite and noncomposite members/sections. This topic will also cover the distinction between unshored and shored construction of steel bridges. The computation of elastic section properties and elastic stresses in composite sections will be discussed next, which covers extremely important concepts that will be commonly utilized in the design of these members. The computation of plastic section properties will then be described. These computations are employed in the design of specific classifications of sections in flexural members. The fundamentals of torsion, including the calculation of flange lateral bending moments and stresses in I-section flexural members, will be described next. Finally, the calculation of two important flange-stress reduction factors employed in the computation of the nominal flexural resistance of these members will be described, followed by a brief discussion on the design of tension flanges of flexural members with holes.

## Slide 4: Composite vs. Noncomposite
Notes: The first topic in this lesson will cover the distinction between composite and noncomposite members/sections. The topic will also introduce the concepts of unshored and shored construction of steel bridges.

## Slide 5: Composite vs. Noncomposite
Composite
Noncomposite
Notes: A composite beam or girder is a steel flexural member connected to a hardened cast-in-place or precast concrete deck so that the steel beam or girder and concrete deck, or the longitudinal reinforcement within the deck, respond to the force effects as a unit. Composite action is ensured by the use of mechanical shear connectors between the girder and the deck. The shear connectors transfer horizontal shear from the deck to the girder and prevent slip between the concrete and the steel parallel to the girder. This ensures a linear strain distribution from the top of the deck to the bottom of the girder and creates a single neutral axis. The design of shear connectors will be covered in Lesson 9.
A noncomposite beam or girder is a steel flexural member that is not connected to a hardened cast-in-place concrete deck by shear connectors. Therefore, slip occurs between the two components. Although permitted by specification, it is not recommended. Unintended composite action does occur but is conservatively ignored; the stiffness of the concrete is ignored in computing the elastic section properties for design. Some Owners specify that shear connectors be omitted in regions of negative flexure in continuous spans resulting in portions of the member being noncomposite in those regions. However, the beam or girder is still considered to be a composite beam or girder in regions with shear connectors. A steel flexural member with shear connectors that supports a wet cast-in-place concrete deck during the deck placement is a noncomposite beam or girder during that temporary construction condition. Some steel bridges have decks that cannot be made composite, such as steel grid decks for moveable bridges or low volume roads with timber decks (Lesson 14).

## Slide 6: Composite Construction
Notes: Composite action is provided through the use of welded shear studs. With a common diameter of 7/8 in., these are installed in groups of several studs placed transverse to the flange and spaced along the length of the beam. They are then cast into the concrete deck. They provide the mechanical connection between the concrete deck and the steel beam needed for composite action. Their design is based on meeting strength requirements, a function of force transfer between the deck and the beam, and also fatigue requirements that ensure the welds between the shear stud and the girder top flange do not cause cracking of the beam flange over time or fail the connection between the stud and the flange.
Photo credits: HDR

## Slide 7: Unshored Construction
No support of the steel beam or girder during the deck placement (other than at permanent support points)
Bare steel beam or girder resists all the permanent load before the deck hardens or is made composite
Composite beam or girder resists all permanent and transient loads after the deck hardens or is made composite
Notes: In unshored construction, there is no support of the steel beam or girder (other than at permanent support points) provided during the concrete deck placement. It is assumed there are no temporary supports used during construction. The bare steel beam or girder resists all the permanent loads applied before the concrete deck has hardened or is made composite. The composite beam or girder resists all the permanent and transient loads applied after the concrete deck has hardened or is made composite. Unshored construction is the most commonly used method of steel beam or girder construction and the most economical. Shoring is not required, and dead load deflections are much better predicted.
Photo Credit: Genesis Structures

## Slide 8: Shored Construction
Beam supported along its entire length during the deck placement
Composite beam or girder resists all the permanent and transient loads
Sometimes used in concrete bridge construction
Not used for steel bridge construction except for beam erection
Shoring for a concrete bridge
Notes: In shored construction, the steel beam or girder would be supported along its entire length by shoring during the concrete deck placement, similar to shored concrete box girder construction that is sometimes used (shown in the photograph on this slide). The composite beam or girder would then resist all the permanent and transient loads.
While shored construction is permitted according to the AASHTO Specifications, its use is not recommended. There has been limited research on the effects of concrete creep on composite steel girders under large dead loads. Also, there have been only a very limited number of demonstration bridges built with shored construction in the U.S. Furthermore, there is an increased likelihood of significant tensile stresses occurring in the concrete deck at permanent interior supports of continuous spans when shored construction is used. The AASHTO Specifications may not be sufficient for shored construction where close tolerances on the girder cambers are important.

## Slide 9: ELASTIC Section properties
Notes: The next topic in this lesson covers the computation of the elastic section properties of noncomposite and composite sections in flexural members. Included in the discussion for composite sections are separate discussions on the effective deck width, the modular ratio, the effects of concrete creep and shrinkage, the concept of a transformed composite section, and the minimum 1 percent longitudinal concrete deck reinforcement utilized for crack control in continuous-span members. Finally, the topic concludes with a discussion on the composite stiffness to be assumed for analysis of flexural members.

## Slide 10: Noncomposite Rolled W Shapes
Notes: Elastic section properties for noncomposite rolled wide-flange (W) shapes are tabulated in the AISC Steel Construction Manual. Shown in the shaded box are the section properties for a W36 x 330 rolled wide-flange shape.

## Slide 11: Noncomposite Rolled W Shapes
W36 x 330 – 36" nominal depth; 330 lbs/ft
Doubly symmetric
D/tw ≤ 60
W24 to W44 for bridge stringers/beams
120 ft maximum length – varies by section size
Span 20 ft to 30 ft when used as substringers between welded girders in larger bridges
Notes: Rolled wide-flange (W) shapes are designated by the nominal depth and weight per foot; e.g., a W36 X 330 is nominally 36 inches deep and weighs 330 lbs/ft. Wide-flange sections are doubly symmetric and have relatively thick webs compared to most welded I-shaped sections. The maximum web depth-to-thickness ratio is approximately 60 or less. The wide-flange sections used for bridge stringers/beams typically range between 24-inch and the deepest shapes available domestically, which have a 44-inch nominal depth. The maximum available length of rolled wide-flange shapes is approximately 120 feet and varies by section size.

## Slide 12: Substringer Example
Substringers span the short distance between the cross-frames
Used to support the slab at close intervals
Notes: One application of rolled beams is for use as substringers between welded girders in larger bridges. In these structures, the rolled beams usually span between 20 and 30 feet and are supported on cross-frames that are bolted to deep widely spaced welded girders. The substringers support the concrete deck and allow for the use of a typical deck thickness. Another use would be to span between floor beams in a truss, an arch, or a cable stayed or suspension bridge.

## Slide 13: Noncomposite Rolled W Shapes
Section Properties of Greatest Interest:
A = cross-sectional area (in.2)
d = actual depth (in.)
Ix = moment of inertia taken about the X-X (major) axis (in.4)
Iy = moment of inertia about the Y-Y (minor) axis (in.4)
Sx= elastic section modulus taken about the X-X (major) axis = Ix/(d/2) (in.3)
Zx= plastic section modulus taken about the X-X (major) axis (in.3)
rx= radius of gyration about the X-X (major) axis = (in.)
ry = radius of gyration about the Y-Y (minor) axis = (in.)
J = St. Venant torsional constant (in.4)
Notes: Sections properties of noncomposite rolled W shapes of greatest interest in design applications include:
A = cross-sectional area (in.2)
d = actual depth (in.)
Ix = moment of inertia taken about the X-X (major) axis (in.4)
Iy = moment of inertia about the Y-Y (minor) axis (in.4)
Sx= elastic section modulus taken about the X-X (major) axis = Ix/(d/2) (in.3)
Zx= plastic section modulus taken about the X-X (major) axis (in.3)
rx= radius of gyration about the X-X (major) axis = (in.)
ry = radius of gyration about the Y-Y (minor) axis = (in.)
J = St. Venant torsional constant (in.4)
Sections properties of noncomposite rolled W shapes of greatest interest in design applications include:
A = cross-sectional area (in.2)
d = actual depth (in.)
Ix = moment of inertia taken about the X-X (major) axis (in.4)
Iy = moment of inertia about the Y-Y (minor) axis (in.4)
Sx= elastic section modulus taken about the X-X (major) axis = Ix/(d/2) (in.3)
Zx= plastic section modulus taken about the X-X (major) axis (in.3)
rx= radius of gyration about the X-X (major) axis = √(𝐼_𝑥∕𝐴) (in.)
ry = radius of gyration about the Y-Y (minor) axis = √(𝐼_𝑦∕𝐴) (in.)
J = St. Venant torsional constant (in.4)

## Slide 14: Noncomposite Welded I-Girders
Often singly symmetric in bridge applications
Parallel Axis Theorem – may be employed in the computation of Ix and the resulting section moduli
The moment of inertia of an area with respect to any axis in its plane is equal to the moment of inertia with respect to a parallel centroidal axis, Io, plus the product of the area and the square of the distance, d, between the two axes. For an I-girder, the resulting moments of inertia of the flanges and web are summed to calculate Ix.
Notes: Noncomposite welded I-girders are often singly symmetric in bridge applications. To calculate the moment of inertia of the girder about the X-X (major) axis, Ix, the parallel axis theorem may be employed. This theorem states in general that “the moment of inertia of an area with respect to any axis in its plane is equal to the moment of inertia with respect to a parallel centroidal axis, Io, plus the product of the area and the square of the distance, d, between the two axes”. For an I-girder, the resulting moments of inertia of the flanges and web are summed to calculate Ix.

## Slide 15: Noncomposite Welded I-Girders
Example – taken from NSBA SBDH Design Example 1 (positive moment section – exterior girder)
Section is singly symmetric
Calculate the elastic section properties for the noncomposite steel girder section
Notes: To illustrate these concepts, the moment of inertia, Ix, and the resulting section moduli will be computed for the section shown, which is taken from Design Example 1 of the NSBA Steel Bridge Design Handbook (SBDH). The girder is an exterior girder, and the section is in a positive moment region in the end span of the three-span continuous girder. The section is singly symmetric. The section properties will be computed for the noncomposite steel section only.

## Slide 16: Noncomposite Welded I-Girders
Calculate the location of the centroidal (neutral) axis of the steel girder section (measured from the mid-depth of the web):
“A” is the area of a component
“d” is the distance of the cg of that component to the cg of the web
Notes: First, calculate the location, ds, of the centroidal (neutral) axis of the steel girder section measured from the mid-depth of the web. ds is computed as the summation of the first moments of the flanges and web about the mid-depth of the web divided by the total area of the section, where d is the distance from the mid-depth of the web to the centroidal (neutral) axis of each component of the cross-section. Note that the sign of d must be considered in this calculation. Since the centroidal axis of the web is located at the mid-depth of the web, d is taken equal to zero for the web. The resulting value of ds is -6.76 inches; that is, the centroidal axis of the steel girder section is located 6.76 inches below the mid-depth of the web.

## Slide 17: Noncomposite Welded I-Girders
Using the Parallel Axis Theorem, calculate Ix and the resulting section moduli for the steel girder section:
Notes: Next, using the Parallel Axis Theorem, calculate Ix and the resulting section moduli of the steel girder section. The distances, d, from the centroidal (neutral) axis of the steel girder section (located 6.76 inches below the mid-depth of the web) to the centroidal axis of each component area (i.e., the flanges and web) are calculated. The product of Ad2 is then added to the moment of inertia, Io, of each component area about its own centroidal axis (Io = bh3/12) to obtain Ix for each component area. These moments of inertia are then summed to give the total Ix for the steel girder section. The section moduli to the top and bottom of the steel girder section are then computed as Ix divided by the respective distances from the centroidal axis to the top and bottom of the steel girder section.

## Slide 18: Composite Sections
Composite sections in positive bending
  Effective deck width
  Modular ratio
  Effects of concrete creep
Composite sections in negative bending
  Minimum longitudinal concrete deck reinforcement
Notes: To compute the elastic section properties for composite sections in positive flexure, the effective deck width and modular ratio must be calculated. In addition, the effects of concrete creep must be accounted for when a composite steel girder section is subject to a constant sustained loading, such as permanent loads applied to the composite section (e.g., barriers, railings, wearing surface, etc.).
To compute the elastic section properties for composite sections in negative flexure in continuous-span beams or girders, assuming shear connectors are provided, the contribution of the minimum longitudinal concrete deck reinforcement may be considered. For composite sections in negative flexure, the concrete deck in tension is typically assumed to be cracked to a degree that it is assumed not to be participating in the resistance of moment at the strength limit state. An exception is permitted by AASHTO for design calculations at the service and fatigue limit states when certain conditions are met, as will be discussed further in Lesson 7.

## Slide 19: Effective Deck Width
Used for elastic section property calculations and for composite stiffness in line girder & traditional 2D grid analyses
Shear lag – longitudinal stresses across deck are non-uniform
Use an effective flange width assuming a uniform stress
Notes: In composite steel girders subject to major-axis bending, longitudinal stresses are distributed to the various components of the cross-section, including the concrete deck, by in-plane shear stresses resulting in shear deformations. As a result of the corresponding shear deformations in the deck, which is wider and less efficient than the steel girder in distributing the stresses, plane sections do not remain plane and the longitudinal stresses across the deck are non-uniform; a phenomenon referred to as shear lag.
The effective deck width is the width of deck over which the assumed uniformly distributed longitudinal stresses result in approximately the same deck force and member moments calculated from elementary beam theory (i.e., assuming plane sections remain plane) as would be produced by the actual non-uniform stress distribution.
The effective deck width is used to compute the elastic section properties of the composite section (and the resulting stresses acting on the composite section), and to compute the stiffness of the composite section for line girder and traditional 2D grid analyses.

## Slide 20: Effective Deck Width – BDS 4.6.2.6
The effective deck width, beff, is the corresponding tributary width of the deck perpendicular to the axis of the girder
Applies for conventional composite girder bridges where the largest skew angle Ɵ ≤ 75○
In other situations, determine by refined analysis
Notes: For conventional composite girder bridges (i.e., beam-slab bridges) in which the largest skew angle, , in the bridge system does not exceed 75 (measured relative to a normal to the centerline of the bridge), the effective deck width, beff, for determining cross-section stiffnesses for analysis and for determining flexural resistances may be taken as the corresponding tributary width of the deck perpendicular to the axis of the member. In other situations, the effective deck width should be determined by a refined analysis (consult AASHTO LRFD Article 4.6.2.6.1).

## Slide 21: Modular Ratio – BDS 6.10.1.1.1b
Used in the calculation of elastic section properties of composite sections in which the concrete deck is effective
Used to transform the concrete deck area into equivalent steel
Divide the effective deck width by the modular ratio
A common value for “n” is between 7 and 8
Notes: The elastic behavior of a composite girder in which the deck is considered effective is similar to the behavior of an equivalent homogenous steel girder composed of the actual steel girder and a transformed area of the concrete deck. The concrete deck in a composite section is transformed into equivalent steel.
The deck area is typically transformed by using a deck width equal to beff/n, where beff is the effective deck width and n is the modular ratio. The effective deck width is reduced rather than the deck thickness so as to have a less significant effect on the computed moment of inertia.
The modular ratio, n, is equal to the modulus of elasticity of steel, E, usually taken as 29,000 ksi, divided by the modulus of elasticity of concrete, Ec. For concrete unit weights, wc, between 0.090 and 0.155 kips/ft3, Ec may be calculated from the equation shown on the slide. For normal weight concrete, wc is usually taken as 0.145 kips/ft3 in the calculation of Ec. Rounding of n is permitted.
In relatively rare cases where the steel girder is relatively small in relation to the concrete deck, the elastic neutral axis of the transformed composite section may fall within the deck. Concrete on the tension side of the neutral axis is not to be considered effective at the strength limit state; the concrete below the neutral axis is assumed cracked in tension and therefore ineffective. Therefore, it should not be included in the calculation of the elastic section properties of the transformed composite section. The location of the neutral axis must be solved for in this case.

## Slide 22: Effects of Concrete Creep
Creep -> a time-dependent increase in concrete strain under a sustained long-term stress
Affects the stresses in a composite steel girder under sustained permanent loads (e.g., concrete barriers, railings, wearing surfaces)
Due to creep in the concrete deck, stresses in the steel girder increase and stresses in the concrete deck decrease
A long-term modular ratio, 3n, is used to account in an approximate fashion for the effects of concrete creep on steel-girder stresses
Notes: When concrete is placed under a sustained long-term stress, there is an instantaneous elastic strain, followed by a time-dependent increase in strain known as creep.
In a composite steel girder, due to the effects of creep in the concrete deck, the strain in the steel girder increases and the steel stresses become larger, while the strains and stresses in the concrete deck are reduced.
The actual calculation of creep stresses in composite girders is theoretically complex and not necessary for the design of composite steel girders. Instead, a simple approximate approach has been adopted for design in which a modular ratio appropriate to the duration of the load is used to compute the corresponding elastic section properties.
A so-called long-term modular ratio, 3n, is used to account in an approximate fashion for the effects of concrete creep on steel-girder stresses in a composite steel girder subject to a constant sustained loading (e.g., concrete barriers, railings and wearing surfaces). Effectively, the stiffness of the concrete deck is being reduced by 1/3 in the computation of the steel-girder stresses due to sustained permanent loads acting on the composite section. The effects of creep are usually conservatively ignored in the computation of the stresses in the concrete deck.

## Slide 23: Effects of Concrete Creep
Instantaneous deformation
Long-term deformation
Instantaneous deformation
Long-term deformation
Strain
Stress
ε
3ε
σ
Notes: A concrete column in compression is a useful tool to illustrate creep. Under an axial stress there is an initial elastic deformation. But due to creep, this initial displacement is amplified under time under the action of a constant and sustained stress. This initial and amplified displacement reduces the effective Modulus of Elasticity of the concrete. It is commonly assumed for steel bridge design that the sum of the initial and long- term strain is three times the original value. This is like saying the Modulus of the concrete is reduced by a factor of three.

## Slide 24: Effects of Concrete Shrinkage
Shrinkage -> as concrete cures, shrinkage occurs with time
The effects of concrete shrinkage on composite steel girders are less well understood than the effects of creep
The effects are often ignored in U.S. design practice
Some State DOTs require shrinkage to be included as part of camber considerations
Notes: As concrete cures, it will contract or shrink with time. Although shrinkage is included in most of the basic load combinations given in AASHTO LRFD Table 3.4.1-1, the effects of shrinkage on the behavior of composite steel girders are less well understood than creep and are often ignored in U.S. design practice as of this writing. However, some state DOTs require that shrinkage be included as part of the camber considerations.
As the concrete deck shrinks, it introduces compression in the flange attached to it in positive moment regions while corresponding tensile stresses are introduced in the concrete deck as long as there is no loss of bond between the two materials. The effect of the shortening of both the concrete deck and top flange is to generate a positive moment in the composite girder with its concomitant increase in deflection. The amount of deflection is a function of a number of parameters including the distance of the deck-flange interface from the neutral axis and the stiffness of both the deck and the girder. Shrinkage stresses cannot exceed the modulus of rupture of the deck concrete.
Although shrinkage increases the stresses in the girder, it does not appreciably diminish its capacity in positive moment regions because added dead and live load applied to the composite section will reverse the shrinkage stresses in the deck, which will release its pull on the girder. In the negative moment regions of a continuous girder, the deck concrete is neglected in determining the member flexural resistance at the strength limit state. Also, due to minor slip at the shear connectors between the slab and the steel girders and minor cracking in the slab, the shrinkage forces are not likely to be fully effective.

## Slide 25: Transformed Composite Sections BDS 6.10.1.11b
Long-term composite section (3n)
Short-term composite section (n)
Effective Flange Width
Effective Flange Width / 3n
Effective Flange Width
Effective Flange Width
/
n
Notes: For the determination of section properties for the computation of steel-girder stresses due to permanent loads applied to the composite section, the so-called long-term modular ratio of 3n is used. The deck is transformed into equivalent steel in this case by dividing the effective deck width by 3n.
For the determination of section properties for the computation of steel-girder stresses due to transient loads applied to the composite section (e.g., live loads), and for determining deck stresses due to both sustained permanent loads and transient loads, the so-called short-term modular ratio n is used. The deck is transformed into equivalent steel in this case by dividing the effective deck width by n.
Note that it is permitted to include the longitudinal reinforcement lying within the effective flange width in the computation of the long-term and short-term composite section properties. However, this reinforcement usually is not considered effective in compression at the strength limit state; therefore, its contribution is typically neglected in positive bending regions for strength limit state checks. Consideration may be given to including the longitudinal reinforcement in positive bending regions when computing stresses at the service and fatigue limit states.
Typically, the area of the concrete deck haunch is not considered in the computation of the composite section properties; the haunch depth may be considered, however, if permitted by the Owner.

## Slide 26: Composite Sections
Example – taken from NSBA SBDH Design Example 1 (positive moment section - exterior girder)
Calculate the elastic section properties for the long-term (3n) composite section and for the short-term (n) composite section
Use n = 8
Girder spacing = 12 ft
Deck overhang = 3.5 ft
Notes: To illustrate, the moment of inertia, Ix, and the resulting section moduli will be computed for the composite section shown, which is taken from Design Example 1 of the NSBA Steel Bridge Design Handbook (SBDH). The girder is an exterior girder, and the section is in a positive moment region in the end span of the three-span continuous girder. The section properties will be computed for the long-term (3n) composite section and for the short-term (n) composite section. A modular ratio, n, of 8 is assumed. The structural thickness of the concrete deck is 9.0 inches (i.e., a ½ in. integral wearing surface is subtracted from the total thickness of the deck), and the depth of the concrete haunch measured from the top of the web to the bottom of the deck is 3.5 inches. The contribution of the longitudinal reinforcement in the deck is ignored. The girder spacing is 12 ft and the deck overhang is 3.5 ft.

## Slide 27: Long-Term (3n) Composite Section
Calculate the effective deck width:
Calculate the location of the centroidal (neutral) axis of the composite section (measured from the mid-depth of the steel girder web):
Notes: First, calculate the effective deck width. The tributary width of the deck perpendicular to the longitudinal axis of the exterior girder is equal to one-half of the girder spacing plus the length of the deck overhang, or 114.0 inches.
Next, calculate the location, d3n, of the centroidal (neutral) axis of the composite section measured from the mid-depth of the steel girder web. d3n is computed as the summation of the first moments of the steel girder section and the transformed concrete deck about the mid-depth of the steel girder web divided by the total area of the transformed composite section, where d is the distance from the mid-depth of the steel girder web to the centroidal (neutral) axis of each component of the cross-section. Note that the sign of d must be considered in this calculation.
The area and first moment of the steel girder section were computed previously in this lesson. The area of the transformed concrete deck is equal to the structural thickness of the deck (9.0 inches) times the effective width of the deck (114.0 inches) divided by the modular ratio of 3n or 24. The distance from the mid-depth of the steel girder web to the mid-thickness of the concrete deck, considering the depth of the concrete haunch (3.5 inches) is 42.50 inches. The resulting value of d3n is 10.12 inches; that is, the centroidal axis of the composite section is located 10.12 inches above the mid-depth of the steel girder web.

## Slide 28: Long-Term (3n) Composite Section
Using the Parallel Axis Theorem, calculate Ix and the resulting section moduli for the composite section to the top and bottom of the steel girder section:
Notes: Next, using the Parallel Axis Theorem, calculate Ix and the resulting section moduli for the long-term (3n) composite section to the top and bottom of the steel girder section. The distances d from the centroidal (neutral) axis of the composite section (located 10.12 inches above the mid-depth of the steel girder web) to the centroidal axis of each component area (i.e., the steel girder section and the transformed concrete deck) are calculated. The product of Ad2 is then added to the moment of inertia, Io, of each component area about its own centroidal axis to obtain Ix for each component area. These moments of inertia are then summed to give the total Ix for the composite section. The section moduli to the top and bottom of the steel girder section are then computed as Ix divided by the respective distances from the centroidal axis to the top and bottom of the steel girder section.

## Slide 29: Short-Term (n) Composite Section
Calculate the location of the centroidal (neutral) axis of the composite section (measured from the mid-depth of the steel girder web):
Notes: For the calculation of the short-term (n) composite section properties, the effective deck width is the same as calculated previously. Calculate the location, dn, of the centroidal (neutral) axis of the composite section measured from the mid-depth of the steel girder web. dn is computed as the summation of the first moments of the steel girder section and the transformed concrete deck about the mid-depth of the steel girder web divided by the total area of the transformed composite section, where d is the distance from the mid-depth of the steel girder web to the centroidal (neutral) axis of each component of the cross-section. Note that the sign of d must be considered in this calculation.
The area and first moment of the steel girder section were computed previously in this lesson. The area of the transformed concrete deck is equal to the structural thickness of the deck (9.0 inches) times the effective width of the deck (114.0 inches) divided by the modular ratio of n or 8. The distance from the mid-depth of the steel girder web to the mid-thickness of the concrete deck, considering the depth of the concrete haunch (3.5 inches) is 42.50 inches. The resulting value of dn is 23.29 inches; that is, the centroidal axis of the composite section is located 23.29 inches above the mid-depth of the steel girder web.

## Slide 30: Short-Term (n) Composite Section
Using the Parallel Axis Theorem, calculate Ix and the resulting section moduli for the composite section to the top and bottom of the steel girder section:
Notes: Next, using the Parallel Axis Theorem, calculate Ix and the resulting section moduli for the short-term (n) composite section to the top and bottom of the steel girder section. The distances d from the centroidal (neutral) axis of the composite section (located 23.29 inches above the mid-depth of the steel girder web) to the centroidal axis of each component area (i.e., the steel girder section and the transformed concrete deck) are calculated. The product of Ad2 is then added to the moment of inertia, Io, of each component area about its own centroidal axis to obtain Ix for each component area. These moments of inertia are then summed to give the total Ix for the composite section. The section moduli to the top and bottom of the steel girder section are then computed as Ix divided by the respective distances from the centroidal axis to the top and bottom of the steel girder section.

## Slide 31: Minimum 1% Longitudinal Reinforcement BDS 6.10.1.7
Size should not exceed No. 6 bars
Spacing should not exceed 12.0 in.
Two layers preferred
2/3 of the area in the top layer
Yield strength ≥ 60 ksi
To control concrete deck cracking in continuous-span beams or girders wherever the longitudinal tensile stress in the deck due to the factored construction loads (Lesson 7) or the Service II load combination (Lessons 3 and 7) exceeds 0.9 times the modulus of rupture of the concrete, fr.
The total cross-sectional area of the longitudinal reinforcement that is provided in these regions is not to be less than 1 percent of the total cross-sectional area of the (structural) concrete deck.
Notes: To control concrete deck cracking in continuous-span beams or girders wherever the longitudinal tensile stress in the deck due to the factored construction loads (Lesson 7) or the Service II load combination (Lessons 3 and 7) exceeds 0.9 times the modulus of rupture of the concrete, fr, AASHTO LRFD Article 6.10.1.7 specifies that the total cross-sectional area of the longitudinal reinforcement that is provided in these regions is not to be less than 1 percent of the total cross-sectional area of the (structural) concrete deck. The effective width of the concrete deck is actually close to the entire deck width in most girder bridges; that is the reason the reinforcement is distributed across the entire concrete section.
The size of the reinforcement should not exceed No. 6 bars. The individual bars should be spaced at intervals not exceeding 12.0 in. The use of small bars at relatively close spacing is intended to ensure closely spaced cracks of small width. It is further stated that the required reinforcement should be placed in two layers uniformly distributed across the deck width, with two-thirds of the reinforcement placed in the top layer. When precast deck panels are used as deck forms, it may not be possible to place the required reinforcement in two layers, in which case this placement requirement may be waived at the discretion of the Engineer. Finally, the specified minimum yield strength of the longitudinal reinforcement must be greater than or equal to 60 ksi.
The determination of the longitudinal placement of this steel will be discussed further in Lesson 7.

## Slide 32: Minimum 1% Longitudinal Reinforcement
Example – taken from NSBA SBDH Design Example 1
Calculate the minimum required negative moment longitudinal reinforcement over the exterior girders of the example cross-section:
Notes: This example will illustrate the computation of the minimum required negative moment longitudinal reinforcement in the concrete deck over the exterior girders in the cross-section shown, which is taken from NSBA SBDH Example 1.
The structural depth of the concrete deck is 9.0 in.; i.e., the ½ in. integral wearing surface is subtracted from the total thickness of the deck. The depth of the concrete haunch is 3.5 in. measured from the top of the girder web to the bottom of the concrete deck. The width of the exterior girder top flanges is assumed to be 18 in.

## Slide 33: Minimum 1% Longitudinal Reinforcement
Notes: Note in the example that the deck overhang tapers shown in the figure on the preceding slide are included in calculating the total cross-sectional area of the deck.
When the section is composite in regions of negative bending, i.e., if shear connectors are present, the longitudinal reinforcement may be included with the steel girder in the computation of the elastic section properties. As specified in AASHTO LRFD Article 6.10.1.1.1c, only the reinforcement within the appropriate effective flange width of the deck is to be considered acting with each girder. The effective deck width for the exterior girder was computed previously to be the tributary width of the deck over the girder, or 114.0 inches. The minimum required negative moment longitudinal reinforcement over the exterior girders is computed to be 10.56 in2.
For the purposes of this example, the longitudinal reinforcement in the two layers is assumed to be combined into a single layer placed at the centroid of the two layers (with each layer also including the assumed transverse deck reinforcement). From separate calculations, the centroid of the two layers is computed to be 4.63 in. from the bottom of the concrete deck. Also, in this example, the area of the longitudinal reinforcement is conservatively taken equal to the minimum required area of longitudinal reinforcement, although a larger area may be provided in the actual deck design and will typically include the temperature and distribution longitudinal reinforcement in the deck (Lesson 14).

## Slide 34: Steel Section + Long. Reinforcement
Example – taken from NSBA SBDH Design Example 1 (interior-pier section – negative moment - exterior girder)
Calculate the elastic section properties for the steel girder section plus the longitudinal reinforcement
Used in the strength limit state calculations – concrete in tension is ignored
Ars= 10.56 in.2
Centroid = 4.63 in. from the bottom of the deck
Notes: To illustrate, the moment of inertia, Ix, and the resulting section moduli will be computed for the composite section shown, which is taken from Design Example 1 of the NSBA Steel Bridge Design Handbook (SBDH). The girder is an exterior girder, and the section is at an interior pier, which is in a negative moment region of a three-span continuous girder. The section properties will be computed for the steel girder section plus the longitudinal reinforcement. These section properties will be used for calculations at the strength limit state. The concrete in tension is ignored in the calculations. The area of the minimum 1 percent longitudinal reinforcement was computed previously to be 10.56 in.2, and the centroid of the longitudinal reinforcement (assumed placed in two layers) was computed previously to be 4.63 in. from the bottom of the structural concrete deck.

## Slide 35: Steel Section + Long. Reinforcement
Calculate the location of the centroidal (neutral) axis of the steel girder section plus the longitudinal reinforcement (measured from the mid-depth of the steel girder web):
Notes: Calculate the location, dsteel + reinf., of the centroidal (neutral) axis of the steel girder section plus the longitudinal reinforcement measured from the mid-depth of the steel girder web. dsteel + reinf. is computed as the summation of the first moments of the component areas of the steel girder section and the longitudinal reinforcement about the mid-depth of the steel girder web divided by the total area of the steel girder section plus the longitudinal reinforcement, where d is the distance from the mid-depth of the steel girder web to the centroidal (neutral) axis of each component of the cross-section. Note that the sign of d must be considered in this calculation.
The distance from the mid-depth of the steel girder web to the centroid of the longitudinal reinforcement, considering the depth of the concrete haunch (3.5 inches) is 42.63 inches. The resulting value of dsteel + reinf. is 2.46 inches; that is, the centroidal axis of the composite section is located 2.46 inches above the mid-depth of the steel girder web.

## Slide 36: Steel Section + Long. Reinforcement
Using the Parallel Axis Theorem, calculate Ix and the resulting section moduli for the steel girder section plus the longitudinal reinforcement to the top and bottom of the steel girder section:
Notes: Next, using the Parallel Axis Theorem, calculate Ix and the resulting section moduli for the steel girder section plus the longitudinal reinforcement to the top and bottom of the steel girder section. The distances d from the centroidal (neutral) axis of the steel girder section plus the longitudinal reinforcement (located 2.46 inches above the mid-depth of the steel girder web) to the centroidal axis of each component area (i.e., the steel girder section and the longitudinal reinforcement) are calculated. Separate calculations similar to those shown previously show the centroidal axis of the steel girder section is located 1.24 inches below the mid-depth of the web. The area of the steel girder section is 114.8 in.2 and the moment of inertia, Io, of the steel girder section about its own centroidal axis is computed to be 111,027 in.4.
The product of Ad2 for each component area of the cross-section is added to the moment of inertia, Io, of each component area about its own centroidal axis to obtain Ix for each component area. These moments of inertia are then summed to give the total Ix for the steel section plus the longitudinal reinforcement. The section moduli to the top and bottom of the steel girder section are then computed as Ix divided by the respective distances from the centroidal axis to the top and bottom of the steel girder section.

## Slide 37: Composite Stiffness for Analysis – BDS 4.5.2.2
For analysis of composite members at all limit states
  The stiffness properties of the full composite section are to be used for permanent and transient loads applied to the composite section
  The concrete deck is to be assumed effective in compression and tension
Notes: In continuous spans, the composite section in negative moment regions will typically have a different stiffness for design calculations at the strength limit state because the concrete deck in tension is assumed cracked and not participating, as discussed previously in this lesson.
However, in computing the stiffness properties to be used in the analysis of composite flexural members at all limit states, AASHTO LRFD Article 6.10.1.5 essentially states that the stiffness properties of the full composite section are to be used for permanent loads and transient loads applied to flexural sections where a concrete deck cast on the top flange of the member has hardened. At sections where the composite stiffness properties are used, the concrete is to be assumed effective in tension and compression for the analysis.
Moments and deflections computed assuming full composite action agree much better with field measurements than those computed assuming no composite action. The assumption of full composite action gives greater girder moments at the interior pier and slightly smaller mid-span moments compared to analyses based on assuming composite action in the so-called positive moment regions only. The increase in negative girder moments occurs over a relatively short length of what is typically a larger cross-section, while the reduction in moment occurs over a much longer positive moment region.

## Slide 38: ELASTIC Stresses in composite sections
Notes: The next topic in this lesson deals with the computation of elastic stresses in composite sections in regions of positive and negative bending. Also covered in this topic are the computation of the elastic depth of the web in compression, Dc, and the yield moment, My.

## Slide 39: Elastic Stress Calculations – Girder Stresses BDS 6.10.1.1.1a
Effective Flange Width
For positive moment:
Dead load DC1: Use the noncomposite steel section
Dead loads DC2 and DW: Use the long-term (3n) composite section
Live load plus impact LL+IM: Use the short-term (n) composite section
Effective Flange Width
/
3
n
Effective Flange Width
Effective Flange Width
/
n
Notes: Assuming unshored construction, for the calculation of the stresses in a composite beam or girder in regions of positive bending moment, the properties of the noncomposite steel section are used for permanent loads applied before the concrete deck has hardened or is made composite (i.e., the DC1 loads as described previously in Lesson 3). The properties of the long-term (3n) composite section are used for permanent loads applied after the concrete deck has hardened or is made composite (i.e., the DC2 and DW loads as also described previously in Lesson 3). The properties of the short-term (n) composite section are used for transient loads applied after the concrete deck is made composite (i.e., the live load plus impact). Refer to AASHTO LRFD Articles 6.10.1.1.1a and 6.10.1.1.1b.
In the calculation of the long-term and short-term composite properties, the appropriate transformed area of the concrete deck is used as described previously in this lesson. The longitudinal reinforcement may be conservatively neglected in positive bending regions of the beam or girder for strength limit state checks.

## Slide 40: Elastic Stress Calculations – Girder Stresses BDS 6.10.1.1.1b
For negative moment:
Dead load DC1: Use the noncomposite steel section
Dead loads DC2 and DW and live load plus impact (LL + IM): Use the steel girder section plus the longitudinal reinforcement (strength limit state)
Notes: For the calculation of the stresses in a composite beam or girder in regions of negative bending moment, the properties of the noncomposite steel section are used for permanent loads applied before the concrete deck has hardened or is made composite (i.e., the DC1 loads). The properties of the steel girder section plus the longitudinal reinforcement are used at the strength limit state for permanent loads and transient loads applied after the concrete deck has hardened or is made composite (i.e., the DC2, DW, and LL + IM loads). Refer to AASHTO LRFD Articles 6.10.1.1.1a and 6.10.1.1.1c
The properties of the steel section plus the longitudinal reinforcement would also be used for loads applied after the concrete deck has hardened or is made composite at the fatigue and service limit states in regions of negative bending, unless the Engineer invokes the provisions of AASHTO LRFD Articles 6.6.1.2.1 and/or 6.10.4.2.1 permitting the concrete to be considered effective in tension for negative flexure at the fatigue and/or service limit states, respectively (to be discussed later in Lesson 7). In that case, the properties of the long-term (3n) composite section would be used for permanent loads DC2 and DW. The properties of the short-term (n) composite section would be used for the LL + IM loads. These properties would be computed exactly as described previously for sections in positive bending.
In regions where the moments due to the transient and permanent loads applied to the composite section are of opposite sign at the strength limit state (i.e., in potential regions of stress reversal), the appropriate composite section to apply to each moment depends on the net unfactored stress in the concrete deck due to these loads (refer to the next slide and AASHTO LRFD Article 6.10.1.1.1b).

## Slide 41: Elastic Stress Calculations – Deck Stresses BDS 6.10.1.1.1d
Deck stresses result only from permanent loads and transient loads applied after the deck has hardened or is made composite; i.e., DC2, DW and LL + IM loads
The calculated stress in the transformed concrete deck must be divided by the modular ratio
The short-term modular ratio, n, is used to compute deck stresses
Notes: Certain calculations to be discussed in subsequent lessons require the calculation of the longitudinal flexural stresses in the concrete deck. For calculating longitudinal flexural stresses in the concrete deck of a composite steel section, the calculated stress in the transformed (structural) concrete deck must be divided by the modular ratio. In a composite girder, longitudinal flexural stresses in the deck are assumed to result only from the permanent loads and transient loads applied after the concrete deck has hardened or is made composite, i.e., the DC2, DW, and LL + IM loads.
AASHTO LRFD Article 6.10.1.1.1d requires that n be used to compute concrete deck stresses for permanent loads, whereas 3n is to be used for calculating the stresses in the steel girder due to permanent loads. The reason for this is to check concrete stresses at the time of construction prior to creep when such stresses are highest, and to check steel stresses after creep has occurred when such stresses are the highest. For the calculation of the longitudinal stresses in the concrete deck due to transient loads, again the properties of the short-term (n) composite section are to be used.
Previous specifications required that the longitudinal flexural stresses in the concrete deck due to permanent loads be calculated using either the n or 3n section, whichever gave the more critical stress in the deck. The n composite section generally governs the deck stress calculation when the deck stresses due to the permanent and transient loads are of the same sign. However, in situations where smaller compressive permanent load stresses can result in larger net tensile stresses in the deck in the vicinity of points of contraflexure (i.e., in potential regions of stress reversal), the use of the 3n composite section when calculating the permanent load stresses will produce a more critical tension stress in the deck. It is felt, however, that such a level of refinement in the calculation of longitudinal deck stresses is not warranted.

## Slide 42: Composite Sections – Elastic Stresses vs. Bending Moments
At elastic stress levels; i.e., when Σfbu ≤ Fy:
Elastic stresses acting on different sections may be summed
👍
Summation of bending moments has no practical meaning due to differing resisting sections
When Σfbu > Fy (or ΣMu > My):
Bending moments acting on different sections may be summed
👎
👍
Notes: The elastic bending stresses in the steel girder of a composite section are dependent on the manner of construction. For unshored construction, the steel girders are erected first and must support their own weight, the weight of the deck forms and wet concrete, or the weight of precast deck panels. Once the concrete deck has hardened or is made composite, bending stresses in the steel girder due to all permanent and transient loads are computed based on the appropriate transformed composite section properties. That is, the long-term (3n) composite section properties are applied to permanent loads and the short-term (n) composite section properties are applied to transient loads.
Regardless of the method of construction, since plane sections are assumed to remain plane, the calculated factored elastic bending stresses, fbu, due to the various loadings acting on the composite section may be summed. However, at elastic stress levels (i.e., when Σfbu ≤ Fy), the principle of superposition of moment has no practical meaning as these moments are each applied to different sections. The girder stiffness is changing as each moment is applied. When Σfbu > Fy (or ΣMu > My), partial yielding of the cross-section occurs and the fact that loads are applied to different cross-sections becomes less significant; therefore, the factored bending moments, Mu, acting on the different sections may be summed under these conditions; the effect of the sequence of application of the different types of loads on the stress states and partial yielding within the cross-section on the resistance is not considered.

## Slide 43: Elastic Stress Calculations
Example – taken from NSBA SBDH Design Example 1 (positive moment section – exterior girder)
Calculate the maximum factored bending stress (fbu) in the bottom flange of the girder for the Strength I load combination.
Modular ratio n = 8
Fyt = 50 ksi
Notes: In this example, the maximum factored bending stress, fbu, in the bottom flange for the Strength I load combination will be computed for the composite section shown, which is taken from Design Example 1 of the NSBA Steel Bridge Design Handbook (SBDH). The girder is an exterior girder, and the section is in a positive moment region in the end span of the three-span continuous girder (at 0.4L). The load modifier  is assumed to be 1.0. Recall that the Strength I load combination and the load modifier, , were discussed previously in Lesson 3. Unshored construction is assumed. The modular ratio n = 8. The section is a homogeneous section with a specified minimum yield strength of the tension (bottom) flange, Fyt, of 50 ksi. The specified minimum yield strength of the compression (top) flange and the web is also 50 ksi.

## Slide 44: Elastic Stress Calculations
Calculate the maximum factored bending stress at 0.4L in the end span. The unfactored bending moments at this point are as follows:
MDC1 = +2,202 kip-ft
MDC2 = +335 kip-ft
MDW = +322 kip-ft
M+LL+IM = +3,510 kip-ft
The section moduli to the bottom flange were computed previously as:
Noncomposite steel section: Sbot of steel = 2,339 in.3
Long-term (3n) comp. section: Sbot of steel = 2,964 in.3
Short-term (n) comp. section: Sbot of steel = 3,211 in.3
Notes: The unfactored bending moments for the three-span continuous girder are shown on this slide at each span tenth point. The moments at the point of maximum positive LL + IM moment in the end span are also shown. The moments were determined using a line-girder analysis as discussed previously in Lesson 4. The moments are shown for one-half of the girder; the moments are symmetrical about the centerline of the bridge (which is located at the right-hand side of the plot). Moments are plotted for the DC1, DC2, and DW loads. Since the live load is a moving load, moment envelopes are plotted for the LL + IM loads; the envelopes represent the maximum (+) and minimum (-) live-load plus impact moment values at each point.
The unfactored positive moments at the four-tenths point (0.4L) in the end span are summarized on the slide. Also summarized are the section moduli to the bottom flange of the girder at this location for the noncomposite steel section, the long-term (3n) composite section, and the short-term (n) composite section. These section moduli were computed earlier in this lesson.

## Slide 45: Elastic Stress Calculations
Therefore, the section remains elastic, and it is appropriate to sum the factored stresses.
Notes: The calculation of the maximum factored bending stress, fbu, in the bottom flange for the Strength I load combination is illustrated for each of the loads: DC1, DC2, DW and +LL+IM. The stress is equal to the moment divided by the appropriate section modulus to the bottom of the girder. Again, the load modifier, , in each case is taken equal to 1.0. For the Strength I load combination, the load factor for DC1 and DC2 is taken equal to 1.25, the load factor for DW is taken equal to 1.50, and the load factor for +LL+IM is taken equal to 1.75. The DC1 moment is applied to the noncomposite steel section, the DC2 and DW moments are applied to the long-term (3n) composite section to account for the effects of creep of the concrete deck in compression since these sustained permanent loads are applied to the composite section, and the +LL+IM moment is applied to the short-term (n) composite section. The ‘(12)’ included in each equation provides for a unit conversion to ‘ksi’. The factored stresses sum to a tensile stress of 40.74 ksi, which is less than the specified minimum yield strength of the tension (bottom) flange of 50 ksi. Therefore, the section remains elastic, and it is appropriate to sum the factored stresses.

## Slide 46: Elastic Stress Calculations
Example – taken from NSBA SBDH Design Example 1 (interior-pier section – negative moment - exterior girder – hybrid section)
A hybrid section is a section with a web that has a specified minimum yield strength less than one or both flanges (Slides 101 to 106).
Calculate the maximum factored bending stress (fbu) in the bottom flange of the girder for the Strength I load combination.
The longitudinal reinforcement will be included and the concrete in tension is ignored at the strength limit state.
Ars = 10.56 in.2 (Slide 33)
Centroid = 4.63 in. from the bottom of the deck (Slide 33)
Fyt= 70 ksi
Fyw = 50 ksi
Fyc = 70 ksi
Ars
Notes: In this example, the maximum factored bending stress, fbu, in the bottom flange for the Strength I load combination will be computed for the composite section shown, which is taken from Design Example 1 of the NSBA Steel Bridge Design Handbook (SBDH). The girder is an exterior girder, and the section is at an interior pier, which is in a negative moment region of a three-span continuous girder (at 1.0L). The load modifier  is assumed to be 1.0. Unshored construction is assumed. The section is a hybrid section with a specified minimum yield strength of the compression (bottom) flange, Fyc, of 70 ksi (a hybrid section is a section with a web that has a specified minimum yield strength less than one or both flanges. Hybrid sections will be discussed further on Slides 101 to 106 of this lesson). The specified minimum yield strength of the tension (top) flange, Fyt, is also 70 ksi and the specified minimum yield strength of the web, Fyw, is 50 ksi. The longitudinal reinforcement will be included in the calculation of the composite section properties and the concrete in tension is ignored at the strength limit state. The area of the minimum 1 percent longitudinal reinforcement was computed previously to be 10.56 in.2 (Slide 33), and the centroid of the longitudinal reinforcement (assumed placed in two layers) was computed previously to be 4.63 in. from the bottom of the structural concrete deck (Slide 33).

## Slide 47: Elastic Stress Calculations
Calculate the maximum factored bending stress at 1.0L (i.e., at the interior pier). The unfactored bending moments at this point are as follows:
MDC1 = -4.840 kip-ft
MDC2 = -690 kip-ft
MDW = -654 kip-ft
M-LL+IM = -4,040 kip-ft
The section moduli to the bottom flange are:
Noncomposite steel section: Sbot of steel = 3,149 in.3
Steel section + long. reinf.: Sbot of steel = 3,327 in.3
Notes: The unfactored negative moments at the interior pier (1.0L) are summarized on the slide. Also summarized are the section moduli to the bottom flange of the girder at this location for the noncomposite steel section and the steel section plus the longitudinal reinforcement. The section modulus for the steel section plus the longitudinal reinforcement was computed earlier in this lesson.

## Slide 48: Elastic Stress Calculations
Therefore, the section remains elastic, and it is appropriate to sum the factored stresses.
Notes: The calculation of the maximum factored bending stress, fbu, in the bottom flange for the Strength I load combination is illustrated for each of the loads: DC1, DC2, DW and +LL+IM. The stress is equal to the moment divided by the appropriate section modulus to the bottom of the girder. Again, the load modifier, , in each case is taken equal to 1.0. For the Strength I load combination, the load factor for DC1 and DC2 is taken equal to 1.25, the load factor for DW is taken equal to 1.50, and the load factor for +LL+IM is taken equal to 1.75. The DC1 moment is applied to the noncomposite steel section, and the DC2, DW, and LL+IM moments are each applied in this case to the composite section consisting of only the steel section plus the longitudinal reinforcement; the concrete in tension is assumed cracked and ineffective at the strength limit state. The ‘(12)’ included in each equation provides for a unit conversion to ‘ksi’. The factored stresses sum to a compressive stress of -55.25 ksi, which is less than the specified minimum yield strength of the compression (bottom) flange of 70 ksi. Therefore, the section remains elastic, and it is appropriate to sum the factored stresses.

## Slide 49: Elastic Stress Calculations
Example – taken from NSBA SBDH Design Example 1 (positive moment section – exterior girder)
Calculate the maximum factored bending stress (fbu) in the concrete deck for the Strength I load combination.
Modular ratio n = 8
In-section = 191,209 in.4
ytop of deck = -23.71 in.
Notes: In this example, the maximum factored bending stress, fbu, in the concrete deck for the Strength I load combination will be computed for the composite section shown, which is taken from Design Example 1 of the NSBA Steel Bridge Design Handbook (SBDH). The girder is an exterior girder, and the section is in a positive moment region in the end span of the three-span continuous girder (at 0.4L). The load modifier  is assumed to be 1.0. The modular ratio n = 8.
Recall that concrete deck stresses are to be computed using the short-term (n) composite section for all loads applied to the composite section. The moment of inertia of the short-term (n) composite section was computed previously to be 191,209 in.4. The centroidal axis of the short-term (n) composite section was also computed previously to be 23.29 inches above the mid-depth of the steel section. Therefore, the distance, y, from the centroidal axis of the short-term (n) composite section to the top of the concrete deck (including the depth of the concrete haunch) is computed as (69/2) – 23.29 + 3.5 + 9.0 = -23.71 inches. The minus sign is added on the distance, y, so that the sign of the calculated stress will be negative (compression). The unfactored bending moments are the same as shown previously for this section on Slide 44 of this lesson.

## Slide 50: Elastic Stress Calculations
Notes: The calculation of the maximum factored bending stress, fbu, in the concrete deck for the Strength I load combination is illustrated for each of the loads: DC2, DW and +LL+IM. Recall that in a composite girder, longitudinal flexural stresses in the deck are assumed to result only from the permanent loads and transient loads applied after the concrete deck has hardened or is made composite, i.e., the DC2, DW, and LL + IM loads. The stress is equal to the moment times the distance, y, from the centroidal axis of the short-term (n) composite section to the top of the concrete deck divided by the moment of inertia of the short-term (n) composite section. Again, the load modifier, , in each case is taken equal to 1.0. For the Strength I load combination, the load factor for DC2 is taken equal to 1.25, the load factor for DW is taken equal to 1.50, and the load factor for +LL+IM is taken equal to 1.75. The ‘(12)’ included in each equation provides for a unit conversion to ‘ksi’. Recall also that for calculating longitudinal flexural stresses in the concrete deck of a composite steel section, the calculated stress in the transformed (structural) concrete deck must be divided by the modular ratio (in this case, n = 8). The factored stresses at the top of the concrete deck sum to a compressive stress of -1.31 ksi.

## Slide 51: Depth of the Web in Compression in the Elastic Range, Dc BDS Appendix D6.3.1
For composite sections in positive bending:
For noncomposite sections:
Use Dc of the steel section
Notes: The depth of the web in compression in the elastic range, Dc, is used primarily in computing the web bend-buckling resistance, Fcrw (discussed further in Lesson 7), and the web load-shedding factor, Rb (discussed later in this lesson). For composite sections in negative flexure and noncomposite sections, Dc is also used to determine whether the section qualifies as a slender or a nonslender web section for determining the nominal flexural resistance, as will be discussed further in Lesson 8.
Dc of the composite section at sections in positive flexure (refer to figure on slide) increases with increasing span length because of the increasing dead-to-live load ratio. With increasing spans, the larger noncomposite dead load stresses acting on the steel section alone effectively cause the neutral axis to be much lower than it would if all loads were applied to the composite section, which obviously increases the depth of the web in compression. Therefore, in general, it is important in certain cases to recognize the effect of the dead load stress on the location of the neutral axis at these sections.
AASHTO LRFD Article D6.3.1 in Appendix D6 states that Dc for composite sections in positive flexure is to be taken as the depth over which the algebraic sum of the stresses acting on the steel, long-term (3n) composite and short-term (n) composite sections due to the dead and live loads, plus impact, is compressive. The equation on this slide, which can simply be derived from an examination of the stress diagram and cross-section given in the figure on this slide (i.e., using similar triangles), is provided in this article to compute Dc in lieu of calculating Dc utilizing the individual stress diagrams.
For noncomposite sections (e.g., during construction), Dc is to be taken as the calculated value of the depth of the web in compression based on the section properties of the steel girder section.

## Slide 52: Depth of the Web in Compression in the Elastic Range, Dc
Example – taken from NSBA SBDH Design Example 1 (positive moment section – exterior girder)
Calculate the depth of the web in compression in the elastic range, Dc, under the Strength I load combination.
Notes: In this example, the depth of the web in compression in the elastic range, Dc, will be computed under the Strength I load combination for the composite section shown, which is taken from Design Example 1 of the NSBA Steel Bridge Design Handbook (SBDH). The girder is an exterior girder, and the section is in a positive moment region in the end span of the three-span continuous girder (at 0.4L). The load modifier  is assumed to be 1.0. Recall that the Strength I load combination and the load modifier, , were discussed previously in Lesson 3. Unshored construction is assumed. The modular ratio n = 8.

## Slide 53: Depth of the Web in Compression in the Elastic Range, Dc
Notes: The factored Strength I stress in the tension (bottom) flange, ft, was computed previously in this lesson for this section to be 40.74 ksi (Slide 45). Separate computations similar to those used to compute ft are used to compute the factored Strength I stress in the compression (top) flange, fc, which is equal to -26.94 ksi. The total depth of the steel girder section, d, is computed to be 71.75 in. The thickness of the compression (top) flange, tfc, is 1.0 in. Substituting into the equation shown on this slide gives a value of Dc equal to 27.56 in.
Note from the previous elastic section property calculations for this section that Dc for the short-term (n) composite section is (69.0 in./2 – 23.29 in.) = 11.21 in. Therefore, the noncomposite dead load stress has a significant effect on the actual value of Dc for this composite section.

## Slide 54: Depth of the Web in Compression in the Elastic Range, Dc
For composite sections in negative bending:
  With concrete deck effective in tension
  Otherwise, use Dc of the steel girder section plus the longitudinal reinforcement
For noncomposite sections:
  Use Dc of the steel section
Notes: The concrete deck is typically not considered to be effective in tension for composite sections in negative flexure, except perhaps at the fatigue and/or service limit states as permitted by the Specifications when certain conditions are satisfied (to be discussed in Lesson 7). The distance between the neutral-axis locations for the steel and composite sections is small when the concrete deck is not considered effective, as the composite section only consists of the steel section plus the longitudinal reinforcement. As a result, the location of the neutral axis for the composite section is essentially unaffected by the dead load stress. In fact, accounting for the effect of the dead load stress actually results in a smaller value of Dc in regions of negative flexure.
Therefore, for the majority of situations involving composite sections in negative flexure, AASHTO LRFD Article D6.3.1 (Appendix D6) conservatively specifies the use of Dc computed for the section consisting of the steel girder plus the longitudinal reinforcement, without considering the algebraic sum of the stresses acting on the noncomposite and composite sections. For noncomposite sections (e.g., during construction), Dc is to be taken as the calculated value of the depth of the web in compression based on the section properties of the steel girder section.
When the concrete deck is assumed to be effective in tension in regions of negative flexure, more than half of the web may be in compression, increasing the susceptibility to web bend buckling. This can control the web thickness used in these regions. In these cases, Dc used in computing the web bend buckling resistance at the service limit state (Lesson 7) must be calculated based on the accumulated factored Service II stresses using the equation shown on this slide. This results in a less critical value of Dc and a larger web bend-buckling resistance.

## Slide 55: Depth of the Web in Compression in the Elastic Range, Dc
Example – taken from NSBA SBDH Design Example 1 (interior-pier section – negative moment - exterior girder – hybrid section
A hybrid section is a section with a web that has a specified minimum yield strength less than one or both flanges (Slides 101 to 106).
Calculate the depth of the web in compression in the elastic range, Dc, under the Service II load combination
Assume the concrete deck may be considered effective in tension at the service limit state (Lesson 7).
Fyt = 70 ksi
Fyw = 50 ksi
Fyc = 70 ksi
Notes: In this example, the depth of the web in compression in the elastic range, Dc, under the Service II load combination will be computed for the composite section shown, which is taken from Design Example 1 of the NSBA Steel Bridge Design Handbook (SBDH). The girder is an exterior girder, and the section is at an interior pier, which is in a negative moment region of a three-span continuous girder (at 1.0L). As discussed previously on Slide 46 of this lesson, the section is a hybrid section (a hybrid section is a section with a web that has a specified minimum yield strength less than one or both flanges. Hybrid sections will be discussed further on Slides 101 to 106 of this lesson). Recall that the Service II load combination and the load modifier, , were discussed previously in Lesson 3. The load modifier  is always taken equal to 1.0 at the service limit state. Unshored construction is assumed. The modular ratio n = 8. For illustration purposes, it will be assumed that the conditions specified for the concrete deck to be considered effective in tension at the service limit state (to be discussed further in Lesson 7) are satisfied.

## Slide 56: Depth of the Web in Compression in the Elastic Range, Dc
Notes: For the Service II load combination, the load factor for DC1, DC2, and DW is taken equal to 1.0, and the load factor for +LL+IM is taken equal to 1.30. The DC1 moment is applied to the noncomposite steel section, and with the concrete deck considered effective in tension, the DC2 and DW moments are applied to the long-term (3n) composite section to account for the effects of concrete creep, and the LL+IM moment is applied to the short-term (n) composite section. The section moduli to the top and bottom flange for each of these sections are calculated separately using the procedures demonstrated previously in this lesson. From separate computations using these section moduli and the unfactored moments at the interior pier shown on a previous slide, the factored Service II stress in the tension (top) flange, ft, is computed to be 26.25 ksi. The factored Service II stress in the compression (bottom) flange, fc, is computed to be -39.07 ksi. The total depth of the steel girder section, d, is computed to be 73.0 in. The thickness of the compression (bottom) flange, tfc, is 2.0 in. Substituting into the equation shown on this slide gives a value of Dc equal to 41.66 in.
Note from separate calculations that Dc for the short-term (n) composite section in this case is equal to 56.35 in. Therefore, this example clearly illustrates the substantial benefit of calculating Dc taking into account the effect of the dead load stress when the concrete is considered effective in tension in regions of negative flexure at the service limit state.

## Slide 57: Yield Moment, My
The moment at which an outer fiber in a section subject to major-axis bending attains the nominal yield stress neglecting the effect of any residual stresses
Noncomposite sections:
  My is taken as the smaller of the moment required to cause nominal first yielding in the compression flange (Myc), or the moment required to cause nominal first yielding in the tension flange (Myt) at the strength limit state.
Notes: In the AASHTO LRFD Specifications, the yield moment, My, is used in the strength limit state resistance calculations for certain types of sections – primarily compact composite sections in regions of positive flexure in straight continuous-span bridges (as discussed further in Lesson 9). My is defined as the moment at which an outer fiber, in a member subjected to flexure about the major-axis, attains the nominal yield stress neglecting the effect of any residual stresses. Calculation of My is to disregard the effects of any flange lateral bending or local web yielding in hybrid sections.
For a noncomposite section, AASHTO LRFD Article D6.2.1 states that My is to be taken as the smaller of the moment required to cause nominal first yielding in the compression flange (Myc), or the moment required to cause nominal first yielding in the tension flange (Myt) at the strength limit state.

## Slide 58: Yield Moment, My BDS Appendix D6.2.2
Composite Sections in Positive Bending:
  My is to be taken as the sum of the moments applied separately to the steel, long-term (3n), and short-term (n) composite sections to cause nominal first yielding in either flange at the strength limit state. My is taken as the lesser of either Myc or Myt.
    Solve for MAD from the following equation:
    Calculate:
58
Notes: As discussed previously in this lesson, in a composite girder, moments are applied to different sections and this fact must be appropriately accounted for in the computation of My. AASHTO LRFD Article D6.2.2 states that My for composite sections in positive flexure can therefore be determined as follows: 1) calculate the factored moment, MD1, caused by the permanent load applied before the concrete deck has hardened or is made composite and apply this moment to the steel section; 2) calculate the factored moment, MD2, caused by the remainder of the permanent load and apply this moment to the long-term (3n) composite section; 3) calculate the additional moment, MAD, that must be applied to the short-term (n) composite section to cause nominal yielding in either steel flange; and 4) calculate My as the sum of the total factored permanent load moment and MAD. This procedure can be represented in equation form as shown on this slide. SNC, SLT, and SST are the section moduli for the steel section, long-term (3n) composite section, and short-term (n) composite section, respectively, for the flange under consideration. The procedure is repeated for each flange and My is taken as the lesser of either Myc or Myt. Myc is the sum of the moments causing nominal first yielding in the compression (top) flange, and Myt is the sum of the moments causing nominal first yielding in the tension (bottom) flange. For composite sections in positive bending, Myt typically controls. In positive bending regions, the longitudinal reinforcement may be neglected in the calculation of SLT and SST.

## Slide 59: Yield Moment, My
Example – taken from NSBA SBDH Design Example 1 (positive moment section – exterior girder)
Calculate the yield moment, My, at the strength limit state.
Modular ratio n = 8
Fyt = 50 ksi
Notes: In this example, the yield moment, My, at the strength limit (for the Strength I load combination) will be computed for the composite section shown, which is taken from Design Example 1 of the NSBA Steel Bridge Design Handbook (SBDH). The girder is an exterior girder, and the section is in a positive moment region in the end span of the three-span continuous girder (at 0.4L). The load modifier  is assumed to be 1.0. Recall that the Strength I load combination and the load modifier, , were discussed previously in Lesson 3. Unshored construction is assumed. The modular ratio n = 8. The section is a homogeneous section with a specified minimum yield strength of the tension (bottom) flange, Fyt, of 50 ksi. The specified minimum yield strength of the compression (top) flange and the web is also 50 ksi.

## Slide 60: Yield Moment, My
For composite sections in positive flexure, Myt, or the yield moment calculated for the tension (bottom) flange, typically controls.
Solve for MAD from the following equation:
Calculate:
Notes: For composite sections in positive flexure, Myt, or the yield moment calculated for the tension (bottom) flange, typically controls. From earlier calculations in this lesson, the section moduli to the bottom flange for this section were calculated as follows: SNC = 2,339 in.3; SLT = 2,964 in.3; SST = 3,211 in.3. The unfactored dead load moments at this section are: MD1 = 2,202 kip-ft; MDC2 = 335 kip-ft; MDW = 322 kip-ft.
For the Strength I load combination (with the load modifier  taken equal to 1.0), and using the equation shown on the slide, solve for the additional moment, MAD, applied to the short-term (n) composite section to reach the specified minimum yield strength of 50 ksi in the tension (bottom) flange. From this calculation, MAD is equal to 8,624 kip-ft. Adding MAD to the factored dead load moments gives a theoretical yield moment, My, of 12,278 kip-ft.

## Slide 61: Yield Moment, My BDS Appendix D6.2.3
Composite Sections in Negative Bending:
  My is calculated using the same procedure as for composite sections in positive bending, only in this case, both SLT and SST are to be taken for the section consisting of the steel girder plus the longitudinal reinforcement within the effective flange width of the concrete deck. My is taken as the lesser of either Myc or Myt.
  Myt is to be taken with respect to either the tension flange or the longitudinal reinforcement, whichever is the smallest value. For the calculation of Myt with respect to the longitudinal reinforcement, MD1 is to be taken equal to zero and Fyf is to be taken equal to the specified minimum yield strength of the longitudinal reinforcement.
Notes: For composite sections in negative bending, AASHTO LRFD Article D6.2.3 states that a procedure similar to the procedure for composite sections in positive bending is to be used to compute My, only in this case, both SLT and SST are to be taken for the section consisting of the steel girder plus the longitudinal reinforcement within the effective flange width of the concrete deck. My is to be taken as the lesser or Myc or Myt.
Myt is to be taken with respect to either the tension flange or the longitudinal reinforcement, whichever is the smallest value. For the calculation of Myt with respect to the longitudinal reinforcement, MD1 is to be taken equal to zero and Fyf is to be taken equal to the specified minimum yield strength of the longitudinal reinforcement.

## Slide 62: PLASTIC Section properties BDS Appendix D6.1
Notes: The next topic in this lesson covers the computation of plastic section properties, which are employed in the design of specific classifications of sections in flexural members. The computation of the plastic moment, Mp, for noncomposite and composite sections is covered, along with the computation of the depth in the web in compression at the plastic moment, Dcp.

## Slide 63: Plastic Moment, Mp
Mp is the resisting moment of a fully yielded cross-section about the major axis. It is the moment of the plastic forces acting on the cross-section about the plastic neutral axis (PNA).
Mp is a theoretical measure of the maximum potential resistance of noncomposite or composite sections satisfying certain limits.
An idealized elastic-plastic response is assumed (i.e., strain hardening is ignored).
Notes: The plastic moment, Mp, is defined in the AASHTO LRFD Specifications as the resisting moment of a fully yielded cross-section about the major axis. Mp is calculated as the moment of the plastic forces acting on the cross-section about the plastic neutral axis (PNA). The position of the plastic neutral axis is calculated based on the equilibrium condition that there is no net axial force acting on the cross-section. Plastic forces in steel portions of the cross-section are calculated using the nominal yield strengths of the flanges, web and longitudinal reinforcing steel, as appropriate. Plastic forces in concrete portions of the cross-section (in compression only) are based on a rectangular stress block, with the magnitude of the compressive stress taken equal to 0.85fc. Concrete in tension is neglected.
Mp is used as a theoretical measure of the maximum potential resistance of noncomposite or composite sections satisfying specific steel grade, flange and web slenderness, compression-flange bracing and ductility requirements, as applicable. Such sections in straight bridges that are composite in regions of positive flexure are termed compact sections (Lesson 9). Noncomposite sections or composite sections in regions of negative flexure in straight bridges satisfying these requirements are termed compact web sections, which are less commonly used (Lesson 8).
For sections that can achieve Mp, it is assumed for design that the section is completely elastic up to Mp and then rotates inelastically at Mp with no increase in the moment resistance, as shown by the ‘Idealized Curve’ in the plot on this slide. This idealized moment-rotation behavior is termed elastic-perfectly plastic behavior. In the girder cross-sections shown on this slide, the black in Stages II and Stage III indicates nominal yielding. For design (i.e., assuming elastic-perfectly plastic behavior), only Stages I and III are assumed to apply for sections that can achieve Mp. Under moment gradient conditions, compact sections and compact web sections may be able to exceed Mp due to strain hardening (see the ‘Actual Curve’ on the plot on this slide), in which case the stresses in the flanges and upper and lower portions of the web shown in Stage II would continue to increase beyond the nominal yield strength, Fy (Stage III would not apply in this case). However, the effects of strain hardening are conservatively ignored in design.

## Slide 64: Plastic Section Modulus, Z
Fy
Fy
C
T
y2
y1
b
h
PNA
A2 = area above the neutral axis (PNA)
A1 = area below the neutral axis (PNA)
Plastic Section Modulus
For the rectangle:
Notes: Assume the fully yielded rectangular cross-section shown on this slide with a width, b, and a height, h. The compressive force, C, on the cross-section is equal to the nominal yield strength, Fy, times the cross-sectional area, A2, above the neutral axis (termed the plastic neutral axis in this case or the PNA). The tensile force, T, on the cross-section is equal to Fy times the cross-sectional area, A1, below the PNA. For equilibrium, T – C must equal zero. Since the total area of the cross-section, A = A1 + A2, it is apparent then that A1 = A2 = A/2.
The moment, Mp, about the PNA is equal to Ty1 + Cy2. Substituting and performing the algebra, Mp is equal to FyZ, where Z is termed the ‘plastic section modulus’ given by the equation shown on the slide. Z may be interpreted geometrically as the first moment taken about the neutral axis of the area of the cross-section above the neutral axis plus the first moment of the area below the neutral axis.
As shown on the slide, for the rectangular cross-section, Z is equal to bh2/4. The shape factor, or ratio of Z to the elastic section modulus, S, is equal to 1.5. Thus, the plastic moment, Mp, for a rectangular cross-section is 50 percent greater than the yield moment, My.

## Slide 65: Noncomposite Rolled W Shapes
For W36 x 330:
Notes: For noncomposite rolled wide-flange (W) shapes, values of the plastic section modulus, Z, are tabulated in the AISC Manual of Steel Construction. The values include the contribution of the rolled-beam fillets. In this case for a W36 x 330 shape, using the tabulated value of Zx of 1,410 in.3 about the major-axis of the cross-section and assuming the yield strength, Fy, is equal to 50 ksi, the plastic moment, Mp, is computed to be 5,875 kip-ft.
The ratio of Mp/My (or of Z/S) is a property of the cross-sectional shape known as the shape factor, where My is the yield moment discussed previously in this lesson. For doubly symmetric non-composite rolled W-shapes bent about their major axis, the shape factor is approximately in the range of 1.1 to 1.2. For singly symmetric composite sections in regions of positive bending, the shape factor is much larger. Values on the order of 1.4 to 1.6 are quite common.

## Slide 66: Noncomposite Welded I-Girders
Often singly symmetric in bridge applications
Location of the PNA is different than the elastic neutral axis and must be determined for the calculation of Z
Example – taken from NSBA SBDH Design Example 1 (positive moment section – exterior girder)
  Section is singly symmetric
  Calculate the plastic section modulus, Z, and the plastic moment, Mp, for the noncomposite steel girder section.
Fy = 50 ksi
Notes: As discussed previously, noncomposite welded I-girders are often singly symmetric in bridge applications. Therefore, unlike doubly symmetric sections, the location of the plastic neutral axis (PNA) is different than the location of the elastic neutral axis. As a result, the location of the PNA must be assumed in the calculation of the plastic section modulus, Z.
To illustrate, the plastic section modulus, Z, and the plastic moment, Mp, will be computed for the composite section shown, which is taken from Design Example 1 of the NSBA Steel Bridge Design Handbook (SBDH). The girder is an exterior girder, and the section is in a positive moment region in the end span of the three-span continuous girder (at 0.4L). The section is a homogeneous section with a specified minimum yield strength, Fy, of 50 ksi.

## Slide 67: Noncomposite Welded I-Girders
Component | Force, kips | Z (= yA), in.3
Top Flange | C = (16)(1.0)(50) = -800 | (50.5)(16)(1.0) = 808
Web (above PNA) | C = (50)(0.5)(50) = -1,250 | (25.0)(50)(0.5) = 625
Web (below PNA) | T = (19)(0.5)(50) = 475 | (9.5)(19)(0.5) = 90.3
Bottom Flange | T = (18)(1.75)(50) = 1,575 | (19.875)(18)(1.75) = 626.1
 | ΣC = ΣT ok | Σ = 2,149.4
From earlier calculations, the elastic neutral axis is located 6.76 in. below the mid-depth of the steel-girder web (Slides 15 and 16).
However, the plastic neutral axis (PNA) is 15.50 in. below the mid-depth of the steel-girder web. This is found by balancing the tensile and compressive forces above and below the PNA. This is done either by trial and error or by using the equations in BDS Appendix D6.1.
Determine the plastic moment capacity:
Notes: From earlier calculations in this lesson, the elastic neutral axis for the noncomposite steel girder section was determined to be 6.76 in. below the mid-depth of the steel-girder web (refer to Slides 15 and 16 of this lesson). After several trials, assume the plastic neutral axis (PNA) is 15.50 in. below the mid-depth of the steel-girder web and check equilibrium of the forces on the cross-section assuming the section is fully yielded (refer to the figure of the steel cross-section on the preceding slide). As shown in the center column of the table on this slide, the sum of the compressive forces in the top flange and in the web above the assumed PNA is -2,050 kips. The sum of the tensile forces in the bottom flange and in the web below the assumed PNA is +2,050 kips. Therefore, the PNA is located 15.50 in. below the mid-depth of the steel-girder web.
In the right-hand column of the table, the plastic modulus, Z, is then computed for each component of the cross-section and is taken as the first moment of each component area about the PNA. Summing the values for the individual component areas gives Z equal to 2,149.4 in.3 The plastic moment, Mp, is then computed as the yield strength, Fy, times Z or 8,956 kip-ft.
For hybrid sections, the product of Fy times Z would need to be computed for each individual component area, with the sum of the values for the individual component areas then equal to Mp.

## Slide 68: Composite Sections – Positive Bending BDS Appendix D6.1
Forces in concrete portions of the cross-section are based on Whitney’s stress block, with the magnitude of the compressive stress taken equal to 0.85fc.
Concrete in tension is ignored.
The PNA is commonly in the concrete deck or in the top flange.
Example
  NSBA SBDH Design Example 1 (positive moment section – exterior girder)
  Calculate Z for the steel girder section and Mp for the composite section.
Fy = 50 ksi
f’c = 4.0 ksi
beff = 114.0 in.
Notes: For composite sections in positive bending, an additional compressive force in the concrete deck must be considered in the computation of Mp. Plastic forces in compression in concrete portions of the cross-section are based on the Whitney rectangular stress block model used in reinforced concrete design, except that the rectangular stress block is always taken as the full depth in compression above the plastic neutral axis (PNA) rather than a fraction of this depth. This simplification generally results in a negligible or only a slight increase of the calculated plastic moment. Concrete in tension is ignored. The effective width of the concrete deck is assumed stressed in compression at 0.85f’c. Typically, the area of the concrete deck haunch is not considered in the computation of Mp; the haunch depth may be considered, however, if permitted by the Owner. The longitudinal deck reinforcement, which is assumed to be stressed to its yield strength, may or may not be considered. The PNA for these sections is typically in the concrete deck or in the top flange.
For composite sections, the stress distribution in the cross-section at Mp is assumed independent of the manner in which the stresses are induced into the beam. Thus, Mp is computed in the same manner for both unshored and shored construction even though the elastic stress distribution differs for each method of construction. Also, creep and shrinkage are assumed to have no effect on the internal stress distribution at Mp. Thus, when checking the flexural resistance of a composite section against Mp, the moments acting on the noncomposite, long-term (3n) composite, and short-term (n) composite sections may be directly summed for comparison to Mp. The effect of the sequence of application of the different types of loads on the stress states and partial yielding within the cross-section on the resistance is not considered. Since these cross-section types are able to sustain inelastic curvatures sufficient to develop their nominal full plastic moment, the effect of the different loadings is negligible with respect to the section maximum strength.
To illustrate, the plastic section modulus, Z, for the steel girder section and the plastic moment, Mp, will be computed for the composite section shown, which is taken from Design Example 1 of the NSBA Steel Bridge Design Handbook (SBDH). The girder is an exterior girder, and the section is in a positive moment region in the end span of the three-span continuous girder (at 0.4L). The structural thickness of the concrete deck is 9.0 inches, and the depth of the concrete haunch measured from the top of the web to the bottom of the deck is 3.5 inches and will be considered in the computations. The contribution of the longitudinal reinforcement in the deck is ignored. The section is a homogeneous section with a specified minimum yield strength, Fy, of 50 ksi. The 28-day compressive strength, f’c, of the concrete deck is 4.0 ksi. The effective width of the concrete deck, beff, was computed previously in this lesson to be 114.0 in.

## Slide 69: Composite Sections – Positive Bending
Component | Force - kips | Z (= yA) – in.3
Concrete Deck | C = 0.85(4.0)(114.0)(9.0) = -3,488 | N/A
Top Flange (above PNA) | C = (16)(0.383)(50) = -306 | (0.192)(16)(0.383) = 1.18
Top Flange (below PNA) | T = (16)(0.617)(50) = 494 | (0.309)(16)(0.617) = 3.05
Web | T = (69)(0.5)(50) = 1,725 | (35.12)(69)(0.5) = 1,212
Bottom Flange | T = (18)(1.75)(50) = 1,575 | (70.50)(18)(1.75) = 2,220
 | ΣC = ΣT ok | Σ = 3,436
The plastic neutral axis (PNA) is 0.383 in. below the top of the top flange (see next slide)
Check equilibrium of forces assuming the steel girder section is fully yielded, and the concrete deck is at its specified strength of 0.85f’c
Notes: From earlier calculations in this lesson (Slides 29 and 30), the elastic neutral axis for the short-term (n) composite section was determined to be 23.29 in. above the mid-depth of the steel section. After several trials, assume the plastic neutral axis (PNA) is 0.383 in. below the top of the top flange of the steel girder section and check equilibrium of the forces on the cross-section assuming the steel girder section is fully yielded, and the concrete deck is at its ultimate compressive strength of 0.85f’c (refer to the figure of the composite section shown on the preceding slide). As shown in the center column of the table on this slide, the sum of the compressive forces in the concrete deck and in the top flange above the assumed PNA is –3,794 kips. The sum of the tensile forces in the bottom flange, in the web, and in the top flange below the assumed PNA is +3,794 kips. Therefore, the PNA is located 0.383 in. below the top of the top flange.
In the right-hand column of the table, the plastic modulus, Z, is then computed for each component of the steel girder cross-section and is taken as the first moment of each component area about the PNA. Summing the values for the individual component areas gives Z equal to 3,436 in.3 The plastic moment, Mp, is then computed as the yield strength of the steel, Fy, times Z, plus the moment arm to the centroid of the concrete deck (considering the depth of the concrete haunch) times the compressive force in the deck, or 16,462 kip-ft.

## Slide 70: Composite Sections – Positive Bending
Notes: In lieu of a trial-and-error procedure to locate the plastic neutral axis (PNA) and calculate the plastic moment, Mp, for composite sections in positive bending, as illustrated on the preceding slide, AASHTO LRFD Table D6.1-1 in Appendix D6 provides a table (a portion of which is shown on this slide) to conveniently calculate the location of the PNA and Mp.
The element forces in the table are shown on the right-hand side of this slide. Forces in the top and bottom layers of reinforcement in the concrete deck may be included if desired. In the equations in the table, d is the distance from the element plastic force to the plastic neutral axis. The element forces are assumed to act at the mid-thickness of the flanges and concrete deck, at the mid-depth of the web and at the center of the longitudinal reinforcement. All element forces, dimensions, and distances are to be taken as positive. The conditions shown in the third column of the table should be checked in the order listed in the table to determine where the PNA is located. The forces in the longitudinal reinforcement may be conservatively neglected by setting the terms, Prb and Prt, equal to zero in the equations given in the table. The plastic moment of a noncomposite section may be calculated by eliminating the terms pertaining to the concrete deck and longitudinal reinforcement from the equations in the table for composite sections.
The figure at the bottom right of this slide shows the location of the PNA as determined from the table for the two most common cases, i.e., the PNA in the top flange and the PNA in the concrete deck.

## Slide 71: Composite Sections - Positive Bending
Using Table D6.1-1, compute Mp for the preceding example problem. Ignore the longitudinal deck reinforcement. Assuming the PNA is not located in the web, check the Condition for Case II in the table first:
Notes: To illustrate, the plastic moment, Mp, will be computed for the preceding example problem using AASHTO LRFD Table D6.1-1. The longitudinal deck reinforcement will be ignored. Assuming for this case that the plastic neutral axis (PNA) is not located in the web, check the Condition for Case II in the third column of the table first. Since the force in the concrete deck, Ps = 3,488 kips, is less than the total force in the steel girder section; i.e., Pt + Pw + Pc = 4,100 kips, the Condition for Case II is satisfied and the PNA is located in the top flange. Substituting into the equation for the PNA for this Condition shows that the PNA is located 0.383 in. from the top of the top flange.

## Slide 72: Composite Sections - Positive Bending
Calculate the distances from the PNA to the centroid of each element:
72
Notes: The equation for Mp shown at the top of this slide is taken from the table for Case II. The distances from the PNA to the centroid of the deck (ds), the centroid of the web (dw), and the centroid of the bottom (tension) flange (dt) are then computed. The appropriate substitutions are then made into the equation for Mp resulting in a value of 16,464 kip-ft, which is approximately the same as the value computed previously on Slide 69 of this lesson using the trial-and-error approach.

## Slide 73: Composite Sections – Negative Bending BDS Appendix D6.1
Notes: AASHTO LRFD Table D6.1-2 in Appendix D6 is a similar table to compute the plastic moment, Mp, and the location of the plastic neutral axis (PNA) for composite sections in negative bending. In this case, however, the tensile strength of the concrete is ignored, and the contribution of the longitudinal reinforcement should be included. The table contains the equations for the two cases most likely to occur in practice; the PNA in the web (most common) or the PNA in the top flange of the steel girder section. Again, the conditions should be checked in the order listed in the table. The plastic moment of a noncomposite section may be calculated by eliminating the terms pertaining to the longitudinal reinforcement from the equations in the table for composite sections.
The figure at the bottom right of this slide shows the location of the PNA as determined from the table for the two most common cases, i.e., the PNA in the web and the PNA in the top flange.

## Slide 74: Depth of the Web in Compression at the Plastic Moment, Dcp
For composite sections in positive bending (w/ PNA in the web):
For composite sections in negative bending (w/ PNA in the web):
Notes: In the AASHTO LRFD Specifications, the depth of the web in compression at the plastic moment, Dcp, is used primarily in one of the criteria to determine if a composite section in positive flexure qualifies as a compact section at the strength limit state, and to determine if a composite section in negative flexure or a noncomposite section qualifies as either a compact web or a noncompact web section at the strength limit state (to be discussed further in Lessons 9 and 8, respectively).
At sections in positive bending, the depth of the web in compression typically reduces (i.e., from Dc) as plastic strains associated with moments larger than My are incurred. In fact, the neutral axis at the plastic moment, Mp, will often be located either in the concrete deck or in the top flange of the steel girder as discussed previously. In such cases, the entire web of the girder is in tension and Dcp is to be taken as zero. When Dcp is equal to zero, all web-slenderness requirements in the Specifications based on Dcp are assumed automatically satisfied. For deeper girders (e.g., with longitudinal web stiffeners), it is possible, although somewhat rare, that the conditions in AASHTO LRFD Table D6.1-1 may indicate that the plastic neutral axis is located in the web. In this case, Dcp may be calculated from the equation shown at the top of this slide.
At sections in negative bending, the depth of the web in compression typically increases (i.e., from Dc) as plastic strains associated with moments larger than My are incurred. In calculating Dcp in regions of negative bending, the concrete deck is assumed not to be effective in tension. Therefore, in most all cases, the plastic neutral axis will be located in the web. For rare cases in which the plastic neutral axis is located in the top flange and the entire web is in compression, Dcp is to be taken equal to the web depth D. For composite sections in negative flexure where the conditions in AASHTO LRFD Table D6.1-2 indicate that the plastic neutral axis is located in the web, Dcp may be computed from the equation shown at the bottom of this slide. For noncomposite sections, all terms related to the longitudinal reinforcement in the equation should be set equal to zero.

## Slide 75: Depth of the Web in Compression at the Plastic Moment, Dcp
Example – taken from NSBA SBDH Design Example 1 (interior-pier section – negative moment - exterior girder - hybrid section
A hybrid section is a section with a web that has a specified minimum yield strength less than one or both flanges (Slides 101 to 106).
Calculate the depth of the web in compression at the plastic moment, Dcp.
The longitudinal reinforcement will be included and the concrete in tension is ignored at the strength limit state.
Ars = 10.56 in.2; Fyrs = 60 ksi
Fyt = 70 ksi
Fyw = 50 ksi
Fyc = 70 ksi
Notes: To illustrate, the depth of the web in compression at the plastic moment, Dcp, will be computed for the composite section shown, which is taken from Design Example 1 of the NSBA Steel Bridge Design Handbook (SBDH). The girder is an exterior girder, and the section is at an interior pier, which is in a negative moment region of a three-span continuous girder (at 1.0L). The section is a hybrid section with a specified minimum yield strength of the compression (bottom) flange, Fyc, of 70 ksi (a hybrid section is a section with a web that has a specified minimum yield strength less than one or both flanges. Hybrid sections will be discussed further on Slides 101 to 106 of this lesson). The specified minimum yield strength of the tension (top) flange, Fyt, is also 70 ksi and the specified minimum yield strength of the web, Fyw, is 50 ksi. The longitudinal reinforcement will be included in the calculation and the concrete in tension is ignored at the strength limit state. The area of the minimum 1 percent longitudinal reinforcement was computed previously in this lesson to be Ars = 10.56 in.2 and the yield strength of the longitudinal reinforcement, Fyrs, is equal to 60 ksi.

## Slide 76: Depth of the Web in Compression at the Plastic Moment, Dcp
Check equilibrium by calculating and comparing the total plastic forces acting on the tension and compression sides of the plastic neutral axis:
Tension Side:
Compression Side:
Notes: To begin the calculation, the cross-sectional areas of the tension (top) flange, At, the web, Aw, and the bottom (compression) flange, Ac, are computed. Substituting these areas and the corresponding yield strengths, along with the area of the longitudinal reinforcement, Ars, yield strength of the longitudinal reinforcement, Fyrs, and the web depth, D, into the equation gives Dcp equal to 40.79 in.
A check is then made to ensure equilibrium of the plastic forces on the tension and compression sides of the plastic neutral axis based on the computed value of Dcp.
Note that for the section consisting of the steel girder plus the longitudinal reinforcement, the elastic depth of the web in compression Dc was computed previously in this lesson (Slide 36) to be 38.96 in. – 2.0 in. = 36.96 in., which is smaller than Dcp as expected.

## Slide 77: FLANGE LATERAL bending
Notes: The next topic in this lesson covers the fundamentals of torsion along with the computation of flange lateral bending moments and stresses in I-sections due to warping torsion. Potential sources of torsion in I-girder bridges are covered representing specific cases in which reasonable estimates of the flange lateral bending moments and stresses due to torsion are required for design.

## Slide 78: Torsion
Notes: To adequately discuss the topic of flange lateral bending, it is first instructive to cover the fundamentals of torsion theory. Application of a load in a plane other than one through the so-called “shear center” of the cross-section will cause torsion in the cross-section. The member will twist to the extent that torsional restraints prevent such twisting. The torsional stresses consist of shear and flexural stresses. These stresses must be combined with the stresses due to flexure.
The shear center is defined as the unique point for a cross-section through which any load will create no torsion. The shear center is the point about which a section rotates when subjected to torque. Flexural bending does not create torsion when the applied loads pass through the shear center. This can be tacitly assumed in the analysis with little error in many cases. However, there are many cases where loads do not pass through the shear center, in which case they may create significant torsional stresses.
The shear center does not necessarily coincide with the centroid of the cross-section. For doubly-symmetric sections, such as the I-sections shown in the left and center sketches on this slide, the shear center coincides with the centroid. For singly-symmetric and unsymmetrical sections, such as channels, tees and single angles, the shear center does not coincide with the centroid. For the channel shown in the right sketch on this slide, the shear center is actually located outside of the section. All the sections shown on this figure are categorized as open sections. This simply means that the elements of the section do not form a closed or box-type shape. Open sections warp out-of-plane when subjected to torsion.

## Slide 79: St. Venant Torsion
G = shear modulus (ksi)
J = torsion constant or polar
moment of inertia;
for a solid round =
L = member length (in.)
T = applied torque (kip-in.)
Notes: The simplest form of torsion is referred to as pure torsion or St. Venant torsion. Pure torsion can best be visualized by a solid prismatic round member free to twist at one end and restrained against twisting at the other end as shown on this slide. If a torque, or torsional moment, is applied to the free end, the torque will travel unreduced to the opposite (torsionally restrained) end where it will be resisted by a torque equal but opposite to the applied torque. The only stresses generated are torsional shear stresses, ., which are proportional to the distance from the centroid; there is no warping of the cross-section. The torsion resistance resulting from this distribution of shear stresses is known as pure torsion or St. Venant torsion. St. Venant torsion is also referred to as uniform torsion because the torsion is non-diminishing along the length.
The magnitude of the resulting total angle of twist, , is computed from the equation shown on this slide, where T is the applied torque, L is the member length, G is the shear modulus (equal to E/2(1+γ), where γ is Poisson’s ratio equal to 0.3 for steel), and J is the St. Venant torsion constant (also referred to as the polar moment of inertia for a solid round equal to πr4/2). The maximum St. Venant torsional shear stress is equal to the applied torque times the radius divided by J. The resisting torque, Ts, is equal to G times J times the rate of twist per unit length, d/dz.

## Slide 80: St. Venant Torsion
:
J = St. Venant torsional constant ≈
Which can be simplified to:
Notes: The rate of twist per unit length, d/dz, may be assumed constant for an open cross-section, such as the I-girder section shown on this slide, when the cross-section is assumed not to distort, and the torsion is pure and not interrupted by other loads or torsional restraints. The assumption of no distortion allows a torsional constant to be computed. The section may be thought of as three interconnected rectangular elements (i.e., two flanges and a web) with respect to twist. This assumption is not true for many steel bridge girders where the web is deep and will distort. When the assumption of no distortion is appropriate, the St. Venant torsion shear distribution in an I-section will be almost identical to that which exists in three separate narrow rectangles.
For a narrow rectangle subject to pure torsion, the relationship between the resisting torque, Ts, and the twist per unit length can be expressed as the shear modulus, G, times the St. Venant torsion constant, J, times the rate of twist per unit length, d/dz. In this case, J can be taken in the simplified form of the more general equation as the sum of bt3/3, where b and t are the width and thickness of each individual rectangle (i.e., the flanges and web). A more accurate approximation of J for an I-section, neglecting the effect of web-to-flange fillets, is given by the equation on the top right of this slide. For flanges with bf/2tf greater than 7.5, the term in parentheses for that flange in this equation may be taken equal to one. More accurate values of J for rolled I-shapes, including the effect of the web-to-flange fillets, are tabulated in the AISC Steel Construction Manual. St. Venant torsional shear stresses in the flanges (f) and web (w) can be approximated from the equations shown on the bottom left of this slide. Peaks of the shear stress occur on the outer fibers at the center of the flange and on the outer fibers at the mid-height of the web.

## Slide 81: St. Venant Torsion
Notes: In open sections, torsional shear flows around the individual elements. In closed sections, torsional shear flows around the whole section. For a single cell box section, the uniform St. Venant torsional shear flow, f = t in units of force/length, develops around the circumference of the box as shown in the figure on this slide. As shown by the derivation on this slide, for any thin-walled single-cell closed shape, the torsional shear stress at any point is equal to the torque divided by the product of the wall thickness at that point and twice the enclosed area, A. The preceding is true even when the wall thickness varies as long as the change is not abrupt enough to cause a concentration of stress; the shear flow follows the peripheral line and is constant. The St. Venant torsional constant, J, for a rectangular box section with adequate torsional stiffness is determined from Bredt’s formula and is given by the equation shown on the right-hand side of this slide, where b is the width of the plate element under consideration. This equation may be used to compute J for tub-girder sections if the distortion of the section is adequately controlled. Cross-section distortion of boxes is usually constrained by internal cross-bracing members.
In the U.S., most box girders used in bridge superstructures are tub girders having open tops. The open top is braced with a top lateral bracing system that forms a pseudo-box section. The top lateral bracing is designed to resist the shear flow combined with the flexural bending moment in the box. Formulas are available to calculate the thickness of an equivalent plate for different possible configurations of top lateral bracing for use in determining J. The St. Venant torsional stiffness of a box section is between 100 and 1,000 times the torsional stiffness of a comparable I-section. When used on horizontally curved alignments, a single box has the ability to resist torsion alone, unlike open sections that depend on adjacent open sections for stability. However, this inherent torsional stiffness limits the twist the box will permit during fit-up, which is particularly evident with boxes resting on skewed supports.

## Slide 82: Warping Torsion
Cw = warping torsional constant = Iyh2/4 (in.6)
h = distance between the centerlines of the flanges (in.)
Iy = moment of inertia of the I-section about a vertical axis in the plane of the web (in.4)
Notes: If a non-circular cross-section, such as an I-section, is subjected to a torsional moment, the cross-section will again twist, as shown in the figure on the left, but in this case, it will also deform non-uniformly in the longitudinal direction so that plane sections do not remain plane after twisting occurs. This cross-sectional deformation is referred to as warping, as shown in the center figure on this slide. If warping is restrained, as shown for the I-section on the right, which is restrained from warping as well as twisting at its base, the forces, F, are developed and exerted by the support due to restraint of warping. The forces, F, acting in the directions shown represent flange lateral bending moments. These forces cause flange shear stresses, which result in transverse shear forces, H, in each flange. These transverse shears bend each flange much like a rectangular beam about its own major axis. Bending in the web is neglected due to its lack of rigidity in the weak direction. In this case, the transverse shear times the distance, h, between flange centers results in a couple having the same direction as the resisting torque. Thus, the restraint at the end provides the warping torsion resistance. This additional component of the torsion resistance resulting from restraint of warping is known as warping torsion. Warping torsion is also commonly referred to as “non-uniform torsion” due to the fact that the shear stress patterns under St. Venant torsion are disturbed because of warping restraint. Thus, non-uniform torsion results from a variation of torque along the span and/or also where there are discontinuities in the torque introduced along the span caused by warping restraint (e.g., at cross-frames).
Whenever warping restraint is present in an I-section, only part of the applied torque need be resisted in St. Venant torsion. The remainder is carried by so-called warping torsion that is developed due to the transverse shears that result from the flexural resistance of the flanges. The equation for the warping component of the total torque for an I-section, Tw, is given by the equation shown on this slide, where Cw is the warping torsional constant. The warping torsion constant for box sections is usually assumed equal to zero. This means that shear and normal stresses due to warping torsion are typically quite small and are usually neglected for box sections.
See Lesson 4 for additional discussion of warping torsion.

## Slide 83: Torsion Resistance for Design
For closed cross-sections, such as box girders, and for certain smaller singly-symmetric and unsymmetrical open cross-sections, such as rolled channels, tees or angles, St. Venant torsion generally predominates.
For larger open cross-sections, such as I-sections, warping torsion is generally predominant.
The St. Venant torsion component is typically ignored for I-sections with slender webs and all torsion is assumed resisted by warping torsion.
Notes: The total torsion resistance is the sum of the St. Venant torsion resistance and the warping torsion resistance, or the resistance that results from the restraint of warping. The differential equation defining the total torsional moment resistance, T, whenever warping restraint is present is given by the equation on this slide. Knowing the boundary conditions, the differential equation can be solved for the twist angle, , and its various derivatives leading to exact theoretical solutions for the various torsional stresses and flange lateral bending moments. In lieu of solving a complex differential equation, however, flange lateral bending is commonly determined in design by reasonable approximations, or by direct computation in a 3D finite element model of the section that properly recognizes the lateral bending stiffness.
In design, it is often convenient and always conservative to base the design on the dominant type of torsion resistance for the section under consideration and neglect the effects of the other type of torsion resistance. For closed cross-sections, such as box girders, and for certain smaller singly-symmetric and unsymmetrical open cross-sections, such as rolled channels, tees or angles, St. Venant torsion generally predominates. For larger open cross-sections, such as I-sections, warping torsion is generally predominant. Without a significant force couple distance between the shear flows across the thickness of any given element of the I-section, the ability of I-sections to develop St. Venant torsion shear resistance is low. The resistance of the flanges to twisting and the interaction between the flanges and web will cause the section to distort. When web distortion becomes significant, the two flanges plus the adjacent portions of the web act as semi-independent beams bent in the transverse direction. As a result, the more slender the web, the more the St. Venant torsion stiffness is reduced causing a greater portion of the total torque to be resisted by warping torque than indicated by strength of materials theory (assuming warping restraint is present). For this reason, St. Venant torsion stiffness is conservatively neglected in determining the elastic lateral-torsional buckling resistance of slender-web I-sections (Lesson 8) in the AASHTO LRFD Specifications. For compact web and noncompact web sections (Lesson 8), the use of the full St. Venant torsional stiffness is permitted in determining the elastic lateral-torsional buckling resistance if the ratio of the strong-axis moments of inertia of the compression flange to the tension flange is greater than or equal to 0.3.

## Slide 84: Torsional Force Effects in I-Sections
I-sections subject to major-axis bending and torsion are typically designed for the following force effects:
  Normal stresses due to the major-axis bending moment;
  Flange lateral bending stresses due to warping torsion;
  Shears due to the major-axis bending moment
Shears due to St. Venant torsion and warping torsion in I-sections are generally small and are typically neglected.
Notes: As described previously, in I-sections, warping torsion results in the development of transverse shears in the flanges, along with flange lateral bending moments and associated flange lateral bending stresses. The warping torque is typically not used in the design of open sections. The flange lateral bending moment times the distance between the flange centers is often referred to as the “bimoment”, which is commonly used in the computation of certain fundamental torsional section properties. These properties are not employed in conventional designs.
Individual I-sections subject to major-axis bending and torsion are typically designed for the force effects shown on this slide. The girders are designed for the normal stresses due to the major-axis bending moment and flange lateral bending stresses due to warping torsion, as shown in the top figure, and for shears resulting from the major-axis bending moment, as shown in the bottom figure. Shears due to St. Venant torsion and warping torsion in I-sections are generally small and are typically neglected. Flange lateral bending stresses are the primary action consideration in the design of I-sections for torsion.

## Slide 85: Potential Sources of Torsion
Horizontal Curvature
Support Skew
Notes: Potential sources of torsion in steel-girder bridges include horizontal curvature and support skew.
In curved bridges, the torsion results from radial components of the compressive and tensile forces in the flanges due to major-axis bending. The radial components result from the non-collinearity of the forces in the horizontally curved flanges. The radial components act in opposite directions in the top and bottom flanges creating a distributed torque along the entire length of the girders. The distribution of the radial flange forces (and the resulting torque) is proportional to the shape of the major-axis bending moment diagram. Due to the torsional effects resulting from curvature, a single curved girder by itself is not stable without some form of torsional restraint. This restraint is typically provided by the cross-frames between the individual girders.
In skewed bridges, the torsion results from the differential vertical deflections that occur at each end of the intermediate cross-frames, which occur primarily because the cross-frames are typically connected to the adjacent girders at different positions along the length of each girder. The girders twist due to the compatibility of the cross-frame to member connectivity. Because the cross-frame member lengths must be maintained, twisting of the girders is inevitable. If the skews at both ends of the span are parallel, the girders twist in opposite directions at their ends.
Photo credit: HDR

## Slide 86: Potential Sources of Torsion
Eccentric Loads
  (e.g., overhang brackets)
Lateral Loads
  (e.g., wind loads)
Notes: Torsion can also result from eccentric loads, e.g., loads induced by deck overhang brackets acting on exterior girders during construction, and by lateral loads such as wind loads.
The eccentricity of the deck weight and other loads acting on the deck overhang brackets creates equal and opposite lateral forces on the exterior (fascia) girder flanges that result in torsional moments. The resultant of the lateral wind loads acting on the girders is typically not applied through the shear center of the girders also resulting in torsional moments.
Photo credit: HDR

## Slide 87: Horizontal Curvature
Notes: An example curved and skewed steel I-girder bridge is shown. The effects of curvature and skew are explored further on subsequent slides.
Photo credit: HDR

## Slide 88: Flange Lateral Bending - Curvature
88
Notes: As mentioned previously, flange lateral bending is commonly determined in design by reasonable approximations, or by direct computation in a 3D finite element model of the section that properly recognizes the lateral bending stiffness. This slide and the following two slides will discuss how to predict the flange lateral moments due to curvature in an approximate fashion.
Shown in the top left figure on this slide is a partial free-body of a portion of a horizontally curved girder in-between two cross-frames. This portion of the girder is assumed taken from the center region of the span; thus, the girder segment is subjected to near constant positive major-axis bending moment. Internally, because of the curvature, the axial compressive forces in the girder flanges created by the major-axis bending moment are not collinear along any given segment of the flange. Therefore, to maintain equilibrium, radial flange forces must be created in the girder, as illustrated in the plan view of the top flange shown in the bottom left figure on this slide. In this case, the top flange is in compression, and so the radial force is directed outward. Ignoring the effect of the web, the axial force in the girder flange may be taken as M/h, where M is the major-axis bending moment and h is the depth between flange centerlines.
The radial component of flange force due to curvature may be assumed to act as a radial distributed force, q, over the length of the flange in-between the cross-frames as shown in the center figure on this slide. The magnitude of the radial distributed force, q, can best be derived by examining a very small segment of the flange (shown shaded in orange in the center figure on this slide). For the equilibrium condition of this small segment of the flange (isolated in the top right figure on this slide), the direction of q must be reversed. Although the radial force, q, and axial force, F, vary along the flange in proportion to the major-axis bending moment, for a very small segment of the flange, they may be considered constant. As shown in the calculations given on this slide, from the equilibrium equation in the radial direction, the magnitude of the virtual distributed radial component of flange force on a curved girder flange can be derived as q=M/hR, where M is the major-axis bending moment, R is the girder radius, and h is the depth between flange centerlines.

## Slide 89: Flange Lateral Bending - Curvature
Notes: Cross-frames in curved bridges help resist flange lateral bending moments and stresses, and thus, act as lateral supports for the flanges. As described on the preceding slide, torsion and the associated lateral bending due to curvature is caused by radial flange forces. Thus, flange lateral bending moments and stresses can be determined in an approximate fashion by isolating each flange and analyzing the flange as a straight flange rigidly supported at each cross frame.
The flange is loaded by the appropriate distributed radial flange force due to curvature derived on the preceding slide, M/hR, as shown on this slide for a top flange from a two-span continuous girder. M is the total factored major-axis bending moment in the curved girder, which can be determined either from an approximate analysis or a refined 2D or 3D analysis, h is the vertical depth between the flange centerlines, and R is the radius of the girder under consideration. Since the radial flange force is directly proportional to M, the distribution of the force follows the shape of the major-axis bending moment diagram. In regions where the top flange is in compression (i.e., out in the spans), the radial forces are directed outward away from the center of curvature. In the region where the top flange is in tension over the interior pier, the radial forces are directed inward towards the center of curvature. The bottom flange is subject to equal and opposite radial flange forces, as shown on Section A-A.
In lieu of analyzing a multi-span continuous beam such as the one shown here for the distributed radial flange force, a simpler conservative assumption can be made by isolating a portion of the flange out in the span in-between two cross-frames where the radial flange force is reasonably constant (shaded in purple on this slide) .

## Slide 90: Flange Lateral Bending - Curvature
Notes: This slide shows a cross-section and a plan view of that isolated portion of the top flange in-between the two cross-frames spaced at a distance, . The assumption is made that the radial flange force has a constant value of M/hR, where M is the factored major-axis bending moment at each cross-frame and h is the vertical depth between the flange centerlines. For simplicity, the web depth, D, is conservatively used in place of h, resulting in a lateral distributed force of M/DR.
Since the cross-frames are assumed to act as rigid supports for the flanges, the lateral flange moment at each cross-frame, Mlat, due to the effects of curvature can then be conservatively calculated in an approximate fashion from the fixed-end moment equation shown at the bottom left of this slide. This approximate equation is provided in AASHTO LRFD Article C4.6.1.2.4b. The lateral flange bending stress, f, is then determined by dividing the lateral moment by the lateral section modulus of the flange under consideration, Slat = tfbf2/6, resulting in the equation shown at the bottom left of this slide (the ‘6’ has been moved to the numerator of the equation).
The approximate equation for Mlat assumes the presence of a cross-frame at the point under investigation. Therefore, at points not actually located at cross-frames, flange lateral moments from the equation may not be strictly correct. The equation also assumes approximately equal adjacent unbraced lengths such that due to approximate symmetry boundary conditions, the ends of the unbraced length are effectively torsionally fixed. Other more appropriate idealizations should be considered when this assumption does not approximate actual conditions; e.g., unbraced lengths adjacent to abutments.

## Slide 91: Effects of Skew
Notes: A photo of a skewed steel bridge being erected is shown on this slide.
Photo Credit: HDR

## Slide 92: Flange Lateral Bending - Skew
Consider flange lateral bending effects wherever cross-frames are discontinuous.
Flange lateral bending effects are less critical in regions where cross-frames are contiguous.
Determination of flange lateral bending effects:
  Preferably by refined analysis of the superstructure, or
  Use approximate values given in AASHTO LRFD Art. C6.10.1.
Notes: Flange lateral bending effects due to skew should be considered in all regions of the girders where cross-frames are discontinuous. This includes regions adjacent to supports skewed more then 20 degrees from normal for which it is recommended that the first cross-frame adjacent to the skewed support be offset a minimum distance, O, as shown in the top framing plan on this slide to avoid a stiff transverse load path near the support (refer to AASHTO LRFD Article C6.7.4.2 and Lesson 10 for further details). Another example of discontinuous cross-frames is where the cross-frames are arranged in a staggered pattern along the length of the span, as shown in the bottom figure. This pattern reduces the transverse stiffness of the bridge by allowing the flanges to flex in the transverse direction. By reducing the transverse stiffness of the superstructure, the forces in the transverse bracing members are reduced. Staggering the cross-frames also has the effect of increasing the lateral bending stresses in the girder flanges. Often, this lateral bending is not critical, however, and the net result is a desirable reduction in cross-frame forces. Lateral bending effects due to skew are typically less critical in regions where cross-frames are contiguous, or arranged in a continuous line across the width of the bridge, as shown in the top framing plan, and may be ignored.
Closed-form solutions to estimate the flange lateral bending stresses and the restoring forces in the cross-frame members in skewed bridges, with or without discontinuous cross-frame lines, do not currently exist so these effects are preferably determined through a refined structural analysis of the bridge superstructure. In the absence of calculated values of flange lateral bending stresses from a refined analysis, estimates for these stresses are provided in AASHTO LRFD Article C6.10.1, but their use is not recommended for curved bridges with skewed supports, except perhaps for preliminary design.

## Slide 93: Flange Lateral Bending - Skew
Flange lateral bending effects due to skew are less critical in exterior (fascia) girders.
Flange lateral bending effects are larger in interior girders relative to exterior (fascia) girders – particularly for staggered arrangements.
BDS Art. C6.10.1:
  Top pattern: Ext. –> f = 7.5 ksi
  Int. –> f = 10.0 ksi
  Staggered: Ext. –> f = 2.0 ksi
  Int. –> f = 10.0 ksi
  All values are unfactored.
Notes: Exterior girders (i.e., fascia girders) always have cross-frames on one side, but since there are no opposing cross-frames on the other side, flange lateral bending due to skew effects is usually smaller in these girders, which is fortuitous since the outside girder often has critical major-axis bending moments compared to the other girders. Interior girders are generally subject to significantly larger lateral flange moments due to skew effects relative to exterior girders, in particular, whenever a discontinuous cross-frame arrangement is employed along the entire length of the bridge (i.e., a staggered arrangement).
In the absence of calculated values of the flange lateral bending stresses from a refined analysis, conservative estimates for these stresses are provided in AASHTO LRFD Article C6.10.1 as mentioned previously. These estimates are based on a limited examination of refined analysis results for bridges with skews approaching 60 degrees from normal and an average D/bf ratio of approximately 4.0. As such, these estimates represent, at best, a rough approximation of the actual flange lateral bending stresses, and as a result they should be used in a conservative, simplified manner. The suggested estimate for the total unfactored f in a flange at a cross-frame due to the use of discontinuous cross-frame lines at or near supports, but not along the entire length of the bridge (as shown in the top framing plan), is 10.0 ksi for interior girders and 7.5 ksi for exterior girders. For a staggered arrangement as shown in the bottom framing plan, a value of 2.0 ksi is suggested for f for the exterior girders in such cases, with the suggested value of 10 ksi retained for the interior girders. In all cases, it is suggested that the recommended unfactored values of f be proportioned to dead and live load in the same proportion as the unfactored major-axis dead and live load stresses at the section under consideration.

## Slide 94: Overhang Bracket Force Effects BDS 6.10.3.4
Notes: The most common method of deck overhang forming is shown on this slide. Steel brackets supporting removable lumber forms are used to support the overhang concrete and most commonly also support the deck finishing machine. As shown, they bear on the girder near the bottom flange with the diagonal leg of the bracket pushing inward on the web and flange. At the top, a similar outward force exists. This combination of “push and pull” forces creates torsion and flange lateral bending in exterior steel beams during deck casting.
Photo credit: HDR

## Slide 95: Flange Lateral Bending – Deck Overhangs
Notes: The eccentricity of the deck weight and other loads acting on the overhang brackets during construction creates applied torsional moments on the exterior (fascia) girders. The torsional moments bend the top flanges outward resulting in lateral bending stresses that must be considered in the design of the flanges. The top flange must have sufficient capacity to resist these lateral loads acting in combination with the vertical loads resulting from the deck casting. The effect of the reactions from the brackets on the cross-frame forces should also be considered (Lesson 10). The overhang brackets, which are usually spaced at 3 to 4 feet along the exterior girders, are typically attached to the top flanges of the girders. The brackets may either bear directly on the web or be carried to (or near) the intersection of the bottom flange and the web, which is preferred.
The lateral force, F, on the flanges due to the vertical load, P, on the overhang brackets may be approximated as shown on this slide for a bracket extending down to the bottom flange. The engineer must approximate the portion of total load carried at the tip of the overhang (Load P) since a large portion of vertical load is also carried at the bracket to the web intersection where a diagonal hanger (not shown) is located. From the equation for F shown in the figure, it is evident how F increases and the force on the web increases when the bracket bears directly on the web.

## Slide 96: Flange Lateral Bending – Deck Overhangs
F = uniformly distributed lateral overhang bracket force
Pf = concentrated finishing machine lateral overhang bracket force
Notes: Similar to the approximation for the flange lateral bending moments due to curvature discussed previously in this lesson (Slide 90), the approximate fixed-end moment equations shown at the bottom of this slide may then be used to conservatively estimate the maximum lateral bending moments, Mlat, in the flanges acting at the cross-frames due to the lateral overhang bracket forces in the absence of a more refined analysis. The first equation on the left applies if a statically equivalent uniformly distributed lateral overhang bracket force, F (kips/in.), is assumed. The second equation in the center applies if a statically equivalent concentrated lateral overhang bracket force, Pf (kips), is assumed to act at the middle of the unbraced length, . Pf is a lateral force in this case and is not the same as the vertical load, P, acting on the deck overhang shown on the preceding slide. Overhang bracket dead loads are typically assumed applied uniformly. The finishing machine lateral overhang bracket force may be assumed to be applied as a single concentrated load. Finishing machine truss loads are typically available from the manufacturer (e.g., Bidwell).
The two equations are based on the assumption of interior unbraced lengths in which the flange is continuous with adjacent unbraced lengths. In addition, approximately equal adjacent unbraced lengths are also assumed, such that the ends of the unbraced length under consideration are effectively torsionally fixed. When these assumptions do not approximate actual conditions for the unbraced length under consideration, other more appropriate idealizations should be considered. Once the lateral bending moments are obtained, the lateral bending stress in the flange under consideration can be computed based on the lateral section modulus of the rectangular flange, as shown in the bottom right equation on this slide.

## Slide 97: Flange Lateral Bending – Deck Overhangs
Example – taken from NSBA SBDH Design Example 1 (positive moment region – exterior girder)
Estimate the factored lateral flange force, F, and the maximum lateral bending moment and lateral bending stress in the top flange due to the overhang load, P.
Use a load factor = 1.4 (AASHTO LRFD Article 3.4.2.1) – Lesson 7 (Slide 15)
Deck plus haunch weight (DC): P = 255 lbs/ft
Overhang deck forms (C): P = 40 lbs/ft
Screed rail (C): P = 85 lbs/ft
Railing (C): P = 25 lbs/ft
Walkway (C): P = 125 lbs/ft
Finishing machine (C): P = 3,000 lbs
 = 24’-0”
1” x 16”
Notes: To illustrate, the factored lateral flange force, F, and maximum factored lateral bending moment and lateral bending stress in the top flange due to the vertical deck overhang load, P, will be estimated for the deck overhang configuration shown on this slide, which is taken from Design Example 1 of the NSBA Steel Bridge Design Handbook (SBDH). The girder is an exterior girder, and the section is in a positive moment region in the end span of the three-span continuous girder. The web depth of the girder is 69 inches, and the length of the deck overhang is 3.5 feet. The top flange of the girder is 1” x 16”. The cross-frame spacing, , in this region is 24.0 feet.
A reasonable estimate of the unfactored vertical loads, P, acting on the deck overhang is shown. Since the bracket is assumed to extend near the edge of the deck overhang, it can be assumed that half of the deck overhang weight is placed on the fascia girder and half is placed on the overhang brackets. One-half of the deck haunch weight is also conservatively included. This represents the component dead load (DC) acting on the overhang bracket. The loads also include estimated loads due to the overhang deck forms, the screed rail for the finishing machine, a walkway and railing for the workers, plus one-half the weight of the finishing machine truss, plus some additional load to account for the weight of the engine, drum and operator assumed to be located on one side of the truss. These loads are all considered to be construction loads (C), which are temporary loads acting on the bridge only during construction. In this example, a load factor of 1.4 will be applied to the overhang DC loads (i.e., deck plus haunch weight acting on the overhang) plus the overhang dead and live load construction (C) loads. AASHTO LRFD Article 3.4.2.1 specifies that in addition to the applicable Strength load combinations for construction (i.e., Strength I in this case or 1.25DC + 1.25DW + 1.5C, which is assumed not to control in this example), primary steel superstructure components are to be investigated for an additional special load combination equal to 1.4 times the component dead loads, DC, and any construction loads, C, that are applied to the fully erected steelwork (the load combinations for construction are discussed further on Slide 15 of Lesson 7). The load modifier  is assumed to be 1.0.

## Slide 98: Flange Lateral Bending – Deck Overhangs
DC Load + Dead Load C Loads (uniformly distributed):
Notes: First, calculate the lateral flange force, F, due to the vertical overhang loads, P. For an overhang bracket extending down to the bottom flange, F can be approximated as P times the length of the overhang divided by the web depth, D, which is equal in this case to 0.609P.
For the component dead loads, DC, and dead load construction loads (C), which are uniformly distributed loads, the factored vertical load, P, acting on the deck overhang is computed to be 742 lbs/ft. Multiplying P by 0.609 gives a uniformly distributed factored lateral force, F, acting on the flanges of 451.9 lbs/ft. Using the fixed-end moment equation for a uniformly distributed load taken from Slide 96 in this lesson results in a factored flange lateral bending moment at the cross-frames of 21.7 kip-ft for the 24.0-foot cross-frame spacing in this region. Dividing the flange lateral moment by the lateral section modulus of the 1” x 16” top flange results in a factored flange lateral bending stress in the top flange at the cross-frames due to the DC loads and dead load C loads of 6.10 ksi.

## Slide 99: Flange Lateral Bending – Deck Overhangs
Finishing Machine Load (Live Load C Load – concentrated load):
Notes: For the finishing machine load, which is considered to be a concentrated live load C load (impact is not included in this example), the factored vertical load, P, acting on the deck overhang is computed to be 4,200 lbs. Multiplying P by 0.609 gives a factored concentrated lateral force, F (or Pf), acting on the flanges of 2,558 lbs. Using the fixed-end moment equation for a concentrated load assumed acting at the middle of the unbraced length taken from Slide 96 in this lesson results in a factored flange lateral bending moment at the cross-frames of 7.67 kip-ft for the 24.0-foot cross-frame spacing in this region. Dividing the flange lateral moment by the lateral section modulus of the 1” x 16” top flange results in a factored flange lateral bending stress in the top flange at the cross-frames due to the finishing machine load of 2.16 ksi. The total factored flange lateral bending stress in the top flange at the cross-frames due to the DC loads plus the dead load C loads plus the finishing machine live load C load is 8.26 ksi.
Approaches to estimate the flange lateral bending moments and lateral bending stresses due to wind loads during construction will be discussed further in Lesson 7.

## Slide 100: FLANGE-STRESS REDUCTION FACTORS – BDS 6.10.1.10
Notes: Two flange-stress reduction factors used in the computation of the nominal flexural resistance of a member will be discussed next in this lesson; namely, the hybrid factor, Rh, and the web load-shedding factor, Rb.

## Slide 101: Hybrid Factor, Rh – BDS 6.10.1.10.1
Hybrid Girder -> a fabricated steel girder with a web that has a specified minimum yield strength less than one or both flanges.
Hybrid girders may be used in straight or horizontally curved bridges.
Recommended for greater design efficiency that the difference in the specified minimum yield strengths of the web and the higher strength flange be limited to one steel grade.
Notes: A hybrid girder is defined as a fabricated steel girder with a web that has a specified minimum yield strength less than one or both flanges. Hybrid girders may be used in straight or horizontally curved bridges.
Hybrid girders are covered in general in AASHTO LRFD Article 6.10.1.3. For greater design efficiency, it is recommended that the difference in the specified minimum yield strengths of the web and the higher strength flange be limited to one steel grade. That is, the specified minimum yield strength of the web should not be less than the larger of 70 percent of the specified minimum yield strength of the higher strength flange and 36.0 ksi. This minimum limit on the web yield strength helps guard against early inelastic web bend-buckling of slender hybrid webs.

## Slide 102: Hybrid Factor, Rh
Hybrid girders utilizing Grade HPS 70W steel for the flanges and Grade 50W steel for the web have proven to be a popular and economical option, primarily in regions of negative bending in longer continuous spans.
Hybrid girders utilizing a tension flange with a higher yield stress (Grade HPS 70W) than the web and a compression flange with the same yield stress as the web (Grade 50W) may also prove economical, particularly for composite sections in positive bending in longer continuous spans.
Notes: Hybrid girders utilizing Grade HPS 70W steel for the flanges and Grade 50W steel for the web have proven to be a popular and economical option, primarily in regions of negative bending in longer span continuous-span girders. Hybrid girders utilizing a tension flange with a higher yield stress (Grade HPS 70W) than the web and a compression flange with the same yield stress as the web (Grade 50W) may also prove economical, particularly for composite sections in positive bending on longer-span continuous-span girders. Because of stability issues before the concrete deck cures, it is often necessary to use a top flange that is not fully stressed at the strength limit state in regions of positive flexure.

## Slide 103: Hybrid Factor, Rh
The hybrid factor, Rh, is used to account for the effect of earlier yielding of the lower strength steel in the web at the strength limit state.
Notes: The hybrid factor, Rh, is used to account for the effect of earlier yielding of the lower strength steel in the web. As illustrated on this slide, a redistribution of stress from the web to the flanges occurs in hybrid sections as a result of the early localized yielding of the lower strength web; the redistribution occurs to both the compression and tension flanges.
The hybrid factor, which is less than or equal to 1.0, can be used to either reduce the section modulus to each flange effectively increasing the flange stresses, or to reduce the nominal flexural resistance of each flange. Design specifications, including the AASHTO LRFD Specifications, have traditionally followed the latter course. In the AASHTO LRFD Specifications, the hybrid factor to be applied to the nominal flexural resistance of each flange of a hybrid girder. For rolled shapes, which are obviously homogeneous sections based on the nominal yield strength, homogeneous built-up sections, and built-up sections with a higher-strength steel in the web than in both flanges, Rh is to be explicitly taken equal to 1.0.
For hybrid sections that are composite in the final condition, but that are noncomposite during construction (i.e., sections in bridges built using unshored composite construction), Rh must be calculated separately for the noncomposite and composite sections. For constructibility checks and service limit state checks of a hybrid girder where the factored flange flexural stress does not exceed the specified minimum yield strength of the web, Rh is to be taken equal to 1.0.

## Slide 104: Hybrid Factor, Rh
 = the smaller of Fyw/fn and 1.0
Afn = sum of the flange area and the area of any cover plates on the side of the neutral axis corresponding to Dn (in.2)
Dn = larger of the distances from the elastic neutral axis of the cross-section to the inside face of either flange (in.)
fn = for sections where yielding occurs first in the flange, a cover plate or the longitudinal reinforcement on the side of the neutral axis corresponding to Dn, the largest of the specified minimum yield strengths of each component in the calculation of Afn (ksi). Otherwise, the largest of the elastic stresses in the flange, cover plate or longitudinal reinforcement on the side of the neutral axis corresponding to Dn at first yield on the opposite side of the neutral axis.
Notes: The equation for Rh in AASHTO LRFD Article 6.10.1.10.1 considers all possible combinations associated with different positions of the elastic neutral axis and different yield strengths of the top and bottom flange elements in a non-iterative fashion. The equation may be used in lieu of a direct iterative strain compatibility analysis. Singly symmetric sections (both noncomposite and composite) are handled by focusing on the side of the neutral axis where nominal yielding occurs first, or the side of the neutral axis subject to the most extensive web yielding prior to first yielding of any flange element (i.e., a flange, cover plate, or longitudinal reinforcement associated with the top flange only). All flange elements on the side of the neutral axis where nominal yielding occurs first are conservatively assumed to be located at the edge of the web in the calculation of Rh. In addition, any shift in the neutral axis caused by the effect of web yielding is considered negligible.
The first step in computing Rh is to determine Dn, which is to be taken as the larger of the distances from the elastic neutral axis of the cross-section to the inside face of either flange. In cases where the neutral axis is located at the mid-depth of the web, Dn is to be taken as the distance from the neutral axis to the inside face of the flange on the side of the neutral axis where yielding occurs first. Should yielding occur simultaneously on both sides of the neutral axis, Dn should be taken as the distance to the flange element with the smaller value of Afn. Once the value of Dn has been established, the next step is to calculate Afn. Afn is defined as the sum of the areas of the flange elements on the side of the neutral axis corresponding to Dn. With Dn and Afn established, the constant  can then be calculated. To calculate the constant , the stress fn must first be calculated. For sections where nominal yielding occurs first in a flange element on the side of the neutral axis corresponding to Dn, which is the case in most instances, fn is to be taken as the largest of the specified minimum yield strengths of each flange element included in the calculation of Afn. Should yielding occur first on the other side of the neutral axis, fn is to be taken as the largest of the calculated elastic stresses in the various flange elements on the side of the neutral axis corresponding to Dn when nominal first yielding occurs on the opposite side.

## Slide 105: Hybrid Factor, Rh
Example – taken from NSBA SBDH Design Example 1 (interior-pier section – negative moment - exterior girder – hybrid section)
Calculate the hybrid factor, Rh, at the strength limit state
The longitudinal reinforcement will be included and the concrete in tension is ignored at the strength limit state
Fyc = 70 ksi; Fyt = 70 ksi; Fyw = 50 ksi
Ars = 10.56 in.2; Centroid = 4.63 in. from the bottom of the deck
Notes: In this example, the hybrid factor, Rh, at the strength limit state will be computed for the composite section shown, which is taken from Design Example 1 of the NSBA Steel Bridge Design Handbook (SBDH). The girder is an exterior girder, and the section is at an interior pier, which is in a negative moment region of a three-span continuous girder (at 1.0L). The section is a hybrid section with a specified minimum yield strength of the compression (bottom) flange, Fyc, of 70 ksi. The specified minimum yield strength of the tension (top) flange is also 70 ksi and the specified minimum yield strength of the web is 50 ksi. The longitudinal reinforcement will be included in the calculation and the concrete in tension is ignored at the strength limit state. The area of the minimum 1 percent longitudinal reinforcement was computed previously to be 10.56 in.2, and the centroid of the longitudinal reinforcement (assumed placed in two layers) was computed previously to be 4.63 in. from the bottom of the structural concrete deck.

## Slide 106: Hybrid Factor, Rh
Calculate Dn or the larger of the distances from the elastic neutral axis of the cross-section to the inside face of either flange. From previous calculations:
Distance from N.A. to top flange = 34.5 – 2.46 = 32.04 in.
Distance from N.A. to bot. flange = 34.5 + 2.46 = 36.96 in.
Dn = 36.96 in.
Calculate Afn or the sum of the area of the flange elements on the side of the neutral axis corresponding to Dn: Afn = 20(2) = 40.0 in.2 (bottom flange)
fn is taken as the largest of the specified minimum yield strengths of each flange element included in the calculation of Afn: fn = 70 ksi (bottom flange)
Notes: First, calculate Dn or the larger of the distances from the elastic neutral axis of the cross-section to the inside face of either flange. For composite sections in negative flexure at the strength limit state, use the section consisting of the steel girder plus the longitudinal reinforcement to calculate Dn. From previous calculations for this section in this lesson, the distance from the neutral axis to the inside face of the top flange is 32.04 in. and to the inside face of the bottom flange is 36.96 in. Therefore, Dn is 36.96 in.
Next, calculate Afn or the sum of the area of the flange elements on the side of the neutral axis corresponding to Dn. Since there are no cover plates and Dn is measured to the bottom flange, the only flange element contributing to Afn is the bottom flange. Therefore, Afn = 20(2) = 40.0 in2. β is then calculated to be 1.04.
Since the flanges are the same yield strength, nominal yielding will occur first on the side of the neutral axis corresponding to Dn (separate calculations show that the 60-ksi longitudinal reinforcement does not yield first). For sections where nominal yielding occurs first in a flange element on the side of the neutral axis corresponding to Dn, fn is taken as the largest of the specified minimum yield strengths of each flange element included in the calculation of Afn. Therefore, fn = 70.0 ksi. ρ is then calculated to be 0.714 and Rh is calculated to be 0.984.
If the concrete deck is considered to be effective in negative flexure at the service limit state, as permitted in AASHTO LRFD Article 6.10.4.2.1 (to be discussed further in Lesson 7), a different value of Rh should be calculated for use in the service limit state design checks. In this case, Dn may conservatively be taken as the distance from the neutral axis of the short-term (n) composite section to the inside face of the bottom flange.

## Slide 107: Web Load Shedding Factor, Rb BDS 6.10.1.10.2
Rb is a postbuckling strength reduction factor that accounts for the nonlinear variation of stresses subsequent to local bend-buckling of slender webs (applied at the strength limit state).
Rb accounts for the reduction in the section flexural resistance caused by the shedding of compressive stresses from a slender web and the corresponding increase in the flexural stress within the compression flange.
The tension flange stress is not increased significantly by the shedding of the web compressive stresses.
Notes: When the theoretical web bend-buckling load is reached, a slender-web section (Lesson 8) does not fail but has significant post-buckling resistance that can be utilized at the strength limit state. As buckling of the compression zone of the web increases, the ability of the web to carry its portion of the load, as computed by ordinary beam theory, decreases. However, this does not mean failure. Instead, a redistribution of stress to the stiffer longitudinal elements (i.e., the compression flange and the immediately adjacent portion of the web) occurs. As a result, for a given moment, the stress in the compression portion of the web that is deflecting laterally is less than that calculated for a linear distribution and the stress in the compression flange is greater, as illustrated in the figure on this slide. Therefore, yielding may occur in the compression flange before the yield moment calculated from ordinary beam theory is attained. The effect of load shedding to the compression flange is not considered significant and is ignored whenever the nominal flexural resistance exceeds the yield moment, My. The tension flange stress is also not increased significantly by the shedding of the web compressive stresses.
As discussed previously in this lesson, a similar redistribution of stress from the web to the flanges occurs in hybrid sections as a result of the early localized yielding of the lower strength web; the primary difference being that in the case of the hybrid section, the redistribution occurs to both the compression and tension flanges. In this case, the redistribution of resulting from localized bend buckling of the web occurs only to the compression flange. The web load-shedding factor, Rb, is used to account for the reduced contribution of the web to the nominal flexural resistance resulting from web bend buckling of slender webs. The web load-shedding factor, which is less than or equal to 1.0, can be used to either reduce the section modulus to the compression flange effectively increasing the flange stress, or to reduce the nominal flexural resistance of the compression flange. Again, design specifications, including the AASHTO LRFD Specifications, have traditionally followed the latter course. In the AASHTO LRFD Specifications, the web load-shedding factor to be applied to the nominal flexural resistance of the compression flange at the strength limit state.

## Slide 108: Web Load-Shedding Factor, Rb
For webs without longitudinal stiffeners:
4.6 ≤ ke ≤ 5.7
ke = edge-condition coefficient
bfc = width of the compression flange (in.)
tfc = thickness of the compression flange (in.)
Dc = depth of the web in compression in the elastic range (in.)
tw = web thickness (in.)
Notes: For webs without longitudinal stiffeners, the web load-shedding factor, Rb, is given in AASHTO LRFD Article 6.10.1.10.2 by the equation shown on this slide. A different equation is given to calculate Rb for webs with longitudinal stiffeners.
The term, λrw, is the web slenderness limit for a noncompact web (Lesson 8). Sections with a web slenderness based on the depth of the web in compression in the elastic range, 2Dc/tw, exceeding λrw are termed slender-web sections. For these sections, web bend buckling (Lesson 7) is assumed to occur in the compression zone of the web prior to reaching the specified minimum yield strength of the compression flange, Fyc, at the strength limit state. As a result, the compressive stresses in the web are shed from the web to the compression flange and the web load-shedding factor, Rb, will be less than 1.0.
The coefficient, ke, in the expression for λrw is an edge-condition coefficient that accounts for the assumed boundary conditions at the web-to-compression flange juncture. The coefficient transitions between a lower limit of 4.6 (assuming simply-supported boundary conditions) and an upper limit of 5.7 (assuming approximately 80 percent of fixed boundary conditions) as a function of the quantity, awc. awc is the ratio of two times the area of the web in compression to the area of the compression flange.

## Slide 109: Web Load-Shedding Factor, Rb
Example – taken from NSBA SBDH Design Example 1 (interior-pier section – negative moment - exterior girder – hybrid section)
Calculate the web load-shedding factor, Rb, at the strength limit state
The longitudinal reinforcement will be included and the concrete in tension is ignored at the strength limit state
Fyc = 70 ksi; Fyt = 70 ksi; Fyw = 50 ksi
Ars = 10.56 in.2; Centroid = 4.63 in. from the bottom of the deck
Notes: In this example, the web load-shedding factor, Rb, at the strength limit state will be computed for the composite section shown, which is taken from Design Example 1 of the NSBA Steel Bridge Design Handbook (SBDH). The girder is an exterior girder, and the section is at an interior pier, which is in a negative moment region of a three-span continuous girder (at 1.0L). The section is a hybrid section with a specified minimum yield strength of the compression (bottom) flange, Fyc, of 70 ksi. The specified minimum yield strength of the tension (top) flange is also 70 ksi and the specified minimum yield strength of the web is 50 ksi. The longitudinal reinforcement will be included in the calculation and the concrete in tension is ignored at the strength limit state. The area of the minimum 1 percent longitudinal reinforcement was computed previously to be 10.56 in.2, and the centroid of the longitudinal reinforcement (assumed placed in two layers) was computed previously to be 4.63 in. from the bottom of the structural concrete deck.

## Slide 110: Web Load-Shedding Factor, Rb
Determine if the section is a slender-web section. For sections in negative flexure at the strength limit state, use Dc for the section consisting of the steel girder plus the longitudinal reinforcement (i.e., Dc = 36.96 in.)
Section is a slender-web section
Notes: First, determine if the section is a slender-web section by comparing the web slenderness based on the elastic depth of the web in compression, 2Dc/tw, for the section consisting of the steel girder plus the longitudinal reinforcement (= 131.4) to the slenderness limit for a noncompact web, λrw. The slenderness limit depends on the edge-condition coefficient, ke, which is a function of the parameter, awc. awc is the ratio of two times the area of the web in compression to the area of the compression flange, and is equal to 1.04 for this example. Substituting in the expression for ke gives a ke of 7.9, which is larger than the upper limit of 5.7. Therefore, ke is equal to 5.7, which gives a slenderness limit λrw of 116. Since this limit is less than the calculated value of 2Dc/tw equal to 131.4, the section is a slender-web section and the web load-shedding factor, Rb, must be calculated. Substituting the previously calculated values into the expression for Rb gives an Rb equal to 0.989.

## Slide 111: Tension Flanges with Holes
Notes: The last topic to be covered in this lesson will be a brief discussion on the design of tension flanges of flexural members with holes.
Photo Credit: HDR

## Slide 112: Tension Flanges with Holes BDS 6.10.1.8
When checking flexural members at the strength limit state or for constructability, the following requirement must be satisfied at all cross-sections containing holes in the tension flange:
An = net area of the tension flange (in.2)
Ag = gross area of the tension flange (in.2)
ft = factored major-axis bending stress on the gross area of the tension (ksi)
Fu = specified minimum tensile strength of the tension flange (ksi)
Notes: AASHTO LRFD Article 6.10.1.8 specifies that if there are holes in the tension flange of a flexural member, all cross-sections containing holes in the tension flange must satisfy the equation shown on this slide at the strength limit state and for constructibility. It is assumed that the holes are the size of those typically used for connectors, such as bolts. For larger holes, the provisions of AASHTO LRFD Article 6.8.1 should be applied instead. The equation shown here provides a limit on the maximum bending stress in tension permitted on the gross section of the girder, neglecting the loss of area due to the holes. The factor of 0.84 in the equation is approximately equivalent to the ratio of the resistance factor for fracture of tension members, u = 0.80, to the resistance factor for yielding of tension members, y = 0.95, in the AASHTO LRFD Specification (Lesson 12). This equation will prevent holes from being located in the tension flange at or near points of maximum applied moment where significant yielding of the web, beyond the localized yielding permitted in hybrid sections, may occur.
Examples of where this equation must be checked include at bolted field splices and at locations where lateral bracing members and/or cross-frame connection plates are bolted to the tension flange of a flexural member.

## Slide 113: Lesson 6 Summary – Flexure Part 1 Fundamental Calculations
Composite vs. Noncomposite
Elastic Section Properties
Elastic Stresses in Composite Sections
Plastic Section Properties
Flange Lateral Bending
Flange-Stress Reduction Factors
Tension Flanges with Holes
Notes: This slide summarizes the various topics that were covered in Lesson 6. This lesson covered important fundamental calculations that are employed in the design of I-section flexural members. These calculations and concepts will be utilized throughout the remaining lessons of this course on the design of I-section flexural members.

## Slide 114: END