## Slide 1: Fundamentals of Steel Bridge Engineering
Lesson 12 – Tension and Compression Members
Notes: This presentation is part of the "Fundamentals of Steel Bridge Engineering" teaching aid, available at aisc.org/teachingaids. This set of (14) lessons was prepared by Frank Russo, PE, PhD and Michael Grubb, PE with support from the National Steel Bridge Alliance (NSBA) and AISC University Programs. For questions or comments on these presentations, please contact: AISC University Programs universityprograms@aisc.org

## Slide 2: Lesson 12 Roadmap – Tension and Compression Members
Tension Members
  Introduction
  Factored Tensile Resistance
  Limiting Slenderness Ratios
  Combined Loading
  Built-up Members
Compression Members
  Introduction
  Factored Compressive Resistance
  Limiting Slenderness Ratios
  Combined Loading
  Single-Angle Members
  Built-up Members
Notes: Lesson 12 deals with the design of tension and compression members; i.e. members subject to axial tension or compression.
For tension members, topics to be covered in this lesson include an introduction to the different types of tension members that are typically utilized in steel-bridge structures, the calculation of the factored tensile resistance of these members using the AASHTO LRFD provisions (including illustrative examples), the limiting slenderness ratios that apply to these members, the design for combined loading on these members, ; i.e., loading consisting of any combination of axial tension, uniaxial or biaxial flexure, and flexural and/or torsional shear, and the design of built-up tension members.
Similarly, for compression members, topics to be covered in this lesson include an introduction to the different types of compression members that are typically utilized in steel-bridge structures, the calculation of the factored compressive resistance of these members using the AASHTO LRFD provisions, the limiting slenderness ratios that apply to these members, the design for combined loading on these members; i.e., loading consisting of any combination of axial compression, uniaxial or biaxial flexure, and flexural and/or torsional shear (which includes an example illustrating the application of the these provisions to the design of a tee-section top lateral bracing member in a straight tub-girder bridge), the special design requirements for single-angle compression members (including an example illustrating the application of these provisions to the design of a single-angle member serving as the bottom strut of a cross-frame in a horizontally curved I-girder bridge), and the design of built-up compression members.

## Slide 3: TENSION MEMBERS INTRODUCTION
Notes: The first topic in this lesson will be an introduction to the different types of tension members that are typically utilized in steel-bridge structures.

## Slide 4: Typical Tension Members
Round & rectangular bars and plates
Cables
Single & double angles
Rolled W, M, S, or HP shapes
Structural tees
Rectangular & round HSS and noncomposite box sections
Built-up sections
Eyebars
Pin-connected plates
Notes: Tension members are members subject to axial tension and occur commonly in steel-bridge structures as chord and diagonal members in a truss, as tension ties in tied-arches, as bracing members; e.g., cross-frame and lateral bracing members in beam and girder bridges, and as main cables and suspenders in cable-stayed bridge and suspension bridge systems. The design of tension members is covered in AASHTO LRFD Article 6.8
Typical cross-sections of tension members are shown on this slide. Tension members may consist of a single structural shape, or they may be built-up from several structural shapes. Structural shapes used as tension members include rolled W, M, S, or HP shapes, single and double angles, structural tees, channels (not shown) and rectangular and round Hollow Structural Sections (HSS). Round and rectangular bars and plates, noncomposite box sections, and cables composed of smaller wires can also serve as tension members. Wire rope and bridge strand (not shown) can also be used as tension members; the design of cables, wire rope and bridge strand is not covered in this course.
Tension members in bridges also include eyebars and pin-connected plates. The design of eyebars is covered in AASHTO LRFD Article 6.8.6 and the design of pin-connected plates is covered in AASHTO LRFD Article 6.8.7; the design of these members is not covered in this course. Eyebars and pin-connected plates were commonly used in the nineteenth century when Engineers were often concerned with minimizing secondary stresses. They were also often more economical and faster to erect than hand-riveted construction. Since there is greater knowledge and less concern in modern design about the minimization of secondary stresses, the use of these members in new construction has largely disappeared.

## Slide 5: Built-up Tension Members
Notes: Built-up tension members typically consist of two or more steel shapes, either: 1) closely spaced shapes (e.g., angles or channels) interconnected at intervals by intermittent bolted/riveted or welded filler/stay plates, or 2) widely spaced shapes or plates connected by lacing (i.e., flat bars, angles, channels, or other shapes), tie plates (also referred to as batten or stay plates), solid plates, or perforated cover plates. Illustrations of perforated cover plates, batten plates and lacing are shown on this slide. Solid plates and perforated cover plates are most commonly used to connect widely spaced shapes or plates in modern steel bridges; lacing and tie plates are now less commonly used. The design of built-up tension members is covered in AASHTO LRFD Article 6.8.5. Built-up tension members will be discussed further later in this lesson.
The images at the center of the slide show the use of four angles to form the corners of a box section with plates used as the webs and flanges of the boxes. The image at the right, from a major river crossing, shows many different shapes all used within close proximity of each other. A mix of tension and compression members, these are representative of a variety of shapes used in older trusses. A modern truss would typically use all welded shapes. Member M9-U9 is a built-up I-section consisting of four flange angles and a web plate. Member M9-U10 has four corner angles, two web plates on each side (36” x 5/8”) and two “cover plates”, i.e., the flanges labeled as (28-12) x 5/8 in. This means the cover plates are 28 in. wide and have a 12 in. perforation / hand hole. These are used for tools and workers hands / arms to be placed inside the box to make shop and field connections. Finally, M9-L10 (L10 not shown) is made up of two C18 x 42.7 channel sections and two cover plates (30-12) x ½ in. It is common in older structures to see these various member types used in the same bridge. Engineers will configure built-up sections to have the needed tension or compression strength, and equally as important, to have common out-to-out dimensions since they must join at nodes / gusset plates and therefore must be dimensionally compatible. The out-to-out dimension of the member becomes the control to allow for easy fit-up at the gusset plates.

## Slide 6: TENSION MEMBERS Factored tensile resistance
Notes: The next topic in this lesson will cover the computation of the factored tensile resistance of tension members using the AASHTO LRFD provisions, including the calculation of the factored yield resistance on the gross section, the factored fracture resistance on the net section, the calculation of the net area, An, the calculation of the shear lag reduction factor, U, the calculation of the block shear rupture resistance, and illustrative examples illustrating the application of these provisions.

## Slide 7: Factored Tensile Resistance Yielding on the Gross Section
The factored tensile resistance, Pr, at the strength limit state for members subject to axial tension is to be taken as the lesser of the resistance for yielding on the gross section and fracture on the net section.
The factored tensile resistance for yielding on the gross section is taken as (AASHTO LRFD Article 6.8.2.1):
where:
y = resistance factor for yielding of tension members as specified in AASHTO LRFD Article 6.5.4.2 (= 0.95)
Ag = gross cross-sectional area of the member (in.2)
Fy = specified minimum yield strength of the member (ksi)
Pny = nominal tensile resistance for yielding on the gross section (kips)
Notes: AASHTO LRFD Article 6.8.2.1 specifies that the factored tensile resistance, Pr, at the strength limit state for members subject to axial tension is to be taken as the lesser of the factored tensile resistance for yielding on the gross section and fracture on the net section.
The factored tensile resistance for yielding on the gross section is to be taken as the nominal tensile resistance for yielding on the gross section, Pny, times the resistance factor for yielding of tension members, y, equal to 0.95 (AASHTO LRFD Article 6.5.4.2). Pny is equal to the specified minimum yield strength of the member, Fy, times the gross cross-sectional area of the member, Ag. Ag is to be determined considering all holes larger than those typically used for connectors (e.g., bolts). Holes that must typically be deducted when computing the gross area include access holes, pin holes and perforations. These locations are designed for general yielding over their net area.
Although steel members loaded in axial tension can generally resist a force greater than the product of their gross area and the specified minimum yield stress due to strain hardening (Lesson 1), substantial elongation due to yielding throughout the gross area along the member length could precipitate the failure of the structural system of which the member is a part. Therefore, overall yielding of the gross area is considered as a strength limit state.

## Slide 8: Factored Tensile Resistance Fracture on the Net Section
The factored tensile resistance for fracture on the net section is taken as (AASHTO LRFD Article 6.8.2.1):
where:
u = resistance factor for fracture of tension members as specified in AASHTO LRFD Article 6.5.4.2 (= 0.80)
An = net area of the member (in.2)
Fu = specified minimum tensile strength of the member (AASHTO LRFD Table 6.4.1-1) (ksi)
Pnu = nominal tensile resistance for fracture on the net section (kips)
Rp = reduction factor for holes taken equal to 0.90 for bolt holes punched full size, and 1.0 for bolt holes drilled full size or subpunched and reamed to size
U = reduction factor to account for shear lag; 1.0 for components in which force effects are transmitted to all elements, and as specified in AASHTO LRFD Article 6.8.2.2 for all other cases
Notes: If bolt holes are located at some position along the member length, the net section at these holes also must be checked in general for tension fracture on the net section through the holes. Depending on the ratio of net area to gross area, the geometry of the end connection and the mechanical properties of the steel (the most important of which is the yield-to-tensile ratio, Fy/Fu – Lesson 1 – Slide 84), the component can fail by fracture of the net area at a load smaller than that required to yield the gross area. Thus, both yielding and fracture must be checked. Holes in a member cause stress concentrations at service loads, with the tensile stress adjacent to the hole typically about three times the average stress on the net area. As load increases and the deformation continues, all fibers across the section will achieve or eventually exceed the yield strain. Failure occurs when the localized yielding results in a fracture through the net area. Since the width of the member occupied by the net area at bolt holes is generally negligible relative to the overall width of the member, strain hardening is easily achieved in the vicinity of the holes and yielding on the net area at bolt holes is not considered to be significant.
AASHTO LRFD Article 6.8.2.1 specifies that the factored tensile resistance for fracture on the net section is to be taken as the nominal tensile resistance for fracture on the net section, Pnu, times the resistance factor for fracture of tension members, u, equal to 0.80 (AASHTO LRFD Article 6.5.4.2). A higher margin of safety is typically used when considering the net section fracture resistance versus the yield resistance, as reflected in the relative values of the resistance factors for each limit state. Pnu is equal to the specified minimum tensile strength of the member, Fu (AASHTO LRFD Table 6.4.1-1), times the net area of the member, An, times the reduction factor, Rp, times the reduction factor for shear lag, U. The reduction factor, Rp, conservatively accounts for the reduced fracture resistance in the vicinity of bolt holes that are punched full size, as during the punching operation, the metal at the edge of the hole is damaged. Bolt holes on bracing members are often punched full size. No reduction in the net section fracture resistance is required for holes that are drilled full size or subpunched and reamed to size (i.e., Rp = 1.0). AASHTO LRFD Article 6.6.1.2.3 specifies that when permitted for use, unless specific information is available to the contrary, bolt holes in cross-frame, diaphragm, and lateral bracing members and their connection plates are to be assumed for design to be punched full size. The computation of the net area, An, and the reduction factor for shear lag, U, will be discussed on subsequent slides.

## Slide 9: Factored Tensile Resistance Net Area, An
The net area, An, is the product of the thickness of an element and its smallest net width.
The width of each standard bolt hole for design is to be taken as the nominal diameter of the hole (e.g., for a 7/8-in. diameter bolt, the width of a standard hole is 15/16 in.). The width of oversize and slotted holes, where permitted for use, is to be taken as the nominal diameter or width of the hole, as applicable (AASHTO LRFD Table 6.13.2.4.2-1).
For lateral connection plates, splice plates, and gusset plates, the net area of the plate, An, is not to be taken as greater than 85 percent of the gross area of the plate (AASHTO LRFD Article 6.13.5.2).
For welded connections, An is to be based on the gross section less any access holes in the connection region.
Notes: AASHTO LRFD Article 6.8.3 specifies that the net area, An, is to be taken as the product of the thickness of the member/element and its smallest net width.
The width of each standard bolt hole for design is to be taken as the nominal diameter of the hole. Maximum hole sizes for different bolt diameters are specified in AASHTO LRFD Table 6.13.2.4.2-1. For example, for a 7/8-inch diameter bolt, the maximum hole size of a standard hole is 15/16 inches.
AASHTO LRFD Article 6.13.5.2 specifies that for lateral connection plates, splice plates, and gusset plates, the net area of the plate, An, is not to be taken as greater than 85 percent of the gross area of the plate. Because the length of these connection elements is small compared to the member length, inelastic deformation of the gross section is limited. Hence, the net area of the connecting element is limited to 0.85Ag in recognition of the limited inelastic deformation and to provide a reserve capacity.
For welded connections, An is to be based on the gross section less any access holes in the connection region.
The photo illustrates bridge strengthening plates used for repair of a major river crossing.
Photo credit: W&W Afco

## Slide 10: Factored Tensile Resistance Net Area, An
The net width is to be determined for each chain of holes extending across a member or element along any transverse, diagonal, or zigzag line.
For each chain of holes, the net area is to be determined by subtracting from the gross area, the sum of the areas of all holes in the chain and adding the quantity (s2/4g)t for each space between consecutive holes in the chain when holes are staggered.
where:
de = effective width deducted for a given hole, equal to the nominal diameter or width of the hole perpendicular to the tension direction (in.)
g = transverse center-to-center spacing (gage) between the hole gage lines (in.)
s = longitudinal center-to-center spacing (pitch) between two consecutive holes (in.)
t = plate thickness at the hole along any given diagonal (in.)
Notes: The net width is to be determined for each chain of holes extending across a member or element along any transverse, diagonal or zigzag line. For each chain of holes, the net area is to be determined by subtracting from the gross area, the sum of the areas of all holes in the chain and adding the quantity (s2/4g)t for each space between consecutive holes in the chain when holes are staggered, where s is equal to the longitudinal center-to-center spacing (i.e., pitch) between two consecutive holes and g is the transverse center-to-center spacing (i.e., gage) between the gage lines of the same two holes. In the equation for An shown on this slide, de is the effective width deducted for a given hole, equal to the nominal diameter or width of the hole perpendicular to the tension direction. For hole arrangements without any stagger, the last term in the equation simply drops out.
When holes are staggered around the corner of a member (e.g., on two legs of an angle), the gage length, g, is to be obtained by using a length between the centers of the holes measured along the centerline of the member thickness. That is, the gage can be determined by imagining that the plates are unfolded into a single flat plate at the mid-thickness of the plates. Stated a different way, when holes are staggered in both legs of an angle, the gage for holes in opposite adjacent legs is to be taken as the sum of the gages from the back of the angles less the thickness of the angle.

## Slide 11: Factored Tensile Resistance Net Area, An
In designing a tension member, it is conservative and convenient to use the least net width for any chain together with the full tensile force in the member.
A slightly less conservative calculation may be obtained by subtracting the force removed by each bolt ahead of the fracture path being considered, i.e., closer to the mid-length of the member, from the full tensile force. The full force is assumed to be transferred equally by each bolt in the connection in making this calculation.
In this case, a pseudo net area that can be used to determine the full member tension fracture resistance may be calculated as:
where:
ntotal = total number of bolts in the connection
nr = remaining number of bolts after deducting the number ahead of the fracture path
T
Reduced T
Notes: In designing a tension member, it is conservative and convenient to use the least net width for any chain together with the full tensile force in the member. It is sometimes possible to achieve an acceptable, slightly less conservative design by checking each possible chain with a tensile force obtained by subtracting the force removed by each bolt ahead of that chain, i.e., closer to mid-length of the member, from the full tensile force in the member. This approach assumes that the full force is transferred equally by all bolts at one end whenever the bolts are arranged symmetrically with respect to the centroidal axis of the connected element. In such cases, the equation shown on this slide provides a pseudo net area, An, that can be used to determine the full member tension fracture resistance, where ntotal is the total number of bolts in the connection and nr is the remaining number of bolts after deducting the number ahead of the fracture path. The application of this equation will be demonstrated in a subsequent example.
The photo depicts an engineer intentionally using several rows with a reduced number of bolts at the end of a field splice plate. This was done to reduce the net section deduction in the main member until a fraction of the tension load could be transferred to the splice plate at which time a row of six bolts is used. The first three rows used only four bolts in each row. The bolt spacing and the clipped corners of the plate were all chosen to also meet sealing and spacing / edge distance requirements. The staggered pattern of six bolts was also checked, and the bolt pitch and gage were chosen so this did not control the design. It was not the tension in the splice plate that was of concern, rather the reduced net section of the main member, designed not to have bolt holes, to accept the field-drilled retrofit plate bolt holes.
Photo credit: Michael Baker International

## Slide 12: Factored Tensile Resistance Reduction Factor for Shear Lag, U
The reduction factor for shear lag, U, accounts for shear lag effects associated with end connection geometry. The effective net area is therefore equal to U times An.
Shear lag is a consideration where the tensile force in the member is applied eccentrically or transmitted by connection to some, but not all, of the connection elements; e.g., an angle having a connection to only one leg, or when the connection elements do not lie in a common plane.
In such cases, the tensile force is not uniformly distributed over the net area and the critical net section may not be fully effective.
The reduction factor for shear lag is to be applied when computing the net section fracture resistance at the strength limit state.
Notes: The reduction factor, U, accounts for shear lag effects associated with end connection geometry. The effective net area is therefore equal to U times An. Shear lag is a consideration where the tensile force in the member is applied eccentrically or transmitted by connection to some, but not all of the connection elements; e.g., an angle having a connection to only one leg, or when the connection elements do not lie in a common plane. In such cases, the tensile force is not uniformly distributed over the net area and the critical net section may not be fully effective. The reduction factor for shear lag is to be applied when computing the net section fracture resistance at the strength limit state. The reduction factor is to be taken as 1.0 for components in which force effects are transmitted to all elements, and as specified in AASHTO LRFD Article 6.8.2.2 for all other cases (as described on the following slides).

## Slide 13: Factored Tensile Resistance Reduction Factor for Shear Lag, U
Shear lag does not need to be considered when checking yielding on the gross section.
In the absence of more refined analysis or tests, the reduction factor for shear lag, U, may be calculated as specified in AASHTO LRFD Table 6.8.2.2-1.
For open cross-section members (i.e., W, M, S, C or HP shapes, tees, and single and double angles), the calculated value of U should not be taken to be less than the ratio of the gross area of the connected element or elements to the member gross area.
Case 1 in AASHTO LRFD Table 6.8.2.2-1 specifies that for members where the tension load is transmitted directly to each of the cross-sectional elements by bolts or welds, U = 1.0 (except as specified in Cases 4, 5, and 6 in AASHTO LRFD Table 6.8.2.2-1).
Notes: Shear lag does not need to be considered when checking yielding on the gross section because the non-uniform tensile stresses over the cross-section tend to be equalized by the yielding.
In the absence of more refined analysis or tests, the reduction factor for shear lag, U, may be calculated as specified in AASHTO LRFD Table 6.8.2.2-1.
AASHTO LRFD Article 6.8.2.2. specifies that for open cross-section members (i.e., W, M, S, C or HP shapes, tees, and single and double angles), the calculated value of U should not be taken to be less than the ratio of the gross area of the connected element or elements to the member gross area. This provision does not apply to closed sections, such as HSS, nor to plates.
Case 1 in AASHTO LRFD Table 6.8.2.2-1 specifies that for members where the tension load is transmitted directly to each of the cross-sectional elements by bolts or welds, U is to be taken equal to 1.0 (except as specified in Cases 4, 5, and 6 in AASHTO LRFD Table 6.8.2.2-1).
The photo shows WT sections used for a cross-frame connection. Because only the flange of the WT is connected, shear lag and the eccentricity of the connection need to be considered.
Photo credit: Russo Structural Services

## Slide 14: Factored Tensile Resistance Reduction Factor for Shear Lag, U
For members, except plates and HSS, where the tension load is transmitted to some but not all of the cross-sectional elements by bolts or longitudinal welds or by longitudinal welds in combination with transverse welds (Case 2 in AASHTO LRFD Table 6.8.2.2-1 – 10th Edition):
where:
= connection eccentricity equal to the perpendicular distance from the connection plane or face of the member to the centroid of the member section resisting the connection force (in.)
L = length of the connection equal to the out-to-out distance between the bolts in the connection parallel to the line of force, or the average length of the longitudinal welds (in.)
Notes: For members, except plates and HSS, where the tension load is transmitted to some but not all of the cross-sectional elements by bolts or longitudinal welds or by longitudinal welds in combination with transverse welds (as specified in Case 2 in AASHTO LRFD Table 6.8.2.2-1 – 10th Edition), U may be calculated from the equation shown on this slide.
In this equation, ′x bar′ is the connection eccentricity taken equal to the perpendicular distance from the connection plane or face of the member to the centroid of the member section resisting the connection force, and L is the length of the connection taken equal to the out-to-out distance between the bolts in the connection parallel to the line of force, or the average length of the longitudinal welds. For members with combinations of longitudinal and transverse welds, the transverse weld does not significantly affect the fracture resistance based on shear lag. The presence of the transverse weld does little to influence the transfer of the tension load into the unattached elements of the cross-section.
Illustrative examples of the distances ′x bar′ and L for single-angle members connected with bolts or welds are shown on the next slide.

## Slide 15: Factored Tensile Resistance Reduction Factor for Shear Lag, U
Illustrative examples of the distances and L for members connected with bolts or welds are shown below for a single-angle member:
Alternatively, to calculate U for bolted connections with 3 or more bolts per line in the direction of loading, Case 7 in AASHTO LRFD Table 6.8.2.2-1 is permitted to be used for W, M, S, and HP shapes, and Case 8 is permitted to be used for single and double angles.
For lateral connection plates, splice plates and gusset plates, U is to be taken equal to 1.0, except as specified in Case 4 in AASHTO LRFD Table 6.8.2.2-1 (AASHTO LRFD Article 6.13.5.2 – 10th Edition).
Use average length of longitudinal welds.
Notes: Illustrative examples of the distances ′x bar′ and L to be used in the equation for U shown on the preceding slide for members connected with bolts or welds are shown on this slide for a single-angle member. Note again that for longitudinal welds with unequal lengths, the average length of the longitudinal welds is to be used for L. Illustrative examples of the calculation of the distance ′x bar′ for other members (i.e., structural tees and built-up members) are given under Case 2 in AASHTO LRFD Table 6.8.2.2-1.
Alternatively, to calculate U for bolted connections with 3 or more bolts per line in the direction of loading, Case 7 in AASHTO LRFD Table 6.8.2.2-1 is permitted to be used for W, M, S, and HP shapes, and Case 8 is permitted to be used for single and double angles. Cases 7 and 8 permit single values of U between 0.60 and 0.90 to be used depending on the number of bolts per line in the direction of loading and other specified conditions. If U is also calculated per Case 2, i.e., using the equation shown on the preceding slide, the larger value of U is permitted to be used. For cases with fewer than 3 bolts per line in the direction of loading, Case 2 is to be used.
AASHTO LRFD Article 6.13.5.2 (10th Edition) specifies that for lateral connection plates, splice plates, and gusset plates, U is to be taken equal to 1.0, except as specified in Case 4 in AASHTO LRFD Table 6.8.2.2-1 (which applies to plates where the tension load is transmitted by longitudinal welds only – 10th Edition).

## Slide 16: Factored Tensile Resistance Block Shear Rupture Resistance
The governing value of the factored tensile resistance, Pr, must not exceed the factored block shear rupture resistance, Rr, of the member determined as specified in AASHTO LRFD Article 6.13.4.
Block shear rupture is to be checked for the web connection of coped beams and for all tension connections, including connection plates, splice plates and gusset plates.
The connection is to be investigated by considering all possible failure planes in the connected elements, including those parallel and perpendicular to the applied forces, and determining the most critical set of planes.
Planes parallel to the applied force are to be considered to resist only shear stresses and planes perpendicular to the applied force are to be considered to resist only tensile stresses.
Notes: The governing value of the factored tensile resistance, Pr, must not exceed the factored block shear rupture resistance, Rr, of the member determined as specified in AASHTO LRFD Article 6.13.4. Block shear rupture is a tearing limit state, which must be investigated at the end connections of the member.
A block shear rupture failure for an angle in tension bolted to a gusset plate is shown in the figure on this slide. In the figure, the tearing failure along the bolt holes occurs along section a-b-c. The tearing or shear rupture resistance on section a-b, plus the tensile yield resistance on section b-c, will result in the total block shear rupture resistance. Note that the failure path is defined by the centerlines of the bolt holes.
AASHTO LRFD Article 6.13.4 specifies that block shear rupture is to be checked for the web connection of coped beams and for all tension connections, including connection plates, splice plates and gusset plates. Tests on coped beams have indicated that a block shear failure can occur around the perimeter of the bolt holes. The block shear rupture mode is not limited to the coped ends of beams, however. Tension member connections are also susceptible, and the block shear rupture mode should also be checked around the periphery of welded connections.
The connection is to be investigated by considering all possible failure planes in the connected elements, including those parallel and perpendicular to the applied forces, and determining the most critical set of planes. Planes parallel to the applied force are to be considered to resist only shear stresses and planes perpendicular to the applied force are to be considered to resist only tensile stresses. Block shear rupture is most likely to control in the design of bolted end connections to thin webs of girders (e.g., coped beams) and in the design of short compact bolted connections. It is unlikely to control in the design of bolted flange and web splices of typical proportions.

## Slide 17: Factored Tensile Resistance Block Shear Rupture Resistance
The factored block shear rupture resistance, Rr, is taken as (AASHTO LRFD Article 6.13.4):
where:
bs = resistance factor for block shear rupture as specified in AASHTO LRFD Article 6.5.4.2 (= 0.80)
Avg = gross area along the plane resisting shear stress (in.2)
Avn = net area along the plane resisting shear stress (ksi)
Atn = net area along the plane resisting tensile stress (kips)
Ubs = reduction factor for block shear rupture resistance taken equal to 0.50 when the tension stress is non-uniform and 1.0 when the tension stress is uniform
Notes: AASHTO LRFD Article 6.13.4 specifies that the factored block shear rupture resistance, Rr, at the strength limit state be given by the equation shown on this slide. In determining Rr, the resistance to rupture along the shear plane is added to the resistance to rupture on the tensile plane, as given by the parenthetical term on the left side of the equation. Avn is the net area along the plane resisting shear stress and Atn is the net area along the plane resisting tensile stress. Each plane is again defined by the centerlines of the bolt holes. The reduction factor, Ubs, has been included in the equation to approximate the effect of a non-uniform stress distribution on the tensile plane in certain cases; e.g., coped beam connections with multiple rows of bolts. In such cases, the tensile stress on the end plane is non-uniform because the rows of bolts nearest the beam end pick up most of the shear. For the majority of connections encountered in steel bridges, Ubs will equal 1.0. The terms Rp and Fu were defined previously on Slide 8 in this lesson. bs is the resistance factor for block shear rupture as specified in AASHTO LRFD Article 6.5.4.2 (= 0.80).
Block shear rupture is a rupture or tearing phenomenon and not a yielding phenomenon. However, gross yielding along the shear plane can occur when tearing on the tensile plane commences if 0.58FuAvn exceeds 0.58FyAvg, where Avg is the gross area along the plane resisting shear stress. Therefore, the parenthetical term on the right side of the equation limits 0.58FuAvn to not exceed 0.58FyAvg.
In determining the net area of cuts carrying shear stress, the full effective diameter of staggered holes centered within two hole diameters of the cut is to be deducted; holes further removed are to be disregarded. In determining the net area of cuts carrying tension stress, the effect of staggered holes adjacent to the cuts is to be determined using the s2/4g correction discussed on Slide 10 in this lesson.

## Slide 18: Factored Tensile Resistance Example 1
Determine the factored tensile resistance, Pr, at the strength limit state of the single-angle bracing member
(L6 x 4 x ½) shown in the figure.
All bolts are 7/8-inch diameter ASTM F3125 Grade 325 high-strength bolts placed in standard holes assumed for design to be punched full size.
From AASHTO LRFD Table 6.4.1-1, the specified minimum tensile strength, Fu, for ASTM A709 Grade 50 steel is 65 ksi.
Fy = 50 ksi (ASTM A709 Grade 50)
Notes: To illustrate the application of the provisions discussed on the preceding slides, in this example (Example 1), the factored tensile resistance, Pr, at the strength limit state of the single-angle bracing member (L6 x 4 x ½) shown in the figure on this slide will be determined. The cross-sectional area of the member is 4.75 in.2 and the specified minimum yield strength of the member, Fy, is 50 ksi. The bolts in the end connection to the gusset plate are 7/8-inch diameter ASTM F3125 Grade 325 high-strength bolts placed in standard holes assumed for design to be punched full size. The bolt holes are staggered in this case at a longitudinal spacing, s, of 3.0 inches and with a gage distance between the bolt lines, g, of 2.75 inches (refer to Detail A in the figure). The center of gravity of the single-angle member is located at a distance, ′x bar′, of 0.987 inches from the connection plane. From AASHTO LRFD Table 6.4.1-1, the specified minimum tensile strength, Fu, for ASTM 709 Grade 50 steel is 65 ksi.

## Slide 19: Factored Tensile Resistance Example 1 - cont.
The factored tensile resistance for yielding on the gross section is taken as :
The factored tensile resistance for fracture on the net section is taken as :
(Slide 7)
(Slide 8)
(Slide 14)
Rp = 0.90 (punched holes)
Fu = 65 ksi
Notes: Using the equation shown previously on Slide 7 of this lesson, the factored tensile resistance, Pr, for yielding on the gross section is computed to be 225.6 kips.
The factored tensile resistance, Pr, for fracture on the net section is computed from the equation shown previously on Slide 8 of this lesson. The reduction factor for shear lag, U, is computed from the equation shown previously on Slide 14 of this lesson (refer also to Case 2 in AASHTO LRFD Table 6.8.2.2-1). Substituting the distance, ′x bar′ equal to 0.987 inches, and the length of the connection, L, taken equal to the out-to-out distance between the bolts in the connection parallel to the line of force equal to 21.0 inches (refer to the figure on the preceding slide), gives U equal to 0.95. As stated previously on Slide 13 of this lesson, for open-section members, the calculated value of U should not be taken to be less than the ratio of the gross area of the connected element (i.e., the longer leg of the angle in this case) to the member gross area. This ratio is computed to be 0.63, which is less than the calculated value of 0.95. The calculated value of U is also larger than the alternative value of 0.80, which is permitted for single-angle members with 4 or more bolts per line in the direction of loading (refer to Case 8 in AASHTO LRFD Table 6.8.2.2-1). Therefore, a U value of 0.95 will be used.
The reduction factor, Rp, is taken equal to 0.90 for holes punched full size (Slide 8), and the specified minimum tensile strength, Fu, was given on the preceding slide as 65 ksi.

## Slide 20: Factored Tensile Resistance Example 1 - cont.
Calculate the net area, An (Slide 10):
Notes: Calculate the net area of the member, An, for the staggered hole configuration in the end connection using the equation given previously on Slide 10 of this lesson. For the calculation of the net area, the width of each standard bolt hole is taken as the nominal diameter of the hole (Slide 9). For a 7/8-inch diameter bolt, the maximum hole size of a standard hole is 15/16 inches. The smallest net width is to be determined for each chain of holes extending across a member or element along any transverse, diagonal, or zigzag line (Slide 10). In this case, two chains will be investigated; i.e., Chain 1-1 and Chain 2-2. Both chains are assumed to act in conjunction with the full factored tensile force, Pu. Chain 1-1 has one hole and no stagger; An is computed to be 4.28 in.2 Chain 2-2 has 2 holes along the stagger and therefore the s2/4g correction must be made as shown. The net area is computed to be 4.22 in.2, which governs.

## Slide 21: Factored Tensile Resistance Example 1 - cont.
Therefore:
The factored block shear rupture resistance, Rr, is taken as:
(Slide 17)
(Slide 19)
Notes: Substituting in the values of Fu, An, Rp, and U from the preceding two slides gives a factored tensile resistance for fracture on the net section, Pr, of 187.6 kips. This value is less than the factored tensile resistance for yielding on the gross section of 225.6 kips (computed previously on Slide 19). Therefore, fracture on the net section controls and Pr equals 187.6 kips.
This governing value of Pr must not exceed the factored block shear rupture resistance of the end connection, Rr, given by the equation shown in the middle of this slide (refer to Slide 17). Assume the block shear failure planes shown at the bottom of this slide. The failure planes are assumed to pass through the centerlines of the holes.

## Slide 22: Factored Tensile Resistance Example 1 - cont.
Calculate the net area along the plane resisting the tensile stress, Atn:
Calculate the net area along the plane resisting the shear stress, Avn:
Calculate the gross are along the plane resisting the shear stress, Avg:
Notes: To calculate the block shear rupture resistance, first calculate the net area along the plane resisting the tensile stress, Atn. This failure plane is defined by the vertical plane on the right-hand side of the connection passing through the centerline of the two outermost staggered bolt holes in the figure (i.e., the plane perpendicular to the tensile force); therefore, the s2/4g correction must be considered (Slide 10). The net area is equal to the angle leg thickness of 0.5 inches times the width of the plane passing through the centerline of the two staggered holes, which is equal to the gage distance of 2.75 inches plus the edge distance of 1.25 inches minus the width of 1.5 standard bolt holes (i.e., 1.5 times 0.9375 inches) plus the s2/4g correction, which is equal to 1.71 in.2
Next, calculate the net area along the plane resisting the shear stress, Avn. This failure plane is defined by the horizontal plane passing through the centerline of the top row of bolt holes in the figure (i.e., the plane parallel to the tensile force). As specified in AASHTO LRFD Article 6.13.4, since the staggered holes in the bottom row adjacent to the failure plane (or cut) are centered more than two holes diameters from the cut (i.e., 2.75 inches > 2(0.9375) = 1.875 inches), the full effective diameter of these holes need not be deducted in determining Avn. The net area is therefore equal to the angle leg thickness of 0.5 inches times the width of the plane passing through the centerline of the top row of bolt holes, which is equal to the end distance to the first hole of 1.5 + 3.0 = 4.5 inches plus 6 staggered spaces at 3.0 inches minus the width of 3.5 standard bolt holes (i.e., 3.5 times 0.9375 inches), which is equal to 9.61 in.2
Finally, calculate the gross area along the plane resisting the shear stress, Avg, which is equal to the angle leg thickness of 0.5 inches times the end distance to the first hole of 4.5 inches plus 6 staggered spaces at 3.0 inches, or 11.25 in.2

## Slide 23: Factored Tensile Resistance Example 1 - cont.
Therefore, the factored block shear rupture resistance, Rr, is taken as:
Ubs = 1.0 (uniform tensile stress)
Rr = 315 kips > Pr = 187.6 kips (Slide 21)
Pr = 187.6 kips
Notes: The areas on the preceding slide will now be substituted into the equation shown at the top of the slide for the factored block shear rupture resistance, Rr. The reduction factor, Ubs, in the equation is taken equal to 1.0 since the tensile stress is uniform in this case. The term on the left-hand side of the equation is equal to 341 kips, and the term on the right-hand side of the equation is equal to 315 kips. Therefore, gross yielding along the shear plane controls in this case, and Rr is equal to 315 kips.
The factored block shear rupture resistance, Rr, exceeds the governing factored tensile resistance, Pr = 187.6 kips (Slide 21), which in this case is based on fracture on the net section. Therefore, the factored tensile resistance, Pr, is equal to 187.6 kips.
As will be discussed later in this lesson, the effects of the combined flexure and axial force due to the eccentricity of the loading acting on a single-angle bracing member subject to tension are accounted for in determining the factored tensile resistance of the member at the strength limit state through the use of the reduction factor for shear lag, U.

## Slide 24: Factored Tensile Resistance Example 2
Determine the factored tensile resistance, Pr, at the strength limit state of the gusset plate shown in the figure.
All bolts are 7/8-inch diameter ASTM F3125 Grade 325 high-strength bolts placed in standard holes that are assumed for design to be punched full size.
From AASHTO LRFD Table 6.4.1-1, the specified minimum tensile strength, Fu, for ASTM A709 Grade 50W steel is 70 ksi.
Fy = 50 ksi (ASTM A709 Grade 50W)
gusset plate
Notes: In this example (Example 2), the factored tensile resistance, Pr, at the strength limit state of the 5/8” x 17” gusset plate shown in the figure on this slide will be determined. The specified minimum yield strength of the gusset plate, Fy, is 50 ksi. The bolts in the gusset plate are 7/8-inch diameter ASTM F3125 Grade 325 high-strength bolts placed in standard holes that are assumed for design to be punched full size. The bolt holes are staggered in this case at a longitudinal spacing, s, of 3.0 inches and with a gage distance between the bolt lines, g, of 3.5 inches. From AASHTO LRFD Table 6.4.1-1, the specified minimum tensile strength, Fu, for ASTM 709 Grade 50W steel is 70 ksi.

## Slide 25: Factored Tensile Resistance Example 2 - cont.
The factored tensile resistance for yielding on the gross section is taken as :
The factored tensile resistance for fracture on the net section is taken as :
(Slide 7)
(Slide 8)
(Slide 15)
Rp = 0.90 (punched holes)
Fu = 70 ksi
U = 1.0
Notes: Using the equation shown previously on Slide 7 of this lesson, the factored tensile resistance, Pr, for yielding on the gross section is computed to be 504.7 kips.
The factored tensile resistance, Pr, for fracture on the net section is computed from the equation shown previously on Slide 8 of this lesson. It will be assumed in this example that the connection plate to which the gusset plate is attached has adequate net area and does not control the net section fracture resistance. For gusset plates, the reduction factor for shear lag, U, is taken equal to 1.0 (Slide 15) since the tension load is transmitted directly to each of the cross-sectional elements (i.e., the gusset plate and connection plate) by the bolts.
The reduction factor, Rp, is taken equal to 0.90 for holes punched full size (Slide 8), and the specified minimum tensile strength, Fu, was given on the preceding slide as 70 ksi.

## Slide 26: Factored Tensile Resistance Example 2 - cont.
Calculate the net area, An (Slides 10 and 11):
Chain 1-3-1:
Chain 1-2-3-2-1:
Chain 1-2-2-1:
(governs)
gusset plate
Notes: Calculate the net area of the gusset plate, An, for the staggered hole configuration using the equations given previously on Slides 10 and 11 of this lesson. For the calculation of the net area, the width of each standard bolt hole is taken as the nominal diameter of the hole (Slide 9). For a 7/8-inch diameter bolt, the maximum hole size of a standard hole is 15/16 inches. The smallest net width is to be determined for each chain of holes extending across a member or element along any transverse, diagonal, or zigzag line (Slide 10). The total number of bolts in the connection is equal to 10.
In this case, three chains will be investigated; i.e., Chain 1-3-1, Chain 1-2-3-2-1, and Chain 1-2-2-1. Chain 1-3-1 and Chain 1-2-3-2-1 are assumed to act in conjunction with the full factored tensile force, T. Therefore, the equation for An shown on Slide 10 will be used. Chain 1-3-1 has 3 holes and no stagger; An is computed to be 8.87 in.2 Chain 1-2-3-2-1 has 5 holes along the stagger and therefore the s2/4g correction must be made four times as shown. The net area is computed to be 9.30 in.2 Chain 1-2-2-1 has 4 holes along the stagger. In this case, the s2/4g correction must be made two times as shown. Chain 1-2-2-1 is also considered to act in conjunction with a reduced force of 0.9T since one bolt (at Location 3) has transferred its share of the load prior to reaching Chain 1-2-2-1. Therefore, using the equation for An shown on Slide 11, with ntotal equal to 10 and nr equal to 9, gives An equal to 10.09 in.2 As a result, Chain 1-1 controls and the minimum An is equal to 8.87 in2.

## Slide 27: Factored Tensile Resistance Example 2 - cont.
For gusset plates in tension, the net area of the plate, An, is not to be taken as greater than 85 percent of the gross area of the plate (AASHTO LRFD Article 6.13.5.2 – Slide 9).
Therefore:
Separate computations similar to those shown in Example 1 show that the factored block shear rupture resistance, Rr, does not control.
(Slide 25)
Pr = 447.0 kips
Notes: As discussed previously on Slide 9 of this lesson, AASHTO LRFD Article 6.13.5.2 specifies that for gusset plates in tension, the net area of the plate, An, is not to be taken as greater than 85 percent of the gross area of the plate. 85 percent of the gross area of the gusset plate is calculated to be 9.03 in.2, which exceeds the calculated minimum net area, An, of the plate equal to 8.87 in.2
Therefore, substituting in the values of Fu, An, Rp, and U from the preceding two slides gives a factored tensile resistance for fracture on the net section, Pr, of 447.0 kips. This value is less than the factored tensile resistance for yielding on the gross section of 504.7 kips (computed previously on Slide 25). Therefore, fracture on the net section controls and Pr equals 447.0 kips.
This governing value of Pr must not exceed the factored block shear rupture resistance of the connection, Rr.. Separate computations similar to those shown previously in Example 1 in this lesson show that the factored block shear rupture resistance does not control. Therefore, the factored tensile resistance, Pr, is equal to 447.0 kips.

## Slide 28: TENSION MEMBERS limiting slenderness ratios
Notes: The next topic in this lesson will review the specified limiting slenderness ratios for tension members.

## Slide 29: Limiting Slenderness Ratios
The following limiting slenderness ratios, /r, apply for members subject to tension only, other than rods, eyebars, cables, and plates, and for evaluating the tension slenderness of compression members subject to stress reversal (AASHTO LRFD Article 6.8.4):
  For primary members:
  For secondary members:
where:
 = unbraced length (in.)
r = radius of gyration (in.)
Notes: AASHTO LRFD Article 6.8.4 specifies limiting slenderness ratios, /r, for tension members other than rods, eyebars, cables, and plates, and for evaluating the tension slenderness of compression members subject to stress reversal, where  is the unbraced length and r is the minimum radius of gyration for the cross-section. The slenderness limits are not intended to ensure the structural integrity of tension members, but to ensure a minimum degree of stiffness to reduce the potential for undesirable lateral movements or vibrations of the members. The resistance of tension members is not affected by out-of-straightness within reasonable tolerances as the applied tension tends to reduce the out-of-straightness, whereas out-of-straightness tends to be amplified by applied compression.
For primary tension members, the maximum /r is limited to 200. In the AASHTO LRFD Specifications, a primary member is defined as a steel member or component that transmits gravity loads through a necessary as-designed load path. These members are therefore subjected to more stringent fabrication and testing requirements. For secondary members (i.e., a steel member or component that does not transmit gravity loads through a necessary as-designed load path), the maximum /r is limited to 240. Primary and secondary members are identified in AASHTO LRFD Table 6.6.2.1-1. Note that for single angles, the radius of gyration about the z-axis, rz, typically produces the maximum /r.
For evaluating the compression slenderness of tension members subject to stress reversal, the provisions of AASHTO LRFD Article 6.9.3 apply (Slide 66).

## Slide 30: TENSION MEMBERS Combined loading
Notes: The next topic in this lesson will discuss the AASHTO LRFD design provisions for combined loading on tension members; i.e., loading consisting of any combination of axial tension, uniaxial or biaxial flexure, and flexural and/or torsional shear.

## Slide 31: Combined Loading
AASHTO LRFD Article 6.8.2.3 addresses the strength interaction for any combination of axial tension, uniaxial or biaxial flexure, and flexural and/or torsional shear, including combinations where one or more of the individual actions may be zero.
The effect of the moment due to the eccentricities in the connection in angle members and light structural tee members loaded eccentrically in axial tension may be ignored in the design of the member and the connections; the effect of the connection eccentricity is instead addressed through the use of the reduction factor for shear lag, U (AASHTO LRFD Articles C6.8.2.2 and C6.8.2.3.3).
For other members, strength interaction equations address axial tension in combination with uniaxial or biaxial bending and other loading effects.
The interaction equations reduce to the factored tensile resistance in the limit of pure axial loading (with zero flexure), or to the factored flexural resistance about a single principal axis (with zero axial load).
Notes: AASHTO LRFD Article 6.8.2.3 addresses the strength interaction for combined loading consisting of any combination of axial tension, uniaxial or biaxial flexure, and flexural and/or torsional shear, including combinations where one or more of the individual actions may be zero. For members subject to combined axial tension plus uniaxial flexure, these provisions should only be applied if the factored axial force, Pu, exceeds 5 percent of the factored tensile resistance for yielding on the gross section, Pry, of the member (AASHTO LRFD Articles C6.10.6.1 and C6.12.1.2.2).
AASHTO LRFD Articles C6.8.2.2 and C6.8.2.3.3 state that the effect of the moment due to the eccentricities in the connection in angle members and light structural tee members loaded eccentrically in axial tension may be ignored in the design of the member and the connections; the effect of the connection eccentricity is instead addressed through the use of the reduction factor for shear lag, U (discussed previously on Slides 12 through 15 of this lesson). The flexibility of these members and their connections will often allow the member to deform such that the resulting eccentricity is relieved to a considerable extent. Symmetry of the applied tensile load at each end connection of the member can also help to restrain the end rotations of the member. The reduction factor for shear lag, U, can indirectly account for the effects of the eccentricity of the loading in these members. If in the judgment of the Engineer, it is felt that the relative connection and member stiffness is such that the effect of the eccentricity should be considered at the strength limit state, particularly for heavier tee members and double-angle bracing members which typically have larger eccentricities, the interaction equations discussed below may be conservatively applied.
For other members, strength interaction equations address axial tension in combination with uniaxial or biaxial bending and other loading effects. The interaction equations reduce to the factored tensile resistance in the limit of pure axial loading (with zero flexure), or to the factored flexural resistance about a single principal axis (with zero axial load). These interaction equations will be discussed on the next few slides.

## Slide 32: Combined Loading
where:
Pu = maximum factored tensile axial force along the member (kips)
Pry = factored tensile resistance for yielding on the gross section (kips) (Slide 7)
Mux, Muy = factored moments about the x- and y-axes, respectively (kip-in.)
Mrx, Mry = factored flexural resistance about the x- and y-axes, respectively, excluding tension flange rupture (kip-in.)
Eq. 6.8.2.3.1-1
Eq. 6.8.2.3.1-2
Notes: The two equations on this slide represent the stability and overall strength interaction effects for uniaxial or biaxial bending combined with axial tension and general yielding under axial tension and flexure, which may be employed for all types of members (AASHTO LRFD Article 6.8.2.3.1). The accompanying figure on this slide shows the shape of this strength envelope. All ratios are to be taken as positive in the application of these equations. The maximum envelope values of Pu/Pry, Mux/Mrx and Muy/Mry from all relevant load combinations may be combined conservatively to achieve practical member strength evaluations.
When Mrx is influenced by lateral–torsional buckling (Lesson 8), Mux/Mrx depends on the overall length effects associated with the lateral–torsional buckling strength limit state. Therefore, in this case, the two interaction equations are not cross-section resistance checks. Hence, the largest value of Mux/Mrx associated with the unbraced length relevant to the lateral–torsional buckling resistance should be considered along with the other cross-section-based values of Muy/Mry and Pu/Pry. When Mrx is governed by a limit state other than lateral–torsional buckling, all the resistance terms in the two interaction equations are cross-section-based, and therefore, these equations may be evaluated on a cross-section-by-cross-section basis along the member length. Refer to AASHTO LRFD Article C6.9.2.2.1 for a more detailed discussion of when cross-section- by-cross-section based evaluation of strength interaction equations is and is not appropriate, and for a discussion of the application of these equations to nonprismatic members.
For information on computing the factored flexural resistance, Mrx, for sections where the nominal flexural resistance about the major axis of the section is expressed in terms of stress, or where the nominal flexural resistance about the major axis of the section is determined according to the provisions of AASHTO LRFD Appendix A6 (Lesson 8), refer to AASHTO LRFD Article 6.9.2.2.1. For I- and H-shaped sections, the nominal flexural resistance about an axis parallel to the web is determined according to the provisions of AASHTO LRFD Article 6.12.2.2.1.

## Slide 33: Combined Loading
where:
Mrxpe, Mrype = f times the plastic moment about the x- and y-axes, respectively, neglecting any web longitudinal stiffeners (Lesson 6) (kip-in.)
Mrxc, Mryc = factored flexural resistance about the x- and y-axes, respectively, considering compression buckling. For I-section members, Mryc = Mry (kip-in.)
Alternatively, for noncomposite I- and box-section members, the following relationships may be employed in combination
Eq. 6.8.2.3.1-3
Eq. 6.8.2.3.1-4
Notes: AASHTO LRFD Article 6.8.2.3.1 provides an alternative set of strength interaction equations for combined axial tension and flexure on noncomposite I- and box-section members that approximates the negligible to beneficial effect of axial tension on the flexural resistances associated with compression buckling. Therefore, the unity check value from the compression-buckling based strength interaction equation, Eq. 6.8.2.3.1-4, need not consider the influence of the axial tension. The two equations may be applied in combination in lieu of the equations shown on the preceding slide. The strength interaction curve defined by these two equations is shown on this slide. The ratios is both equations are again all taken as positive.
Eq. 6.8.2.3.1-4 limits the flexural resistances to a linear interaction between the factored flexural resistances about the x- and y-axes, M­rxc and Mryc, which consider compression buckling. The flexural resistance is not reduced below that associated with Eq. 6.8.2.3.1-4 until a linear interaction between the yield load in tension, Pry, and the corresponding plastic moments about the x- and y-axes, Mrxpe or Mrype, is reached according to Eq. 6.8.2.3.1-3. For noncomposite box sections, the plastic moments are to be calculated based on the effective compression flange area. The computation of the effective compression flange area is discussed later in this lesson (Slides 57 through 62).
When Eq. 6.8.2.3.1-3 is employed, all the resistance terms are cross-section based, and therefore, this equation may be checked on a cross-section-by-cross-section basis along the length. However, when Eq. 6.8.2.3.1-4 is employed and Mrxc is influenced by lateral–torsional buckling, the largest value of Mux/Mrxc associated with the length relevant to the lateral–torsional buckling resistance should be considered along with the other cross-section-based values of Muy/Mryc along this length.

## Slide 34: Combined Loading
where:
Pu = maximum factored axial force at the cross section under consideration, positive in tension and negative in compression (kips)
Pr = for cross sections subjected to axial tension, factored tensile resistance for fracture on the net section (Slide 8); for cross sections subjected to axial compression, factored tensile resistance for yielding on the gross section (Slide 7) (kips)
Tension Rupture under Axial Tension or Compression Combined with Flexure (AASHTO LRFD Article 6.8.2.3.3) – to be checked at:
  Cross sections containing bolt holes in one or more flanges that are subjected to tension under combined axial tension or compression and flexure;
  Cross sections subjected to axial tension and flexure and containing bolt holes in other cross-section elements, or;
  Cross sections at welded connections subjected to axial tension and flexure.
Eq. 6.8.2.3.3-1
Mu = factored moment about the principal axis of bending under consideration at the cross section under consideration; positive for tension and negative for compression in the cross-section element under consideration (kip-in.)
Mr = see next slide
Notes: Eq. 6.8.2.3.3-1 addresses the strength interaction between flexure and axial tension or compression pertaining to tension rupture at the locations listed. These locations include: 1) cross-sections containing bolt holes in one or more flanges that are subjected to tension under combined axial tension or compression and flexure; 2) cross sections subjected to axial tension and flexure and containing bolt holes in other cross-section elements; or 3) cross sections at welded connections subjected to axial tension and flexure.
This equation focuses on the specific axial force, tension or compression, combined with the specific moment at the cross section under consideration. The axial strength ratio term is negative in Eq. 6.8.2.3.3-1, causing a beneficial subtractive effect, when the cross section having the bolt holes is subjected to axial compression. The axial strength ratio term is positive, causing an additive effect, when the cross section is subjected to axial tension. The terms Pu, Pr, and Mu in the equation are calculated as defined on this slide. The calculation of the term, Mr, is covered on the next slide.

## Slide 35: Combined Loading
where:
Mr = factored tension rupture flexural resistance about the axis of bending under consideration (kip-in.)
Anf = net area of the tension flange; for sections not containing a flange loaded in flexural tension, and for sections at welded connections, Anf /Agf shall be taken equal to 1.0 (in.2)
Agf = gross area of the tension flange; for sections not containing a flange loaded in flexural tension, and for sections at welded connections, Anf /Agf shall be taken equal to 1.0 (in.2)
Fu = specified minimum tensile strength determined as specified in AASHTO LRFD Table 6.4.1-1 of the cross-section element under consideration (ksi)
Fyt = specified minimum yield strength of the cross-section element under consideration (ksi)
St = minimum elastic section modulus of the gross cross section about the axis of bending under consideration (in.3)
Tension Rupture under Axial Tension or Compression Combined with Flexure (AASHTO LRFD Article 6.8.2.3.3) – cont.:
Eq. 6.8.2.3.3-2
Notes: Eq. 6.8.2.3.3-2 on this slide is for the calculation of the term, Mr, in the interaction equation on the preceding slide. Mr is the factored tension rupture flexural resistance about the axis of bending under consideration. This equation is based on the equation given in AASHTO LRFD Article 6.10.1.8 for the handling of tension flanges with holes in flexural members (refer to Slide 112 in Lesson 6). The variable St in this equation is conservatively taken as the minimum elastic section modulus of the gross cross section about the axis of bending under consideration.

## Slide 36: Combined Loading
Interaction with Torsional and/or Flexural Shear (AASHTO LRFD Article 6.8.2.3.2):
  For noncomposite rectangular box-section members, including square and rectangular HSS, and for noncomposite circular tubes, including round HSS, subjected to torsion where fcv/TFcv > 0.2, the factored torsional shear stress shall be considered in the interaction equations.
  For general members, including those specified above, where Pu/Pr > 0.05, the factored flexural shear stresses shall be considered in the interaction equations.
  Pr shall be multiplied by:
  Mrx shall be multiplied by:
  Mry shall be multiplied by:
where:
T = resistance factor for torsion specified in AASHTO LRFD Article 6.5.4.2 (= 1.0)
fve = total factored shear stress due to torsion and/or flexure, as applicable, calculated in a cross-section element (ksi)
Fcv = nominal shear resistance of a cross-section element (ksi)
Notes: AASHTO LRFD Article 6.8.2.3.2 addresses the interaction with torsional and/or flexural shear, as applicable, on the resistance of noncomposite rectangular box-section members, including square and rectangular HSS and noncomposite circular tubes, including round HSS. In addition, it addresses the interaction between the flexural shear resistance and the axial resistance of I-section members. I-section members with thin webs, subjected to significant axial force, potentially have a measurable interaction between their flexural shear and axial load resistances. The interaction between torsional and/or flexural shear stresses in I-section member flanges with other member resistances is neglected. The cross-section shear stresses due to torsion are also neglected in I-section members.
Where the consideration of both the torsional and flexural shear stresses is required, the torsional and flexural shear stresses are to be summed based on their corresponding directions in each of the plate elements of the cross section given the internal loadings. Further discussion and illustration of this for different member cross-section types is provided in AASHTO LRFD Article C6.9.2.2.2. Where either of the exclusion conditions shown on this slide is met, the corresponding contribution to the shear stress is to be taken as zero. Otherwise, the terms in the base interaction equations shown on the preceding slides are to be multiplied by the respective Δ values shown on this slide, as applicable, in lieu of a more refined analysis. The calculation and application of the Δ values for different member cross-section types, along with the definition and calculation of the various terms given in the Δ equations, is discussed further in AASHTO LRFD Articles 6.8.2.3.2 and C6.9.2.2.2.
For further discussion and more detailed background on these interaction equations, refer to Section 6.6 of Chapter 4 of the NSBA Steel Bridge Design Handbook.

## Slide 37: TENSION MEMBERS Built-up members
Notes: The last topic on tension members in this lesson will cover the AASHTO LRFD design provisions for built-up tension members.

## Slide 38: Built-up Tension Members
Built-up tension members typically consist of two or more steel shapes, either:
  Closely spaced shapes (e.g., angles or channels) interconnected at intervals using welds or bolts/rivets or by intermittent bolted/riveted or welded filler/stay plates; or
  Widely spaced shapes or plates connected by lacing (i.e., flat bars, angles, channels, or other shapes), tie plates (also referred to as batten or stay plates), solid plates, or perforated cover plates (Slide 5). Solid plates and perforated plates are most commonly used in modern steel bridges; lacing and tie plates are now less commonly used.
Welded connections between the plates and shapes of built-up tension members must be continuous, and bolted connections between the shapes and plates must satisfy the provisions of AASHTO LRFD Article 6.13.2, including the applicable bolt spacing requirements (Lesson 11).
Notes: As discussed previously on Slide 5 in this lesson, built-up tension members typically consist of two or more steel shapes, either: 1) closely spaced shapes (e.g., angles or channels) interconnected at intervals by intermittent bolted/riveted or welded filler/stay plates, or 2) widely spaced shapes or plates connected by lacing (i.e., flat bars, angles, channels, or other shapes), tie plates (also referred to as batten or stay plates), solid plates, or perforated cover plates. Illustrations of perforated cover plates, batten plates and lacing were shown previously on Slide 5 in this lesson. Solid plates and perforated cover plates are most commonly used to connect widely spaced shapes or plates in modern steel bridges; lacing and tie plates are now less commonly used. AASHTO LRFD Article C6.8.5.1 contains references where some limiting design proportions for batten plates and lacing bars may be found. AASHTO LRFD Article C6.9.4.3.1 also gives a reference for determining section properties (e.g., the moment of inertia and torsional constant) of latticed built-up members. Special design requirements for members composed of perforated plates in built-up tension members are discussed on the next slide.
The design of built-up tension members is covered in AASHTO LRFD Article 6.8.5. AASHTO LRFD Article 6.8.5.1 specifies that welded connections between the plates and shapes of built-up tension members must be continuous, and bolted connections between the shapes and plates must satisfy the provisions of AASHTO LRFD Article 6.13.2, including the applicable bolt spacing requirements (i.e., minimum and maximum spacing, clear distance, sealing, and stitch requirements), which were discussed previously in Lesson 11. Built-up tension members should also satisfy the appropriate maximum slenderness ratio limit discussed previously on Slide 29 of this lesson.
The photo shows solid as well as laced built-up truss members.
Photo credit: Russo Structural Services

## Slide 39: Built-up Tension Members
Requirements for perforated plates (AASHTO LRFD Article 6.8.5.2):
The ratio of the length of the holes in the direction of stress to the width of the holes is not to exceed 2.0;
The clear distance between the holes in the direction of stress is not to be less than the transverse distance between the nearest line of connection bolts or welds;
The clear distance between the end of the plate and the first hole is not to be less than 1.25 times the transverse distance between the bolts or welds;
The periphery of the holes is to have a minimum radius of 1.5 in.;
The unsupported widths at the edges of the holes may be assumed to contribute to the net area of the member, and;
Where the holes are staggered in opposite perforated plates, the net area of the member is to be considered the same as for a section having holes in the same transverse plane.
Notes: Specific design requirements for perforated plates in built-up members are specified in AASHTO LRFD Article 6.8.5.2. Those requirements are listed on this slide.
Built-up truss members with perforated flanges (usually called cover plates in older designs) are shown.
Photo credit: Michael Baker International

## Slide 40: Compression MEMBERS INTRODUCTION
Notes: The first topic in this lesson on compression members will be an introduction to the different types of compression members that are typically utilized in steel-bridge structures.

## Slide 41: Typical Compression Members
Single & double angles
Rolled W, M, S, or HP shapes
Structural tees
Rectangular & round HSS and noncomposite box sections
Built-up sections
Pipe Sections
Concrete-Encased Shapes
Composite Concrete-Filled Steel Tubes (CFSTs)
Internal reinforcement if present
Concrete-Filled Tubes
Concrete infill
Notes: Compression members are members subject to axial compression and also occur commonly in steel-bridge structures as chord and diagonal members in a truss, as arch ribs, as bracing members; e.g., cross-frame and lateral bracing members in beam and girder bridges, and as columns and piles in substructures. The design of compression members is covered in AASHTO LRFD Article 6.9.
Typical cross-sections of compression members are shown on this slide. Compression members may consist of a single structural shape, or they may be built-up from several structural shapes. Structural shapes used as compression members include rolled W, M, S, or HP shapes, single and double angles, structural tees, channels (not shown), and rectangular and round Hollow Structural Sections (HSS). Noncomposite box sections and pipe sections can also serve as compression members.
Compression members can be either noncomposite or composite. Composite compression members include concrete-filled tubes, concrete-encased shapes, and composite concrete-filled steel tubes (CFSTs), as shown at the bottom of this slide. This course will focus on the design of noncomposite compression members only; the design of composite compression members will not be covered. Design provisions for composite compression members, including CFSTs, are provided in AASHTO LRFD Articles 6.9.5, 6.9.6, and 6.12.2.3. The design of arch ribs and piles will also not be covered in this course; design provisions for arch ribs and for piles are provided in AASHTO LRFD Articles 6.14.4 and 6.15, respectively.
Built-up compression members are similar to the built-up tension members discussed previously on Slide 5 of this lesson. General requirements for built-up compression members are similar but somewhat more stringent than those for built-up tension members of the same type and will be covered later in this lesson.

## Slide 42: Compression MEMBERS Factored Compressive resistance
Notes: The next topic in this lesson will cover the computation of the factored compressive resistance of compression members using the AASHTO LRFD provisions, including the calculation of the nominal compressive resistance, Pn, the elastic critical buckling resistance, Pe, used in the computation of Pn, the effective length factor, K, and the effects of potential local buckling of slender cross-section elements on the overall compressive resistance of the member.

## Slide 43: Factored Compressive Resistance
The factored compressive resistance is taken as (AASHTO LRFD Article 6.9.2.1):
where:
c = resistance factor for axial compression as specified in AASHTO LRFD Article 6.5.4.2 (= 0.95 for noncomposite compression members and 0.90 for composite compression members)
Pn = nominal compressive resistance determined as specified in AASHTO LRFD Article 6.9.4 or 6.9.5, as applicable (kips)
Notes: AASHTO LRFD Article 6.9.2.1 specifies that the factored compressive resistance, Pr, at the strength limit state for members subject to axial compression is to be taken as the nominal compressive resistance, Pn, determined as specified in AASHTO LRFD Article 6.9.4 or 6.9.5, as applicable, times the resistance factor for axial compression, c, equal to 0.95 for noncomposite members and 0.90 for composite members (AASHTO LRFD Article 6.5.4.2). The determination of Pn for noncomposite compression members is covered in AASHTO LRFD Article 6.9.4, and the determination of Pn for composite compression members is covered in AASHTO LRFD Article 6.9.5. As mentioned previously, this course will focus on the design of noncomposite compression members only; the design of composite compression members will not be covered.
Note that arches must also satisfy the requirements of AASHTO LRFD Article 6.14.4, and compression chords of half-through trusses must also satisfy the requirements of AASHTO LRFD Article 6.14.2.9. These requirements also are not covered in this course.
The main tower for the Benjamin Franklin suspension bridge is shown. This is an example of a large built-up box section.
Photo credit: Russo Structural Services

## Slide 44: Factored Compressive Resistance Nominal Compressive Resistance, Pn
The nominal compressive resistance, Pn, is to be taken as the smallest value based on the applicable modes of flexural buckling, torsional buckling, and flexural–torsional buckling (AASHTO LRFD Article 6.9.4.1.1).
Applicable buckling modes for doubly symmetric open-section compression members:
  Flexural Buckling (FB)
  about the x- or y-axis
  Torsional Buckling (TB)
    If Kzz > Kyy
Section A-A
P
P
Notes: AASHTO LRFD Article 6.9.4.1.1 specifies that the nominal compressive resistance of noncomposite compression members, Pn, is to be taken as the smallest value based on the applicable modes of flexural buckling, torsional buckling, and flexural-torsional buckling. AASHTO LRFD Table 6.9.4.1.1-1 is a helpful selection table for the determination of the applicable buckling modes that need to be checked for different cross-section types.
Applicable buckling modes for doubly symmetric open-section compression members (e.g., I-sections and cruciform sections) are flexural buckling (FB) and torsional buckling (TB). Concentrically loaded doubly symmetric open-section compression members may buckle flexurally in the x- or y-directions or may buckle torsionally by pure twisting (torsion) about the z-axis about the member shear center, as shown in the figures on the right-hand side of this slide. These buckling modes are independent, and the member will buckle in the lowest of the loads associated with each of these three modes. Torsional buckling need only be checked if the effective length for torsional buckling, Kzz, is significantly larger than the effective length for y-axis flexural buckling, Kyy. Each of these buckling modes will be discussed further on subsequent slides in this lesson.

## Slide 45: Factored Compressive Resistance Nominal Compressive Resistance, Pn
Applicable buckling modes for singly symmetric open-section compression members (with the y-axis defined as the axis of symmetry):
  Flexural Buckling (FB)
  about the x-axis
  Flexural Torsional Buckling (FTB)
y
x
Notes: Applicable buckling modes for singly symmetric open-section compression members in which the y-axis is defined as the axis of symmetry of the cross section (e.g., channels, singly symmetric I-sections, tee sections, and double-angle sections with and without separators) are flexural buckling (FB) and flexural-torsional buckling (FTB). Concentrically loaded singly symmetric open-section compression members may buckle flexurally in the y-direction (i.e., about the x-axis) or may buckle in a flexural-torsional mode by twisting (torsion) combined with flexure in the x-direction (i.e., about the y-axis) without a change in shape, as shown in the figures on the right-hand side of this slide. In these cases, the centroid (denoted by ‘G’ for the channel section in the lower right-hand figure) and shear center (denoted by ‘C’ in the same figure) of the cross-section do not coincide. Note that since the y-axis is defined as the axis of symmetry for FTB, the y-axis for the channel for FTB is actually taken as the x-axis of the cross-section in the figure (i.e., the axis of symmetry). These buckling modes are independent, and the member will buckle in the lowest of the loads associated with each of these two modes. The flexural-torsional buckling mode will also be discussed further on a subsequent slide.

## Slide 46: Factored Compressive Resistance Nominal Compressive Resistance, Pn
Applicable buckling mode for unsymmetric open-section compression members (except for single-angle members):
  Flexural Torsional Buckling (FTB)
Applicable buckling mode for closed-section compression members:
Flexural Buckling (FB)
Notes: The applicable buckling mode for unsymmetric open-section compression members with no cross-section axis of symmetry is flexural-torsional buckling (FTB), except for single-angle members, which are to be designed according to the provisions of AASHTO LRFD Article 6.9.4.4 for flexural buckling (FB) only utilizing a so-called “effective slenderness ratio”, (KL/r)eff. The effective slenderness ratio and the special design provisions for single-angle members in AASHTO LRFD Article 6.9.4.4 will be discussed later in this lesson. All other concentrically loaded unsymmetric open-section compression members may buckle in a flexural-torsional mode by twisting (torsion) combined with flexure in both the x- and y-directions.
The applicable buckling mode for closed-section compression members is flexural buckling (FB). Because of the large St. Venant torsional stiffness (Lesson 6), torsional buckling (TB) and flexural–torsional buckling (FTB) need not be considered for closed sections, including built-up members connected by lacing bars, batten plates, solid plates, perforated plates, or any combination thereof.

## Slide 47: Factored Compressive Resistance Flexural Buckling (FB) Resistance, Pe
In lieu of an alternative buckling analysis, the elastic critical buckling resistance, Pe, based on flexural buckling (FB) is to be taken as (AASHTO LRFD Article 6.9.4.1.2):
Eq. 6.9.4.1.2-1
where:
Ag = gross cross-sectional area of the member (in.2)
K = effective length factor in the plane of buckling determined as specified in AASHTO LRFD Article 4.6.2.5
 = unbraced length in the plane of buckling (in.)
rs = radius of gyration about the axis normal to the plane of buckling (in.)
Notes: Flexural buckling of concentrically loaded compression members refers to a buckling mode in which the member deflects laterally without twist or a change in the cross-sectional shape. Flexural buckling involves lateral displacements of the member cross sections in the direction perpendicular to the x- or y-axes that are resisted by the flexural rigidities, EIx or EIy, of the member, respectively.
In lieu of an alternative buckling analysis, Eq. 6.9.4.1.2-1 in AASHTO LRFD Article 6.9.4.1.2 should be used to calculate the elastic critical flexural buckling resistances about the x- and y-axes (in units of kips). The equation is the classical elastic Euler buckling stress for a concentrically loaded pin-ended compression member times the gross cross-sectional area of the member, Ag. For doubly symmetric open-section compression members, the smaller value about the x- or y-axis should be taken as Pe for use in computing the nominal compressive resistance of the member, Pn, as will be discussed later in this lesson.
In the equation, the slenderness (K/rs) is computed using the effective length factor, K, the unbraced length, , in the plane of buckling, and the radius of gyration, rs = (I/Ag)1/2, about the axis normal to the plane of buckling. I is the cross-sectional moment of inertia about the axis normal to the plane of buckling. The effective length factor, K, is determined as specified in AASHTO LRFD Article 4.6.2.5, and is discussed further on the next slide.
The buckling of a 30-ft tall HP12 x 53 section is shown as an example of flexural buckling of an I-shaped section. An eigenvalue buckling analysis using a commercial software program predicts the capacity as 280 kips. Because the column has pinned ends, and the same unbraced length for both flexural axes, it buckles about the weak Y-Y axis.

## Slide 48: Factored Compressive Resistance Effective Length Factor, K
The effective length factor, K, accounts for the influence of end conditions. K represents the ratio of the idealized pinned-end compression member length to the actual length of a member with other than pinned ends (AASHTO LRFD Article 4.6.2.5).
Recommended values in the braced plane of trusses and frames where lateral stability is provided:
For bolted or welded end connections at both ends: K = 0.750
For pinned connections at both ends: K = 0.875
For single angles, regardless of end connection:
K = 1.0
Notes: The effective length factor, K, which is applied to the actual member unbraced length, , accounts for the influence of end conditions. K is used to compensate for translational and rotational boundary conditions. K represents the ratio of the idealized pinned-end compression member length to the actual length of a member with other than pinned ends. In many cases, some degree of end restraint exists causing an effective length factor other than 1.0. AASHTO LRFD Table C4.6.2.5-1 (shown on this slide) provides theoretical K values taken from the Structural Stability Research Council (SSRC) Guide for idealized end conditions in which translational and/or rotational end conditions are either fully restrained or free. Because actual member end conditions are seldom perfectly fixed or perfectly unrestrained as represented by the ideal conditions, the table also provides recommended design values as suggested by the SSRC. These simple modifications of the ideal values lead to either equal or somewhat higher K values.
In the absence of refined inelastic analysis, AASHTO LRFD Article 4.6.2.5 provides recommended K values in the braced plane of triangulated trusses, trusses, and frames where lateral stability is provided by diagonal bracing or other suitable means, which are shown on the right-hand side of this slide adjacent to the table. A conservative K value of 1.0 is suggested for single angles since these members are often loaded through only one leg and are subject to eccentric loading as well as twist. Caution should be exercised in applying these recommended values to cases with larger unbraced lengths where elastic buckling may control. SSRC recommends the use of K = 0.85 for in-plane buckling of web members in bridge trusses. This is because the position of live load that produces the maximum force in a given web member typically causes less than the maximum force in the adjacent members. Therefore, the adjacent members are able to provide some rotational restraint.
In many situations where rotational restraint exists at the ends of a single bridge column or at the ends of the columns in a bridge frame, e.g., pier columns integral with bridge girders, the traditional sidesway inhibited or sidesway uninhibited alignment charts given in AASHTO LRFD Article C4.6.2.5 provide acceptable solutions for K. However, it is essential to recognize that the alignment charts are based on idealized assumptions that in certain cases are invalid. The commentary to Appendix 7 of the AISC Specification discusses these assumptions in detail and provides a number of modifications to the alignment chart procedures that extend their range of applicability. Article C4.6.2.5 gives closed-form equations that provide a close fit to the base sidesway inhibited and sidesway uninhibited alignment charts. The AISC modifications also must be applied in general in the use of these equations. Refer to NSBA SBDH Chapter 4 for a discussion on recommended K values for arches.
The influence of boundary conditions on buckling strength is shown. The same column from the preceding slide (left figure) is modeled with fixed-fixed conditions at the top and bottom (right figure). The buckling capacity is increased to 1110 kips, 4 times greater than the pin-end condition. Since the effective length has been halved, the buckling strength is increased by a factor of 4.

## Slide 49: Factored Compressive Resistance Torsional Buckling (TB) Resistance, Pe
In lieu of an alternative buckling analysis, the elastic critical buckling resistance, Pe, based on torsional buckling (TB) is to be taken as (AASHTO LRFD Article 6.9.4.1.3):
Eq. 6.9.4.1.3-1
where:
Ag = gross cross-sectional area of the member (in.2)
Cw = warping torsional constant (in.6)
G = elastic shear modulus of steel = 0.385E (ksi)
Ix, Iy = moments of inertia about the major & minor principal axes of the cross-section (in.4)
J = St. Venant torsional constant (in.4)
Kzz = effective length for torsional buckling (in.)
Notes: The limit state of torsional buckling, or pure twisting of the member about the shear center, applies only to concentrically loaded open-section doubly symmetric compression members for which the locations of the centroid and shear center coincide (Slide 44). For such members, in lieu of an alternative buckling analysis, the elastic critical torsional buckling (TB) resistance, Pe, is computed from the equation shown on this slide (AASHTO LRFD Eq. 6.9.4.1.3-1).
Torsional buckling will rarely control and need not be considered for doubly symmetric I-section members satisfying the cross-section proportion limits specified in AASHTO LRFD Article 6.10.2 (Lesson 2), unless the effective length for torsional buckling is significantly larger than the effective length for y-axis flexural buckling; that is, if the member is braced but is not sufficiently restrained against twisting at a number of its brace points. The effective length for torsional buckling, Kzℓz, is typically taken as the length between locations where the member is prevented from twisting. That is, in many cases, Kzℓz can be taken conservatively as 1.0ℓz. For a cantilever member fully restrained against twisting and warping at one end with the other end free, Kzℓz should be taken as 2ℓ where ℓ is the length of the member. For a member with twisting and warping restrained at both ends, Kzℓz may be taken as 0.5ℓ.
For a doubly symmetric I‑section, the warping torsional constant, Cw, may be taken as Iyh2/4, where h is the distance between flange centroids, in lieu of a more precise analysis. For a cruciform section, Cw is equal to zero. For closed sections, Cw may be taken equal to zero and GJ is relatively large. Because of the large GJ, torsional buckling need not be considered for closed sections, including built-up members connected by lacing bars, batten plates, solid plates, perforated plates, or any combination thereof.

## Slide 50: Factored Compressive Resistance Flexural-Torsional Buckling (FTB) Resistance, Pe
In lieu of an alternative buckling analysis, the elastic critical buckling resistance, Pe, based on flexural-torsional buckling (FTB) for open-section singly symmetric members where y is the axis of symmetry of the cross-section is to be taken as (AASHTO LRFD Article 6.9.4.1.3):
Eq. 6.9.4.1.3-2
where:
H =
Pez =
Pey = elastic flexural buckling resistance about the y-axis (Slide 47) (kips)
yo = distance along the y-axis between the shear center and centroid of the cross-section (in.)
Notes: The limit state of flexural-torsional buckling of concentrically loaded open-section compression members refers to a buckling mode in which the member twists and bends simultaneously without a change in the shape of the cross-section. In such cases, the shear center and centroid of the cross-section do not coincide, and the torsional rigidity of the section is relatively low. For open-section members composed of singly symmetric cross-sections where the y-axis is defined as the axis of symmetry of the cross-section (e.g., tees and double angles), in lieu of an alternative buckling analysis, the elastic critical flexural-torsional buckling (FTB) resistance, Pe, may be computed from the equation shown on this slide (AASHTO LRFD Eq. 6.9.4.1.3-2).
As buckling occurs, the axial load has a lateral component resulting from the deflection of the member. The torsional moment caused by this lateral component of axial force acting about the shear center of the section causes twisting of the member. The degree of interaction between the torsional and flexural deformations determines the amount of reduction of the buckling load in comparison to the flexural buckling load. As the distance between the centroid and shear center increases, the twisting tendency increases and the flexural-torsional buckling load decreases. The critical elastic flexural-torsional buckling resistance for open-section singly symmetric members, is always smaller than the critical elastic flexural buckling resistance about the y-axis, Pey (Slide 47). Therefore, for these members, only the elastic flexural buckling resistance about the x-axis, Pex, need be considered along with the elastic flexural-torsional buckling resistance in determining the governing nominal compressive resistance, Pn.
Values of J, ro, and H for rolled tee sections are tabulated in the Ninth Edition AISC Manual of Steel Construction, or more recently in AISC Design Guide 9 Torsional Analysis of Structural Steel Members. ro is the polar radius of gyration (in units of inches). H is a unitless flexural constant. The warping torsional constant, Cw, is to conservatively be taken as zero for tees and double angles. The y-axis is again defined as the axis of symmetry of the cross-section in the equations on this slide. Therefore, for a single channel section, the y-axis would actually be taken as the x-axis of the cross-section (or the axis of symmetry of the channel section) in calculating the preceding values. For a single channel section, refer to AASHTO LRFD Eq. 6.12.2.2.5-6 for the computation of Cw. For singly-symmetric I-sections with equal flange widths (i.e., differing flange thicknesses), flexural-torsional buckling does not need to be considered as long as 0.67  tf1/tf2 1.5, where tf1 and tf2 are the flange thicknesses, and Kzz  Kyy. However, it is recommended that flexural-torsional buckling always be checked for singly symmetric I-sections with differing flange widths that are loaded in axial compression. The warping torsional constant, Cw, for such sections (with equal flange thicknesses) may be computed using AASHTO LRFD Eq. C6.9.4.1.3-1 in lieu of a more precise analysis.
Buckling of an angle loaded through its centroid is illustrated on this slide.

## Slide 51: Factored Compressive Resistance Flexural-Torsional Buckling (FTB) Resistance, Pe
In lieu of an alternative buckling analysis, the elastic critical buckling resistance, Pe, based on flexural-torsional buckling (FTB) for open-section unsymmetric members (except for single angles) is to be taken as the lowest root of the following cubic equation (AASHTO LRFD Article 6.9.4.1.3):
Eq. 6.9.4.1.3-3
where:
Pez =
Pex, Pey = elastic flexural buckling resistances about the x- and y-axes (Slide 47) (kips)
xo, yo = distances along the x- and y-axes between the shear center and centroid of the cross-section (in.)
Notes: Compression members composed of open unsymmetric cross sections, or members with no cross-section axis of symmetry, fail by torsion combined with flexure about the x- and y-axes. Again, in such cases, the centroid and shear center of the cross section do not coincide. For unsymmetric open-section members, or members with no cross-section axis of symmetry (except for single angles designed according to the provisions of AASHTO LRFD Article 6.9.4.4 – to be discussed later on in this lesson), the failure mode always involves torsion combined with flexure about both the x- and y-axes (i.e., flexural buckling need not be considered). In this case, in lieu of an alternative buckling analysis, the elastic critical flexural-torsional buckling resistance, Pe, may be computed as the lowest root of the cubic equation shown on this slide (AASHTO LRFD Eq. 6.9.4.1.3-3).

## Slide 52: Factored Compressive Resistance Nominal Compressive Resistance, Pn
For compression members with cross sections composed only of nonslender longitudinally unstiffened elements satisfying the width-to-thickness or slenderness ratio limits specified in AASHTO LRFD Article 6.9.4.2.1, Pn is to be determined as (AASHTO LRFD Article 6.9.4.1.1):
If , then:
Otherwise:
Eq. 6.9.4.1.1-1
where:
Fy = specified minimum yield strength (ksi)
Pe = elastic critical buckling resistance for FB, TB, or FTB (Slides 47-51), as applicable (kips)
Po = nominal yield resistance = FyAg (kips)
Eq. 6.9.4.1.1-2
Notes: The AASHTO LRFD BDS uses the single column-curve equations shown on this slide to characterize the nominal compressive resistance, Pn, of compression members with cross sections composed only of nonslender longitudinally unstiffened elements satisfying the width-to-thickness or slenderness ratio limits specified in AASHTO LRFD Article 6.9.4.2.1 subject to concentrically-applied axial compression. Nonslender and slender elements will be discussed on subsequent slides in this lesson. Pe is the smallest value of the elastic critical buckling resistance based on the applicable modes of flexural buckling (FB), torsional buckling (TB), and flexural–torsional buckling (FTB) (refer to Slides 47 through 51 in this lesson). The nominal yield resistance, Po, is the effective cross-section or stub-column yield load; that is, the column resistance in the limit of zero length (i.e., K = 0). For a homogeneous prismatic steel member in which none of the cross-section plates are classified as slender, Po is the full yield resistance given as FyAg. For nonhomogeneous cross-section members, Fy may conservatively be taken as the smallest specified minimum yield strength of all the cross-section elements for the calculation of Po. Subsequent slides in this lesson with discuss the computation of Pn for members where some or all of the cross-section elements are classified as slender. For nonprismatic members, refer to Chapter 4 of NSBA SBDH.
The equations are written in terms of the critical elastic buckling resistance, Pe, and the equivalent nominal yield resistance, Po, to facilitate the calculation of the nominal resistance for members subject to buckling modes in addition to, or other than, flexural buckling. Also, this form of the resistance equations may be used to conveniently calculate Pn when a refined buckling analysis is employed to assess the stability of trusses, frames or arches in lieu of utilizing an effective length factor approach. In such cases, Pe in Eqs. 6.9.4.1.1-1 and 6.9.4.1.1-2 would be taken as the axial load in a given member taken from the analysis at incipient elastic buckling of the structure or subassemblage.
Further discussion on the background of these column-curve equations is provided on the next slide.

## Slide 53: Factored Compressive Resistance Nominal Compressive Resistance, Pn
6.9.4.1.1-1
6.9.4.1.1-2
Notes: The AASHTO LRFD BDS column-curve Eqs. 6.9.4.1.1-1 and 6.9.4.1.1-2 shown on the preceding slide account in a broad fashion for the influence of residual stresses and geometric imperfections (i.e., out-of-straightness and out-of-plumbness) on the column resistance. They provide a close fit to SSRC column curve 2P (refer to the graph on this slide), which is based on a mean initial out-of-straightness of 1/1470 of the equivalent simply supported column length, KL. The AASHTO LRFD BDS column curve was modified slightly to reflect an out-of-straightness criterion of L/1500. Eqs. 6.9.4.1.1-1 and 6.9.4.1.1-2 represent the nominal inelastic and elastic column buckling resistances respectively, as illustrated in the graph on this slide plotted in terms of the ratio of Pn/Po vs. KL/r.
Generally, there are significant differences in the mean column resistances depending on the column type. This is evidenced by the differences between SSRC curves 1P, 2P and 3P in the graph. The normalized column resistances are larger on average for lightweight sections, larger yield strengths, and buckling about the major-axis of bending for I-shapes. They tend to be smaller for heavy sections, low yield strengths, and buckling about the minor-axis of bending for I-shapes. Column curve 1P represents the data band of highest resistance, included hot- and cold-formed heat-treated HSS columns. Column curve 3P represents the data band of lowest resistance and applies only to heavy W-shapes with Fy < 50 ksi and welded H-shapes built-up from universal mill plate with Fy < 50 ksi for major-axis buckling and Fy < 60 ksi for minor-axis buckling. Column curve 2P represents the largest group of columns. Welded built-up shapes are no longer manufactured from universal mill plates; furthermore, the minimum yield strength is usually 50 ksi or larger in new construction. Therefore, the resistances of all practical columns in new construction are best fit by column curves 1P and 2P, with 2P being the appropriate curve for most column types.

## Slide 54: Factored Compressive Resistance Effects of Local Buckling on Pn
Nonslender Cross-Section Element―a longitudinally unstiffened plate element within the cross-section of a member having a slenderness small enough such that the element is able to develop its full nominal yield strength in uniform axial compression without any reduction due to local buckling.
where:
λr = corresponding width-to-thickness or slenderness ratio limit as specified in AASHTO LRFD Table 6.9.4.2.1-1
b = element width as specified in AASHTO LRFD Table 6.9.4.2.1-1 (in.)
t = element thickness (in.); for flanges of rolled channels, use the average thickness. For HSS, refer to AASHTO LRFD Article 6.12.1.2.4
Eq. 6.9.4.2.1-1
Local buckling
Notes: Compression members with cross sections composed only of nonslender longitudinally unstiffened plate elements, i.e., cross sections without any longitudinal stiffeners in which all the component elements of the cross-section satisfy the corresponding width-to-thickness or slenderness ratio limits (i.e., b/t ≤ λr), are able to develop their full yield strength under uniform axial compression without any significant impact from local buckling of the elements (AASHTO LRFD Article 6.9.4.2.1).
The corresponding width-to-thickness or slenderness ratio limits, λr, are specified in AASHTO LRFD Table 6.9.4.2.1-1 (refer to the next slide). The appropriate element width, b, to be used for each case is also specified in AASHTO LRFD Table 6.9.4.2.1-1. t is the element thickness. For flanges of rolled channels, t is to be taken as the average thickness. For HSS, the provisions of AASHTO LRFD Article 6.12.1.2.4 apply.
It is important to note that under uniform compression, cross-section elements are classified as either slender or nonslender in the AASHTO LRFD BDS. Compactness requirements apply only when determining the nominal resistance of flexural members for which compression flange and web elements may need to withstand larger inelastic strains to ensure that local buckling does not adversely affect the nominal flexural resistance (Lesson 8).
For compression members composed only of nonslender longitudinally unstiffened elements, the equations shown previously on Slide 52 of this lesson apply for determining the nominal compressive resistance, Pn.

## Slide 55: Factored Compressive Resistance Effects of Local Buckling on Pn
Notes: This slide shows the values of λr and b given in AASHTO LRFD Table 6.9.4.2.1-1 to be used in the equation shown on the preceding slide to determine whether elements supported along one longitudinal edge are nonslender. Examples of elements supported along one longitudinal edge are highlighted on this slide with red arrows for a single-angle section and for a tee section.
The value of the flange local buckling coefficient, kc, to be used in determining the value of λr for flanges of welded and nonwelded built-up I-sections and for plates and angle legs projecting from built-up I-sections (i.e., the third row in the table on the left-hand side of this slide) is given by Eqs. 6.9.4.2.1-2 and 6.9.4.2.1-3 shown in the table on the right-hand side of this slide. This expression accounts for the fact that thinner webs in built-up sections tend to offer less rotational restraint to prevent flange local buckling. The calculated value of kc from Eq. 6.9.4.2.1-2 must fall between the range of 0.35 and 0.76 (Eq. 6.9.4.2.1-3). The lower-bound value of 0.35 (which controls at D/tw values greater than approximately 130) is back-calculated by equating the local buckling resistances given in the AASHTO LRFD BDS to measured resistances from tests with D/tw values ranging from 72 to 245. The fact that the lower-bound value is less than kc = 0.425 (which assumes idealized simply-supported boundary conditions along the web-flange juncture) is indicative of the fact that web local buckling in more slender webs tends to destabilize the compression flange. The upper-bound value of 0.76 corresponds to the traditional value that has been assumed for rolled shapes. Substituting a kc value of 0.76 into the value of λr given in the third row of the table gives the value of λr for rolled shapes given in the second row of the table. Implicit values of kc for the other cases in this table are given in Table 5 of NSBA SBDH Chapter 4 ( Section 6.2.4.2).

## Slide 56: Factored Compressive Resistance Effects of Local Buckling on Pn
Notes: The remainder of AASHTO LRFD Table 6.9.4.2.1-1 is shown on this slide giving values of λr and b for elements supported along two longitudinal edges, and also for other elements; namely, circular tubes and round HSS.

## Slide 57: Factored Compressive Resistance Effects of Local Buckling on Pn
Slender Cross-Section Element―a longitudinally unstiffened plate element within the cross-section of a member having a slenderness large enough such that nominal local buckling of the element may occur and may have an impact on its resistance in uniform axial compression prior to developing its full nominal yield strength.
  For compression members with cross sections containing any slender cross-section elements, the nominal compressive resistance, Pn, is to be determined according to the provisions of AASHTO LRFD Article 6.9.4.2.2.
  For compression members with cross sections containing any longitudinally stiffened plates, Pn is to be determined according to the provisions of AASHTO LRFD Article E6.1.1 (Appendix E6).
Eq. 6.9.4.2.1-1
Notes: For compression members with cross sections containing any slender cross-section elements, i.e., cross sections containing one or more longitudinally unstiffened elements not satisfying the corresponding width-to-thickness or slenderness ratio limits specified in AASHTO LRFD Article 6.9.4.2.1 (i.e., b/t > λr), the nominal compressive resistance, Pn, is instead to be determined according to the provisions of AASHTO LRFD Article 6.9.4.2.2 to account for the effect of potential local buckling of those elements on the overall buckling resistance of the member. These provisions will be discussed on subsequent slides in this lesson. For compression members with cross sections containing any longitudinally stiffened plates, Pn is to be determined according to the provisions of AASHTO LRFD Article E6.1.1 (Appendix E6) to account for the action of the longitudinal stiffeners and their tributary plate widths acting as stiffener struts including any local buckling effects in slender longitudinally stiffened plate panels. These provisions are considered outside the scope of this course. In both of the above cases, the same potential column-buckling modes and corresponding values of Pe given in AASHTO LRFD Table 6.9.4.1.1-1 (and discussed previously in this lesson) are to be considered in the computation of Pn. Flowcharts illustrating the application of the provisions of AASHTO LRFD Article 6.9.4 for determining the compressive resistance of noncomposite I- or box-section members, with or without longitudinally stiffened plates, are provided in AASHTO LRFD Article C6.5.1 (Appendix C6).
The need for consideration of local buckling of slender plate elements and the need for consideration of longitudinal stiffeners and their tributary plate width acting as stiffener struts as well as the potential local buckling of the individual stiffened plate panels is avoided by using longitudinally unstiffened plates satisfying the requirement of Eq. 6.9.4.2.1-1. In some cases, however, it may be more economical to use members having one or more slender plates in which the strength is reduced due to local buckling effects. For instance, rolled wide-flange sections with ratios of d/bf  1.7, where d is the section depth and bf is the flange width, typically have slender webs for uniform axial compression. Webs of welded I- and box sections also typically are classified as slender elements for axial compression. The stems of a significant number of rolled T-sections and one or both legs of many rolled angle sections are also classified as slender elements. Furthermore, a large number of square or rectangular HSS profiles have slender wall elements. AASHTO LRFD Article CE6.1.3 discusses cases where it may or may not be beneficial to consider longitudinal stiffening of cross-section plate elements.

## Slide 58: Factored Compressive Resistance Effects of Local Buckling on Pn
For compression members with cross sections composed of one or more slender longitudinally unstiffened elements not satisfying the width-to-thickness or slenderness ratio limits specified in AASHTO LRFD Article 6.9.4.2.1, Pn is to be determined as (AASHTO LRFD Article 6.9.4.2.2a):
where:
Fcr = Eq. 6.9.4.2.2a-2
Pcr = nominal compressive resistance of the member calculated from Eq. 6.9.4.1.1-1 or 6.9.4.1.1-2, as applicable, using Ag (Slide 52) (kips)
Ag = total gross cross-sectional area of the member (in.2)
Aeff = effective area of the cross-section (Next Slide) (in.2)
Eq. 6.9.4.2.2a-1
Notes: For compression members containing one or more slender longitudinally unstiffened cross-section elements (i.e., elements not satisfying the width-to-thickness or slenderness ratio limits specified in AASHTO LRFD Article 6.9.4.2.1 – Slides 55 and 56), local buckling of the component elements may adversely affect the overall buckling resistance of the member. Hence, the nominal compressive resistance, Pn, based on flexural, torsional, or flexural–torsional buckling, as applicable, may be reduced. For such members, Pn is determined using a generalized form of the so-called “unified effective width/unified effective area approach” (AASHTO LRFD Article 6.9.4.2.2). The unified effective width/unified effective area approach considers the effective width of cross-section plate elements supported along one or two longitudinal edges. This approach provides an accurate characterization of the ultimate strength of all types of slender longitudinally unstiffened plates that recognizes plate postbuckling resistance in all cases.
In this approach, Pn is to be determined using AASHTO LRFD Eq. 6.9.4.2.2a-1, which is shown on this slide. In this equation, Fcr is taken as the nominal compressive resistance, Pcr, calculated from AASHTO LRFD Eq. 6.9.4.1.1-1 or 6.9.4.1.1-2 (Slide 52), as applicable, using the total gross cross-sectional area of the member, Ag, divided by Ag. For nonhomogeneous members, Fy may be taken as the smallest specified yield strength of all the cross-section elements for the calculation of Fcr. The calculated value of Fcr is then multiplied by the effective area of the cross-section, Aeff, to give the nominal compressive resistance of the member, Pn. Aeff is discussed in more detail on the next slide.
The original developments pertaining to the unified effective width method focused on the calculation of member effective cross-section properties, particularly the effective moment of inertia based on plate effective widths, Ie, in the calculation of the column buckling stress. This type of procedure required iteration, since the effective widths are a function of the applied stresses. However, in the context of column flexural buckling, it was observed that the variation in the effective radius of gyration relative to the radius of gyration based on the gross cross-section properties was relatively minor. Similar observations were made with regard to other modes of failure under uniform axial compression. Therefore, it was found that the axial compressive resistance of members containing slender elements could be calculated accordingly, and non-iteratively, by using the gross cross-section properties to determine the column strength in terms of the axial stress, Fcr, and by applying this stress to the effective area of the member cross section, Aeff.

## Slide 59: Factored Compressive Resistance Effects of Local Buckling on Pn
The effective area of the cross-section, Aeff, is to be taken as the summation of the effective areas of the cross-section elements determined as follows:
  Otherwise:
where:
= summation over all longitudinally unstiffened cross-section plate elements
= summation over all the corner areas of a noncomposite box-section member
Ac = gross cross-sectional area of the corner pieces of a noncomposite box-section member (in.2)
b = width of the element under consideration (AASHTO LRFD Table 6.9.4.2.1-1) (in.)
be = effective width of the element under consideration determined as specified in AASHTO LRFD Article 6.9.4.2.2b for slender elements (refer to subsequent slides), and taken equal to b for nonslender elements (in.)
Eq. 6.9.4.2.2a-3
For rolled sections and HSS members containing slender elements:
Eq. 6.9.4.2.2a-4
Notes: Two equations are provided for the cross-section effective area, Aeff, to be used in the unified effective width/unified effective area approach. Aeff is to be taken as the summation of the effective areas of the cross-section elements determined using either AASHTO LRFD Eq. 6.9.4.2.2a-3 or Eq. 6.9.4.2.2a-4, as shown on this slide. Eq. 6.9.4.2.2a-3 facilitates the inclusion of the fillet areas in rolled-section and square or rectangular HSS members containing any slender elements. Eq. 6.9.4.2.2a-4 addresses general welded and nonwelded built-up sections containing any slender plate elements. The second term of Eq. 6.9.4.2.2a-4 represents the sum of the gross cross-sectional areas of the four corner pieces of a noncomposite box-section member not included in the clear width of the component plates; for all other members, Ac is taken as zero. Flange extensions on box-section members, if present, should be evaluated to determine if they are nonslender or slender elements and included accordingly in Eq. 6.9.4.2.2a-4. For circular tubes and round HSS, Aeff is instead to be determined as specified in AASHTO LRFD Article 6.9.4.2.2c.
b is the width of the element under consideration determined as specified in AASHTO LRFD Table 6.9.4.2.1-1 (Slides 55 and 56). t is the thickness of the element under consideration. For flanges of rolled channels, t is to be taken as the average thickness. For HSS, the provisions of AASHTO LRFD Article 6.12.1.2.4 apply. beff is the effective width of the element under consideration determined as specified in AASHTO LRFD Article 6.9.4.2.2b for slender elements (as discussed on subsequent slides), and taken equal to b for nonslender elements.

## Slide 60: Factored Compressive Resistance Effects of Local Buckling on Pn
both longitudinal edges
one longitudinal edge
both longitudinal edges
one longitudinal edge
Notes: A significant attribute of the stability behavior of plates is that local buckling does not correspond to the maximum compressive resistance. Plates subjected to uniform compressive displacements (i.e., shortening) between rigid frictionless platens will bend out-of-plane after buckling as shown in the top figure on this slide, and will redistribute their longitudinal membrane stresses from uniform compression to those shown in the figure. This occurs regardless of whether the plates are supported on both longitudinal edges or on only one longitudinal edge. The plates continue to support increased loads, although with a reduction in their effective axial stiffness. Furthermore, the line of action of the resultant compressive force will move toward the supported edge in the plate that is supported only on one longitudinal edge.
The analysis of the postbuckling action and the subsequent load capacity of a plate generally requires a sophisticated geometric nonlinear load-deflection solution. A simple approximation for the ultimate strength of plates in which both longitudinal edges are supported transversely was suggested in the early 1930s. It was proposed that the actual stress distribution be replaced by two effective widths of be/2 < b/2 on each side of the plate, each subjected to a uniform stress, f, equal to the actual maximum stress at the edge of the plate, as shown in the bottom left figure on this slide, and where the effective width be is determined such that fbet is equal to the total load supported by the plate. It was also suggested that the above two strips be considered as a rectangular plate of total width be, and that the maximum load capacity of the plate corresponds to when the elastic critical stress of that plate becomes equal to the yield strength of the material, Fy. Although this effective width formulation was originally suggested for plate elements with two transversely supported longitudinal edges, this idealization works satisfactorily for the effective width of a plate having only one transversely supported longitudinal edge as well, as shown in the bottom right figure on this slide.

## Slide 61: Factored Compressive Resistance Effects of Local Buckling on Pn
The effective width, be, of slender elements is to be determined as follows (AASHTO LRFD Article 6.9.4.2.2b):
If , then:
If , then:
Eq. 6.9.4.2.2b-1
where:
c1 = effective width imperfection adjustment factor (AASHTO LRFD Table 6.9.4.2.2b-1) (Next Slide)
c2 = effective width imperfection adjustment factor =
c3 = effective width imperfection adjustment factor (AASHTO LRFD Table 6.9.4.2.2b-1)
Fel = elastic local buckling stress (ksi) =
Eq. 6.9.4.2.2b-2
Notes: This slide shows the equations given in AASHTO LRFD Article 6.9.4.2.2b to compute the effective width, be, for slender elements. Eq. 6.9.4.2.2b-2 is a generalized form of the classical equation for plate local buckling effective widths implemented originally in the AISI cold-formed steel specifications and developed by Winter in 1970. This equation expanded on the original effective width formulation discussed on the preceding slide to account for the effects of geometric imperfections and residual stresses. The original Winter equation has been modified in the AASHTO LRFD BDS through the addition of the effective width imperfection adjustment factors, c1, c2 and c3 (given on the next slide), to generalize the equation to more accurately characterize the plate postbuckling strengths for various categories of slender elements. For further background on this equation and these modifications, refer to the NSBA SBDH Chapter 4 (Section 6.2.4.2).
In the equations on this slide, Fcr is the nominal compressive resistance of the member calculated from AASHTO LRFD Eq. 6.9.4.2.2a-2 (refer to Slide 58). Eqs. 6.9.4.2.2b-1 and 6.9.4.2.2b-2 allow for larger plate effective widths in longer members relative to the values associated with f = Fy due to the smaller values of Fcr. It should be emphasized that the classification of a plate as slender under uniform axial compression indicates that the plate is not able to develop the yield capacity on its gross area due to the influence of local buckling, except as indicated in the next paragraph. When calculating the contribution of longitudinally unstiffened compression flange plates in noncomposite steel box-section flexural members, Fcr is taken equal to the specified minimum yield strength of the compression flange, Fyc, in Eqs. 6.9.4.2.2b-1 and 6.9.4.2.2b-2. The member resistance in these cases is best represented by considering the development of Fy on the effective area of the longitudinally unstiffened plates.
If the stress level at overall member buckling, Fcr, is small enough relative to Fy, a slender cross-section element will not exhibit any significant local buckling effects prior to the member reaching its axial compressive resistance. This behavioral attribute is accounted for by checking the element width-to-thickness ratio, b/t, versus the modified limit . If b/t is less then or equal to this limit, no significant local buckling effects occur prior to the member reaching its axial compressive resistance. In these cases, the effective width of the slender cross-section element is equal to the full element width, b, as specified by Eq. 6.9.4.2.2b-1. In the preceding limit, λr is the corresponding width-to-thickness ratio limit as specified in AASHTO LRFD Table 6.9.4.2.1-1 (Slides 55 and 56).
This slide shows the equations given in AASHTO LRFD Article 6.9.4.2.2b to compute the effective width, be, for slender elements. Eq. 6.9.4.2.2b-2 is a generalized form of the classical equation for plate local buckling effective widths implemented originally in the AISI cold-formed steel specifications and developed by Winter in 1970. This equation expanded on the original effective width formulation discussed on the preceding slide to account for the effects of geometric imperfections and residual stresses. The original Winter equation has been modified in the AASHTO LRFD BDS through the addition of the effective width imperfection adjustment factors, c1, c2 and c3 (given on the next slide), to generalize the equation to more accurately characterize the plate postbuckling strengths for various categories of slender elements. For further background on this equation and these modifications, refer to the NSBA SBDH Chapter 4 (Section 6.2.4.2).
In the equations on this slide, Fcr is the nominal compressive resistance of the member calculated from AASHTO LRFD Eq. 6.9.4.2.2a-2 (refer to Slide 58). Eqs. 6.9.4.2.2b-1 and 6.9.4.2.2b-2 allow for larger plate effective widths in longer members relative to the values associated with f = Fy due to the smaller values of Fcr. It should be emphasized that the classification of a plate as slender under uniform axial compression indicates that the plate is not able to develop the yield capacity on its gross area due to the influence of local buckling, except as indicated in the next paragraph. When calculating the contribution of longitudinally unstiffened compression flange plates in noncomposite steel box-section flexural members, Fcr is taken equal to the specified minimum yield strength of the compression flange, Fyc, in Eqs. 6.9.4.2.2b-1 and 6.9.4.2.2b-2. The member resistance in these cases is best represented by considering the development of Fy on the effective area of the longitudinally unstiffened plates.
If the stress level at overall member buckling, Fcr, is small enough relative to Fy, a slender cross-section element will not exhibit any significant local buckling effects prior to the member reaching its axial compressive resistance. This behavioral attribute is accounted for by checking the element width-to-thickness ratio, b/t, versus the modified limit 𝜆_𝑟= √(𝐹_𝑦∕𝐹_𝑐𝑟 ). If b/t is less then or equal to this limit, no significant local buckling effects occur prior to the member reaching its axial compressive resistance. In these cases, the effective width of the slender cross-section element is equal to the full element width, b, as specified by Eq. 6.9.4.2.2b-1. In the preceding limit, λr is the corresponding width-to-thickness ratio limit as specified in AASHTO LRFD Table 6.9.4.2.1-1 (Slides 55 and 56).

## Slide 62: Factored Compressive Resistance Effects of Local Buckling on Pn
Notes: The effective width imperfection adjustment factors, c1, c2, and c3, to be used in AASHTO LRFD Eq. 6.9.4.2.2b-2 on the preceding slide are given in AASHTO LRFD Table 6.9.4.2.2b-1, which is shown on this slide. For a plate with ideal simply-supported edge conditions, where the theoretical plate local buckling coefficient, kc, is equal to 4.0, the coefficients in Winter’s equation for the plate effective width are c1 = 0.22, c2 = 1.485, and c3 = 0.0. These same coefficients are used for all plates supported along one longitudinal edge.
Table 6.9.4.2.2b-1 specifies c1 = 0.20 for 1) flanges and webs of nonwelded built-up box sections; 2) walls of square and rectangular hot-formed HSS; and 3) nonperforated flange cover plates. Table 6.9.4.2.2b-1 specifies c1 = 0.18 for 1) webs of rolled I- and channel sections; 2) webs of nonwelded built-up I- and channel sections; 3) webs of welded and nonwelded built-up I-sections containing two or more longitudinal stiffeners; and 4) flanges and webs of nonwelded built-up box sections containing two or more longitudinal stiffeners. There appears to be no justification for using the smaller c1 = 0.18 on webs of general built-up I-sections containing flanges with a relatively large b/t. In addition, the table specifies c1 = 0.22 for cold-formed HSS sections, which is consistent with the AISI rules. The c1 value for plates with two or more longitudinal stiffeners provides some recognition of the additional net lateral restraint from adjacent panels (within the plane of the plate) at the multiple longitudinal stiffener locations in these plates. The coefficient c3 = 0.075 for all other plates supported along two longitudinal edges given in the last row of the table shifts Winter’s classical plate effective width curve to reflect the results of a wide range of research studies indicating lower local buckling resistances and postbuckling strengths in members composed of general welded plate assemblies, due to the influence of welding residual stresses.

## Slide 63: Factored Compressive Resistance Effects of Local Buckling on Pn
For all cross-section plate elements supported along two longitudinal edges that are slender, and for slender longitudinally stiffened plate panels as defined in AASHTO LRFD Article E6.1.2, the provisions of AASHTO LRFD Article 6.9.4.5 must also be satisfied. Such panels subjected to longitudinal compressive stress at one or both of their longitudinal edges must satisfy the following at the service limit state and for constructibility:
where:
λ = slenderness, bf/tf, w/tf, or D/tw, of the slender flange or web plate element or longitudinally stiffened plate panel under consideration, as applicable
fc = maximum longitudinal compressive stress (ksi) acting on the gross cross section in the plate element or longitudinally stiffened plate panel under consideration due to the Service II loads or the factored load for constructibility (AASHTO LRFD Article 3.4.2.1)
k = plate buckling coefficient considering any gradient in the longitudinal stress (Next Slide)
Eq. 6.9.4.5-1
Notes: Since significant post-buckling resistance is often assumed at the strength limit state in computing the nominal flexural and axial compressive resistance of members with cross sections containing slender plate elements supported along two longitudinal edges and/or longitudinally stiffened plates supported along their two longitudinal edges and containing slender plate panels, such members must also satisfy the provisions of AASHTO LRFD Article 6.9.4.5 to ensure that theoretical local buckling of those plate elements or panels does not occur at the service limit state and for constructibility (Lesson 7). AASHTO LRFD Eq. 6.9.4.5-1, shown on this slide, is used to check for theoretical local buckling at these limit states under the net combined normal stresses acting on each of these types of plate elements or panels subjected to compressive stress due to the Service II loads or the factored load for constructibility specified in AASHTO LRFD Article 3.4.2.1 (Lesson 7). Refer to AASHTO LRFD 6.9.4.5 for the definitions of bf, D, tf, tw, and w.
This check is not required for plate elements supported only along one longitudinal edge, webs of composite or noncomposite I-section and box-section members that are subject to flexure only (except for noncomposite box-section members with more than one longitudinal stiffener), or for the walls of circular tubes. The slenderness or plate buckling response of these types of elements is typically limited by other design provisions, which may be less restrictive in some cases, and/or the postbuckling response is not considered to be of any negative consequence.
In experimental tests, noticeable plate bending deformations and associated transverse displacements can occur from the onset of load application due to initial plate out-of-flatness. Because of stable plate postbuckling behavior, there is no significant change in the rate of increase of the transverse displacements as the theoretical plate buckling stress is exceeded. Due to unavoidable geometric imperfections, the plate buckling behavior is a load-deflection problem rather than a bifurcation problem. Satisfaction of this requirement to prevent theoretical buckling helps limit the magnitude of the corresponding transverse displacements.
Eq. 6.9.4.5-1 is not checked at the fatigue limit state because the plate buckling check under the Service II loads will tend to control over a similar check under the unfactored permanent load plus the Fatigue I load combination. Shear buckling under the factored load for constructibility and under the unfactored permanent load plus the Fatigue I load combination is checked separately (Lesson 7).

## Slide 64: Factored Compressive Resistance Effects of Local Buckling on Pn
The plate buckling coefficient, k, considering any gradient in the longitudinal stress is computed as (AASHTO LRFD Article 6.9.4.5):
If , then:
If , then:
where:
f1 = smaller longitudinal stress at the longitudinal edges of the plate element or longitudinally stiffened plate panel at the cross-section under consideration; taken as positive in compression and negative in tension (ksi)
f2 = larger longitudinal compressive stress at the longitudinal edges of the plate element or longitudinally stiffened plate panel at the cross-section under consideration; taken as positive (ksi)
If , then:
Eq. 6.9.4.5-2
Eq. 6.9.4.5-3
Eq. 6.9.4.5-4
Notes: The plate-buckling coefficient, k, in the equation on the preceding slide is given by AASHTO LRFD Eqs. 6.9.4.5-2 through 6.9.4.5-4, which are shown on this slide. These equations are taken from the Eurocode. These equations address general loading conditions from any combination of axial compression and bending within the plane of the plates for the evaluation of slender longitudinally unstiffened plates and slender longitudinally stiffened plate panels supported along two longitudinal edges. They are based on the idealization of general plates and plate panels as having simply supported boundary edge conditions. The ratio f1/f2 is less than or equal to 1.0 in all cases, since f1 is the smaller edge stress. The stress f1 may be a smaller compressive value compared to f2, or it may be a tensile stress, in which case f1 is taken as a negative value. The ratio f1/f2 is positive when both f1 and f2 are in compression, and it is negative when f1 is in tension. For unusual cases where the ratio of f1/f2 is smaller than -3, buckling of the plate is unlikely. In this case, it is conservative to use k equal to 96.
A plate-buckling coefficient of k = 4.0 may be employed conservatively in Eq. 6.9.4.5-1 shown on the preceding slide as an initial design check. Web plate elements in noncomposite box-section members subjected predominantly to flexure often may require the larger k values from Eqs. 6.9.4.5-2 through 6.9.4.5-4 to satisfy the requirement of Eq. 6.9.4.5-1.

## Slide 65: COMPRESSION MEMBERS Limiting Slenderness Ratios
Notes: The next topic in this lesson will review the specified limiting slenderness ratios for compression members.

## Slide 66: Limiting Slenderness Ratios
The following limiting slenderness ratios, K/r, apply for members subject to compression only, and for evaluating the compression slenderness of tension members subject to stress reversal (AASHTO LRFD Article 6.9.3):
  For primary members:
  For secondary members:
where:
K = effective length factor specified in AASHTO LRFD Article 4.6.2.5 (Slide 48)
 = unbraced length (in.)
r = radius of gyration (in.)
Notes: AASHTO LRFD Article 6.9.3 specifies limiting slenderness ratios, K/r, for compression members, and for evaluating the compression slenderness of tension members subject to stress reversal, where K is the effective length factor specified in AASHTO LRFD Article 4.6.2.5 (refer to Slide 48 in this lesson),  is the unbraced length, and r is the minimum radius of gyration for the cross-section. In computing the maximum slenderness for checking the appropriate limiting ratio only, AASHTO LRFD Article 6.9.3 permits the radius of gyration to be computed on a notional section that neglects part of the area of a component provided that the resistance of the component based on the actual area and radius of gyration exceeds the factored loads, and the resistance of the notional component based on the reduced area and corresponding radius of gyration also exceeds the factored loads.
For primary compression members, the maximum K/r is limited to 120. In the AASHTO LRFD Specifications, a primary member is defined as a steel member or component that transmits gravity loads through a necessary as-designed load path. These members are therefore subjected to more stringent fabrication and testing requirements. For secondary members (i.e., a steel member or component that does not transmit gravity loads through a necessary as-designed load path), the maximum K/r is limited to 140. Primary and secondary members are identified in AASHTO LRFD Table 6.6.2.1-1. Note that for single angles where the effective slenderness ratio approach described later in this lesson is used to design the angle, the actual maximum slenderness ratio, K/r, should be checked against the appropriate limiting value, rather than the effective slenderness ratio, (K/r)eff. For single angles, the radius of gyration about the z-axis typically produces the maximum K/r.
For evaluating the tension slenderness of compression members subject to stress reversal, the provisions of AASHTO LRFD Article 6.8.4 apply (Slide 29).

## Slide 67: COMPRESSION MEMBERS Combined loading
Notes: The next topic in this lesson will discuss the AASHTO LRFD design provisions for combined loading on compression members; i.e., loading consisting of any combination of axial compression, uniaxial or biaxial flexure, and flexural and/or torsional shear. The discussion includes an example illustrating the application of these provisions to the design of a tee-section top lateral bracing member in a straight tub-girder bridge.

## Slide 68: Combined Loading
AASHTO LRFD Article 6.9.2.2 addresses the strength interaction for any combination of axial compression, uniaxial or biaxial flexure, and flexural and/or torsional shear, including combinations where one or more of the individual actions may be zero.
The effect of the moment due to the eccentricities in single-angle members loaded eccentrically in axial compression may be neglected when these members are evaluated as axially loaded compression members for flexural buckling only using an appropriate specified effective slenderness ratio (AASHTO LRFD Article 6.9.4.4).
The interaction equations reduce to the factored compressive resistance in the limit of pure axial loading (with zero flexure), or to the factored flexural resistance about a single principal axis (with zero axial load).
Interaction with torsional and/or flexural shear is handled in the exact same fashion as discussed previously on Slide 36 (AASHTO LRFD Article 6.9.2.2.2).
Notes: AASHTO LRFD Article 6.9.2.2 addresses the strength interaction for combined loading consisting of any combination of axial compression, uniaxial or biaxial flexure, and flexural and/or torsional shear, including combinations where one or more of the individual actions may be zero. For members subject to combined axial compression plus uniaxial flexure, these provisions should only be applied if the factored axial force, Pu, exceeds 5 percent of the factored compressive resistance, Pr, of the member (AASHTO LRFD Articles C6.10.6.1 and C6.12.1.2.2).
AASHTO LRFD Article 6.9.4.4 permits the effect of the moment due to the eccentricities in single-angle members loaded eccentrically in axial compression to be neglected when these members are evaluated as axially loaded compression members for flexural buckling only using an appropriate specified effective slenderness ratio, The provisions of AASHTO LRFD Article 6.9.4.4 and the effective slenderness ratio will be discussed later in this lesson.
For other members, strength interaction equations address axial compression in combination with uniaxial or biaxial bending and other loading effects. The interaction equations reduce to the factored compressive resistance in the limit of pure axial loading (with zero flexure), or to the factored flexural resistance about a single principal axis (with zero axial load). These interaction equations will be discussed on the next few slides.
Interaction with torsional and/or flexural shear is covered in AASHTO LRFD Article 6.9.2.2.2 and is handled in the exact same fashion as discussed previously on Slide 36 of this lesson, and so it will not be covered further under this topic.

## Slide 69: Combined Loading
where:
Pu = factored axial compressive force (kips)
Pr = factored compressive resistance (kips) (Slide 43)
Mux, Muy = factored moments about the x- and y-axes, respectively (Slides 71 and 72) (kip-in.)
Mrx, Mry = factored flexural resistance about the x- and y-axes, respectively, excluding tension flange rupture (kip-in.)
Eq. 6.9.2.2.1-1
Eq. 6.9.2.2.1-2
For members in which all the cross-section elements are defined as compact for flexure:
r
r
r
Eq. 6.9.2.2.1-1
Eq. 6.9.2.2.1-2
Notes: The two equations on this slide represent the strength interaction effects for uniaxial or biaxial bending combined with axial compression for members in which all the cross-section elements are defined as compact for flexure according to the provisions of AASHTO LRFD Articles A6.2.1, A6.3.2, 6.11.6.2.2, and 6.12.2.2.2c, as applicable (AASHTO LRFD Article 6.9.2.2.1). Members with cross-section elements that are classified as compact for flexure were discussed previously in Lessons 8 and 9. Such members are potentially able to develop significant distributed yielding within their cross sections for small axial load and dominant flexural loading. As such, these types of members are able to develop a “knee” in the interaction curve between their flexural and axial compressive resistances. Members with other cross-section types generally have limited capability to develop such a “knee”. The accompanying figure on this slide shows the shape of this strength envelope. All ratios are to be taken as positive in the application of these equations. The maximum envelope values of Pu/Pr, Mux/Mrx and Muy/Mry from all relevant load combinations may be combined conservatively to achieve practical member strength evaluations. The factored moments about the x- and y-axes, Mux and Muy, for application in the interaction equations presented under this topic are to be computed considering moment magnification, which will be discussed further on Slides 71 and 72 in this lesson.
When Mrx is influenced by lateral–torsional buckling (Lesson 8), Mux/Mrx depends on the overall length effects associated with the lateral–torsional buckling strength limit state. Therefore, in this case, all the interaction equations presented under this topic are not cross-section resistance checks. Hence, the largest value of Mux/Mrx associated with the unbraced length relevant to the lateral–torsional buckling resistance should be considered along with the other cross-section-based values of Muy/Mry and Pu/Pr. When Mrx is governed by a limit state other than lateral–torsional buckling, all the resistance terms in the interaction equations are cross-section based, and therefore, these equations may be evaluated on a cross-section-by-cross-section basis along the member length. Refer to AASHTO LRFD Article C6.9.2.2.1 for a more detailed discussion of when cross-section by cross-section-based evaluation of strength interaction equations is and is not appropriate, and for a discussion of the application of these equations to nonprismatic members.
For information on computing the factored flexural resistance, Mrx, for sections where the nominal flexural resistance about the major axis of the section is expressed in terms of stress, or where the nominal flexural resistance about the major axis of the section is determined according to the provisions of AASHTO LRFD Appendix A6 (Lesson 8), refer to AASHTO LRFD Article 6.9.2.2.1. For I- and H-shaped sections, the nominal flexural resistance about an axis parallel to the web is determined according to the provisions of AASHTO LRFD Article 6.12.2.2.1.

## Slide 70: Combined Loading
Eq. 6.9.2.2.1-3
The following interaction equation may be employed for all types of members:
Tee stems and double-angle web legs in which the tip of the stem or leg is in flexural compression are not considered as compact elements; therefore, Eq. 6.9.2.2.1-3 should be applied in cases where the tip of the tee stem or double-angle web legs are subject to flexural compression.
Tee stems and double angle web legs in which the tip of the stem or leg is in flexural tension are considered as compact elements; thus, Eqs. 6.9.2.2.1-1 and 6.9.2.2.1-2 (Slide 69) may be applied in this case.
Notes: For members where AASHTO LRFD Eqs. 6.9.2.2.1-1 and 6.9.2.2.1-2 shown on the preceding slide apply, the member ultimate resistances tend to involve extensive yielding in both tension and compression. For other member types, the member strength interaction is usually governed by additive compression buckling effects from axial compression and flexure, which are captured accurately to conservatively by the linear interaction Eq. 6.9.2.2.1-3 shown on this slide. This equation may be employed for all types of members.
Tee stems and double-angle web legs in which the tip of the stem or leg is in flexural compression are not considered as compact elements; therefore, Eq. 6.9.2.2.1-3 should be applied in cases where the tip of the tee stem or double-angle web legs are subject to flexural compression. Tee stems and double angle web legs in which the tip of the stem or leg is in flexural tension are considered as compact elements; thus, Eqs. 6.9.2.2.1-1 and 6.9.2.2.1-2 (given on the preceding Slide 69) may be applied in this case.
For tees and double angles subject to combined axial compression and flexure in which the axial and flexural stresses in the flange of the tee or the flange legs of the angles are additive in compression, e.g., when a tee is used as a bracing member and the connection of this member is made to the flange, a bulge in the interaction curve occurs. As a result, Eqs. 6.9.2.2.1-1 and 6.9.2.2.1-2 on the preceding slide may significantly underestimate the resistance in such cases. Alternative approaches attempting to capture this bulge have proven to be generally inconclusive or incomplete. Therefore, it is recommended that Eqs. 6.9.2.2.1‑1 and 6.9.2.2.1-2 be conservatively applied to these cases. Should significant additional resistance be required, the use of one or more of these alternative approaches, as described in NSBA SBDH Chapter 4, may be considered.
The strength interaction pertaining to tension flange rupture at a cross section containing holes in one or more flanges that are subjected to tension under combined axial compression and flexure was addressed previously on Slides 34 and 35 in this lesson. AASHTO LRFD Article 6.8.2.3.3 provides a separate linear interaction equation focusing on the specific axial force combined with the specific moment causing the flexural tension in the flange at a given cross section.

## Slide 71: Combined Loading
Moment Magnification:
  For application in the preceding interaction equations, the moments about the x- and y-axes, Mux and Muy, due to the eccentricity of the applied factored axial compressive force, Pu, are to be calculated considering second-order effects arising from the additional secondary moment cause by the axial force acting through the member deflection.
Notes: AASHTO LRFD Article 6.9.2.2.1 specifies that for application in the preceding interaction equations, the moments about the x- and y-axes, Mux and Muy, due to the eccentricity of the applied factored axial compressive force, Pu, are to be calculated considering second-order effects arising from the additional secondary moment cause by the axial force acting through the member deflection. This discussion will focus on the moment about the major x-axis, Mux, as shown in the top figure on this slide. The end moments on the member shown in the bottom figure on this slide will be called M1 and M2.
In the column graphic, end moments about both axes and an axial load are applied at the top of the column. The exaggerated shape shows the displacement at each tenth point of the height. Because the axial load at the top and bottom of the column do not align with the axial load at intermediate points, there is an additional moment caused by this offset. A rigorous second-order elastic analysis can predict these effects or the empirical moment magnification procedure in AASHTO can be used.

## Slide 72: Combined Loading
Moment Magnification - cont.:
  The magnification of the first-order moment, (Mux)1, can be determined from a second-order elastic analysis, or more simply, from the approximate single-step adjustment specified in AASHTO LRFD Article 4.5.3.2.2b as follows:
Cm = equivalent uniform moment factor. For members braced against sidesway and without transverse loading between supports in the plane of bending
=
Pe = Euler buckling load for buckling about the x-axis (i.e., the axis of bending) (kips)
=
K = stiffness reduction factor taken equal to 1.0 for steel members
Eq. 4.5.3.2.2b-1
where:
δb =
Eq. 4.5.3.3.2b-3
)
Eq. 4.5.3.2.2b-6
Eq. 4.5.3.2.2b-5
Notes: As specified in AASHTO LRFD Article 6.9.2.2.1, the magnification of the first-order moment, (Mux)1, can be determined from a second-order elastic analysis, or more simply, from the approximate single-step adjustment specified in AASHTO LRFD Article 4.5.3.2.2b using Eq. 4.5.3.2.2b-1. The discussion on moment magnification in this course will focus on the application of the approximate single-step adjustment equations of AASHTO LRFD Article 4.5.3.2.2b to bracing members (other than single-angle bracing members) subject to combined axial compression and flexure (e.g., structural tees). The second term in Eq. 4.5.3.2.2b-1 (not shown on this slide) is a sidesway term that is generally not applicable for bracing members. For a more general application of the approximate single-step adjustment method to compression members with sidesway considered, refer to AASHTO LRFD Article 4.5.3.2.2b.
The equivalent uniform moment factor, Cm, in the equation for δb for members braced against sidesway and without transverse loading (other than the self-weight of the member) between supports in the plane of bending (Eq. 4.5.3.2.2b-6) depends on the ratio of the moments at the end of the member. M1 is taken as the smaller end moment and M2 taken as the larger end moment. The ratio, (M1/M2), is taken as positive when the member is bent in single curvature and negative when the member is bent in reverse curvature. Therefore, for a uniform moment, which is typically the case for an eccentrically loaded bracing member, Cm is equal to 1.0.
Pe is the Euler buckling load for buckling about the axis of bending, which in this case is the x-axis (Eq. 4.5.3.2.2b-5). Ix is the moment of inertia of the member about the x-axis, Kx is the effective length factor about the x-axis (Slide 48), and x is the unbraced length for buckling about the x-axis. K in the equation for δb is a stiffness reduction factor taken equal to 1.0 for steel members.
The application of these equations will be demonstrated in the following example of a tee-section lateral bracing member.

## Slide 73: Combined Loading - Example
Example – Determine the suitability of a WT8 x 28.5 rolled structural tee subject to eccentric axial compression for use as a diagonal top lateral bracing member in a straight tub-girder bridge.
Assume the tee flange is bolted to the lateral connection plate, and the length, , of the member is 12′-0”.
Assume the structural steel for the tee is ASTM A709 Grade 50W.
The factored compressive force, Pu, due to the Strength I load combination is -117.0 kips.
Ag = 8.39 in.2
d = 8.22 in.
tw = 0.430 in.
bf = 7.12 in.
tf = 0.715 in.
Ix = 48.7 in.4
Sx = 7.77 in.3
rx = 2.41 in.
= 1.94 in.
Iy = 21.6 in.4
ry = 1.60 in.
J = 1.10 in.4
Zx = 13.8 in.3
= 3.30 in.
H = 0.770
WT8 x 28.5
Notes: To illustrate the application of the preceding concepts, this example will determine the suitability of a WT8 x 28.5 rolled structural tee subject to eccentric axial compression for use as a diagonal top lateral bracing member in a straight tub-girder bridge. It is assumed that the tee flange is bolted to a lateral connection plate, and that the length, , of the bracing member is 12′-0”. The structural steel for the tee is assumed to be ASTM A709 Grade 50W. The factored compressive force, Pu, due to the Strength I load combination is computed separately to be -117.0 kips.
The section properties of interest for the WT8 x 28.5 are obtained from the AISC Manual of Steel Construction and are listed on this slide. Note that the thickness of the tee stem exceeds the minimum permissible thickness of 5/16 specified for structural steel in AASHTO LRFD Article 6.7.3. The distances ‘y bar′ and ′yo′ are shown on the top right figure on this slide. The distance ′y bar′ is used in the computation of the eccentricity of the load, e, and the distance ′yo′ is used in the computation of the polar radius of gyration, ′ro bar′ and the flexural constant, H (refer to Slide 50 in this lesson).

## Slide 74: Combined Loading - Example
Calculate the factored compressive resistance, Pr, of the tee-section member:
  First, determine the elastic critical buckling resistance, Pe, for FB, TB, or FTB, as applicable:
    Applicable buckling modes for tee-section compression members (with the y-axis defined as the axis of symmetry) are flexural buckling (FB) about the x-axis and flexural-torsional buckling (FTB) (Slide 45).
    For flexural buckling (FB) about the x-axis:
(Slide 47)
Assume Kx = 1.0
Notes: First, calculate the factored compressive resistance, Pr, of the tee-section member. The first step in calculating Pr is to determine the elastic critical buckling resistance of the member, Pe, for flexural buckling (FB), torsional buckling (TB), or flexural-torsional buckling (FTB), as applicable. As discussed previously on Slide 45 in this lesson, the applicable buckling modes for tee-section compression members (with the y-axis defined as the axis of symmetry) are flexural buckling (FB) about the x-axis and flexural-torsional buckling (FTB). Pe is taken as the smaller value based on these two buckling modes.
The elastic flexural buckling (FB) resistance about the x-axis, Pex, is given by the equation shown in the middle of this slide (refer to Slide 47 in this lesson). Since only the lateral connection plates at each end of the member are providing restraint for buckling about the x-axis, the effective length factor for flexural buckling about the x-axis, Kx, will conservatively be taken equal to 1.0. The length, x, will be taken as the full length of the member, or 12′-0”, since the member is not braced in the vertical plane anywhere along its length. The resulting maximum slenderness ratio, Kxx/rx, is equal to 59.75, which is less than the limiting value of 140 for a secondary compression member (Slide 66). AASHTO LRFD Table 6.6.2.1-1 indicates that top lateral bracing members are to be classified as secondary members. Substituting this slenderness ratio into the equation for Pex, along with the value of Ag taken from Slide 73, gives Pex equal to 672.6 kips.

## Slide 75: Combined Loading - Example
  For flexural-torsional buckling (FTB):
(Slide 50)
Assume Ky = 0.750
(Slide 47)
(Slide 48)
Notes: The elastic flexural-torsional buckling (FTB) resistance is given by the equation shown at the top of this slide (refer to Slide 50 in this lesson).
Pey is the elastic flexural buckling resistance about the y-axis given by the equation shown in the middle of this slide (refer to Slide 47 in this lesson). AASHTO LRFD Article 4.6.2.5 allows the effective length factor, K, to be taken as 0.750 for members with bolted or welded connections at both ends (refer to Slide 48 in this lesson). Therefore, the effective length factor for flexural buckling about the y-axis, Ky, will be taken equal to 0.750 in this example. The length, y, will be taken as the full length of the member, or 12′-0”, since the member is not braced in the out-of-plane direction anywhere along its length. The resulting maximum slenderness ratio, Kyy/ry, is equal to 67.5, which is less than the limiting value of 140 for a secondary compression member (Slide 66). Substituting this slenderness ratio into the equation for Pey, along with the value Ag taken from Slide 73, gives Pey equal to 527.0 kips.

## Slide 76: Combined Loading - Example
  For flexural-torsional buckling (FTB) - cont.:
(Slide 50)
G = 0.385E (Slide 49)
0
(Slide 50)
FTB controls
Pe = 455.9 kips
Notes: Pez is the elastic buckling load for torsional buckling and is given by the equation shown at the top of this slide (refer to Slide 50 in this lesson). As mentioned previously in the discussion for Slide 50, the warping torsional constant, Cw, is to conservatively be taken as zero for tees. Therefore, the first term in the equation for Pez drops out leaving the second equation shown on this slide. G is the elastic shear modulus for steel, which may be taken as 0.385E (refer to Slide 49 in this lesson). Substituting in the values of the St. Venant torsional constant, J, and the polar radius of gyration, ro bar, from Slide 73 into this equation gives Pez equal to 1,128 kips.
The equation for the elastic flexural-torsional buckling (FTB) resistance is taken from Slide 50 in this lesson. Substituting in the values of Pey from Slide 75, Pez from this slide, and the flexural constant, H, from Slide 73 gives Pe for FTB equal to 455.9 kips. The elastic critical buckling resistance of the member, Pe, is taken as the smaller of Pe for FTB and Pe for flexural buckling (FB) about the x-axis, Pex. Pex was computed previously on Slide 74 of this lesson to be 672.6 kips, which exceeds Pe for FTB or 455.9 kips. Thus, FTB controls and the elastic critical buckling resistance of the member, Pe, is taken equal to 455.9 kips.

## Slide 77: Combined Loading - Example
Next, check for slender cross-section elements:
  None of the rolled tee sections in the AISC Manual shape property tables have slender flanges (be = b).
  Check if the tee stem is a slender cross-section element:
Table 6.9.4.2.1-1 (Slide 55)
The tee stem is a slender cross-section element.
Notes: Next, check the tee-section member for any slender cross-section elements. As it turns out, none of the rolled tee sections listed in the AISC Manual of Steel Construction shape property tables have slender flanges. Therefore, the effective width of the tee-section flange, be, is equal to the full width of the flange, b.
Check if the tee stem is a slender element. As discussed previously on Slide 57 in this lesson, a slender cross-section element is a longitudinally unstiffened plate element within the cross-section of a member having a slenderness large enough such that nominal local buckling of the element may occur and may have an impact on its resistance in uniform axial compression prior to developing its full nominal yield strength. Slender cross-section elements have a b/t exceeding the limiting width-to-thickness ratio, λr, given in AASHTO LRFD Table 6.9.4.2.1-1. λr for the stems of rolled tees is given by the equation shown on this slide (refer to Slide 55 in this lesson), which is computed to be 18.1 for Fy equal to 50 ksi. When checking the b/t ratio for stems of structural tees, b is defined as the total depth of the structural tee, d (AASHTO LRFD Table 6.9.4.2.1-1 – Slide 55). For this section, d/t is computed to be 19.1, which exceeds λr. Therefore, the tee stem is a slender cross-section element and the potential effects of local buckling of the element on the overall resistance of the member in uniform axial compression must be considered.

## Slide 78: Combined Loading - Example
(Slide 58)
Pcr = nominal compressive resistance of the member calculated from Eq. 6.9.4.1.1-1 or 6.9.4.1.1-2, as applicable, using Ag (Slide 52) (kips)
Po = nominal yield resistance = FyAg = (50)(8.39) = 419.5 kips
(Slide 52)
(Slide 52)
Notes: For compression members containing one or more slender longitudinally unstiffened cross-section elements, Pn is to be determined using the equation shown at the top of this slide (refer to Slide 58 in this lesson). In this equation, Fcr is taken as the nominal compressive resistance, Pcr, which is equal to Pn calculated from AASHTO LRFD Eq. 6.9.4.1.1-1 or 6.9.4.1.1-2 (Slide 52), as applicable, using the total gross cross-sectional area of the member, Ag, divided by Ag. The calculated value of Fcr is then multiplied by the effective area of the cross-section, Aeff, to give the nominal compressive resistance of the member, Pn.
To calculate Pcr, first compute the nominal yield resistance, Po, which is equal to FyAg or 419.5 kips (refer to Slide 52 in this lesson). Next, calculate the ratio of Po/Pe. Substituting in the value of Pe equal to 455.9 kips taken from the preceding slide, the ratio of Po/Pe is computed to be 0.92, which is less than 2.25. Therefore, Equation 6.9.4.1.1-1 (inelastic column buckling – refer to Slides 52 and 53 in this lesson) controls. Substituting the values of Po and Pe into this equation gives Pcr = Pn = 285.4 kips. Dividing Pcr by Ag gives Fcr equal to 34.0 ksi.

## Slide 79: Combined Loading - Example
  Calculate the effective width, be, of the tee stem:
(Slide 61)
(Slide 59)
0
(Slide 43)
Notes: Calculate the effective width, be, of the tee stem. As discussed previously on Slide 61 of this lesson, if the stress level at overall member buckling, Fcr, is small enough relative to Fy, a slender cross-section element will not exhibit any significant local buckling effects prior to the member reaching its axial compressive resistance. This behavioral attribute is accounted for by checking the element width-to-thickness ratio, b/t, versus the modified limit . If b/t is less then or equal to this limit, no significant local buckling effects occur prior to the member reaching its axial compressive resistance and the effective width of the slender cross-section element is taken equal to the full element width, b. Substituting the value of Fcr equal to 34.0 ksi from the preceding slide, and the value of λr for the tee stem of 18.1 taken from Slide 77, into the top equation on this slide gives a modified limit of 21.9. For a tee stem, b/t is taken equal to d/t (AASHTO LRFD Table 6.9.4.2.1-1 – Slide 55). The resulting d/t value of 19.1 is less than the modified limit of 21.9; therefore, be for the tee stem is taken equal to the full element width, b.
From Slide 59 in this lesson, for rolled sections containing slender elements, the effective area, Aeff, is given by the equation shown in the middle of this slide. Since be is equal to b for both the flange and stem of the tee section, the second term in the equation is equal to zero, and Aeff is equal to the gross area of the tee section, Ag. The nominal compressive resistance, Pn, for members containing slender elements is equal to FcrAeff (Slide 78) or 285.4 kips. The factored compressive resistance of the member, Pr, is taken equal to the resistance factor for axial compression (c = 0.95 for noncomposite members – Slide 43) times the nominal compressive resistance, Pn, or 271.1 kips.
Calculate the effective width, be, of the tee stem. As discussed previously on Slide 61 of this lesson, if the stress level at overall member buckling, Fcr, is small enough relative to Fy, a slender cross-section element will not exhibit any significant local buckling effects prior to the member reaching its axial compressive resistance. This behavioral attribute is accounted for by checking the element width-to-thickness ratio, b/t, versus the modified limit 𝜆_𝑟= √(𝐹_𝑦∕𝐹_𝑐𝑟 ). If b/t is less then or equal to this limit, no significant local buckling effects occur prior to the member reaching its axial compressive resistance and the effective width of the slender cross-section element is taken equal to the full element width, b. Substituting the value of Fcr equal to 34.0 ksi from the preceding slide, and the value of λr for the tee stem of 18.1 taken from Slide 77, into the top equation on this slide gives a modified limit of 21.9. For a tee stem, b/t is taken equal to d/t (AASHTO LRFD Table 6.9.4.2.1-1 – Slide 55). The resulting d/t value of 19.1 is less than the modified limit of 21.9; therefore, be for the tee stem is taken equal to the full element width, b.
From Slide 59 in this lesson, for rolled sections containing slender elements, the effective area, Aeff, is given by the equation shown in the middle of this slide. Since be is equal to b for both the flange and stem of the tee section, the second term in the equation is equal to zero, and Aeff is equal to the gross area of the tee section, Ag. The nominal compressive resistance, Pn, for members containing slender elements is equal to FcrAeff (Slide 78) or 285.4 kips. The factored compressive resistance of the member, Pr, is taken equal to the resistance factor for axial compression (c = 0.95 for noncomposite members – Slide 43) times the nominal compressive resistance, Pn, or 271.1 kips.

## Slide 80: Combined Loading - Example
  The tee section is also subject to uniform bending moment about the major principal axis (x-axis) due to the eccentricity of the connection at each end of the member. Assume the lateral connection plate thickness is 1.0 in. The first-order moment due to the eccentricity, (Mux)1, is computed as:
  Determine the second-order elastic moment acting on the tee section :
(Slide 72)
Notes: The tee section is also subject to a uniform bending moment about the major principal axis (x-axis) due to the eccentricity of the connection at each end of the member. Assume the thickness of the lateral connection plates is 1.0 inch; therefore, the first-order moment, (Mux)1, due to the eccentricity is computed as the factored compressive force, Pu, times the distance ′y bar′ from the center of gravity of the tee section to the top of the tee-section flange (refer to the figure on Slide 73 in this lesson) plus one-half of the lateral connection plate thickness. Substituting in the appropriate values gives (Mux)1 of 285.5 kip-in.
Second-order effects arise from the additional secondary moment caused by the axial force acting through the member deflection (refer to Slide 71 in this lesson). AASHTO LRFD Article 4.5.3.2.2b specifies that the resulting magnification of the first-order moment may be determined from the approximate single-step adjustment method in lieu of a second-order analysis; that is, the second-order elastic moment, (Mux)2, may be determined from the equation shown in the middle of this slide, which is taken from Slide 72 in this lesson. δb is a moment magnification factor given by the bottom-left equation on this slide. Cm is the equivalent uniform moment factor, which for members braced against sidesway and without transverse loading (other than the self-weight of the member) between supports in the plane of bending is given by the center equation at the bottom of this slide. Pe is the Euler buckling load for buckling about the axis of bending, which in this case is the x-axis, and is given by the bottom-right equation on this slide. K in the equation for δb is a stiffness reduction factor taken equal to 1.0 for steel members.

## Slide 81: Combined Loading - Example
Notes: The tee section is bent in single curvature by equal moments at the end of the member due to the eccentricity. For single curvature, the ratio of the end moments (M1/M2 = 1.0) is to be taken as positive. Therefore, from the equation shown at the top of this slide, the equivalent uniform moment factor, Cm, is equal to 1.0.
Pe is the Euler buckling load for buckling about the x-axis (i.e., the plane of bending), which is given by the second equation on this slide. From earlier calculations, the effective length factor for flexural buckling about the x-axis, Kx, was assumed equal to 1.0. The moment of inertia of the tee section about the x-axis, Ix, is 48.7 in.4 (Slide 73). The length of the member for flexural buckling about the x-axis, x, is equal to 12.0 feet. Substituting these values into the equation gives Pe equal to 672.2 kips.
With Cm and Pe now calculated, the magnification factor, δb, is determined by substituting these values, along with the value of K = 1.0, into the equation for δb, which gives a magnification factor of 1.21. Multiplying this factor by the first-order elastic moment of 285.5 kip-in. taken from the preceding slide gives a second-order elastic moment, (Mux)2, of 345.5 kip-in.

## Slide 82: Combined Loading - Example
  Calculate the factored flexural resistance, Mrx, of the tee-section member about the x-axis:
    Determine if the tip of the tee stem is in compression or tension:
    For tees loaded in the plane of symmetry, the nominal flexural resistance, Mn, is taken as the smallest value based on yielding, lateral-torsional bucking, flange local buckling, and local buckling of the tee stem, as applicable (AASHTO LRFD Article 6.12.2.2.4a).
    For tee stems, Mn based on yielding is taken as (AASHTO LRFD Article 6.12.2.2.4b – 10th Edition):
where:
for tee stems subject to tension.
Notes: Next, calculate the factored flexural resistance, Mrx, of the tee-section member for bending about the x-axis. First, it must be determined if the tip of the tee stem in is compression or tension under the combined loading. The factored stress at the tip of the tee stem, ftip, is calculated as the algebraic sum of the factored compressive force, Pu, divided by the gross area, Ag, and the second-order elastic bending moment, (Mux)2, divided by the elastic section modulus to the tip of the tee stem for bending about the x-axis, Sx. Since the factored compressive force is applied above the neutral axis of the tee section, the bending moment is positive at each end of the member. Substituting in the appropriate values gives a tensile stress of 30.5 ksi at the flange tip.
For tees loaded in the plane of symmetry, AASHTO LRFD Article 6.12.2.2.4a specifies that the nominal flexural resistance, Mn, is to be taken as the smallest value based on yielding, lateral-torsional buckling, flange local buckling, and local buckling of the tee stem, as applicable. For tee stems, AASHTO LRFD Article 6.12.2.2.4b (10th Edition) specifies that Mn based on yielding is to be taken as the plastic moment, Mp = FyZx, where Zx is the plastic section modulus for bending about the x-axis. Furthermore, for tee stems subject to tension (i.e., when the flange is subject to compression), Mp is limited to 1.6My, where My is equal to the yield moment, which is intended to indirectly control situations where significant yielding of the tee stem may occur at service load levels. For tee stems subject to compression, Mp is limited to My.

## Slide 83: Combined Loading - Example
    For tee stems subject to tension, Mn based on lateral-torsional buckling is taken as (AASHTO LRFD Article 6.12.2.2.4c – 10th Edition):
      If Lb ≤ Lp, then lateral-torsional buckling does not apply.
      If Lp < Lb ≤ Lr, then:
      If Lb > Lr, then:
Eq. 6.12.2.2.4c-1
Eqs. 6.12.2.2.4c-2 & 5
Terms are defined on the next slide.
Notes: The plastic moment, Mp, is equal to Fy times the plastic section modulus for bending about the x-axis, Zx. Substituting in the value of Zx taken from Slide 73 in this lesson, Mp is computed to be 690.0 kip-in. For tee stems subject to tension, this value cannot exceed 1.6My, where My is the yield moment equal to Fy times the elastic section modulus to the tip of the stem for bending about the x-axis, Sx. Substituting the value of Sx taken from Slide 73 gives 1.6FySx equal to 621.6 kip-in, which is less than Mp. Therefore, the nominal flexural resistance, Mn, based on yielding is equal to 621.6 kip-in.
For tee stems subject to tension, Mn based on lateral-torsional buckling is to be taken as specified in AASHTO LRFD Article 6.12.2.2.4c (10th Edition). If the unbraced length, Lb, is less than or equal to the anchor point, Lp, then lateral-torsional buckling does not apply. If Lb is greater than Lp but less then or equal to the anchor point, Lr, then Eq. 6.12.2.2.4c-1 provides a linear transition in Mn from Mp to My. If Lb exceeds Lr, then Mn is taken equal to Mcr, which is given by Eqs. 6.12.2.2.4c-2 & 5, as shown on this slide. The terms in these equations are defined on the next slide.
For tee stems subject to compression anywhere along the unbraced length, Mn based on lateral-torsional buckling is taken equal to Mcr, but not to exceed My.
The moment gradient modifier, Cb, specified for I-sections (Lesson 8) is not included in these equations as the application of Cb to cases where the stem is in compression is unconservative. Also, for reverse curvature bending, the portion with the stem in compression may govern the lateral–torsional buckling resistance even though the corresponding moments may be small in relation to the moments in the other portions of the unbraced length. The lateral–torsional buckling resistance for the case where the stem is in compression is substantially smaller than for the case where the stem is in tension. For cases where the stem is in tension, connection details should be designed to minimize end restraint moments that may cause the stem to be in flexural compression at the ends of the member.

## Slide 84: Combined Loading - Example
where:
d = depth of the tee (in.)
Iy = moment of inertia about the y-axis (in.4)
J = St. Venant torsional constant (in.4)
ry = radius of gyration about the y-axis (in.)
Sx = elastic section modulus about the x-axis with respect to the tip of the tee stem (in.3)
The terms in the lateral-torsional buckling equations on the preceding slide and on this slide are defined as follows:
Notes: The terms in the lateral-torsional buckling equations on the preceding slide and on this slide are defined as shown.
For tee stems subject to compression anywhere along the unbraced length, the term, B, is taken as a negative value.

## Slide 85: Combined Loading - Example
(Slide 83)
(Slide 83)
Notes: Substituting in the value of the radius of gyration about the y-axis, ry = 1.60 inches (from Slide 73 in this lesson), into the equation for the anchor point, Lp, from the preceding slide gives Lp equal to 67.8 inches, which is less than the unbraced length, Lb, equal to 144.0 inches.
Substituting in the values of Iy, J, d, and Sx taken from Slide 73 in this lesson into the equation for the anchor point, Lr, from the preceding slide gives Lr equal to 788.9 inches, which exceeds Lb.
Since Lb lies in-between the anchor points, Lp and Lr, Mn based on lateral-torsional buckling is computed from the linear transition Eq. 6.12.2.2.4c-1 taken from Slide 83 in this lesson. Substituting in the values of Mp = FyZx ≤ 1.6My equal to 621.6 kip-in. (refer to Slide 83 in this lesson), My = FySx = 388.5 kip-in., Lb, Lp, and Lr gives Mn based on lateral-torsional buckling of 597.0 kip-in.

## Slide 86: Combined Loading - Example
    For tee flanges subject to compression, Mn based on flange local buckling is taken as (AASHTO LRFD Article 6.12.2.2.4d – 10th Edition):
      If λf ≤ λpf, then flange local buckling does not apply.
      If λpf < λf ≤ λrf, then:
      If λf > λrf, then:
Eq. 6.12.2.2.4d-1
Eq. 6.12.2.2.4d-2
where:
λf = flange slenderness = bf/2tf
λpf = limiting slenderness for a compact flange =
λrf = limiting slenderness for a noncompact flange =
Sxc = elastic section modulus about the x-axis to the compression flange (in.3)
Notes: For tee flanges subject compression, Mn based on flange local buckling is to be taken as specified in AASHTO LRFD Article 6.12.2.2.4d (10th Edition). If the flange slenderness, λf = bf/2tf, is less than or equal to the limiting slenderness for a compact flange, λpf, given by the equation shown on this slide, then flange local buckling does not apply. bf is the flange width and tf is the flange thickness. If λf is greater than λpf but less then or equal to the limiting slenderness for a noncompact flange, λrf, given by the equation shown on this slide, then the inelastic flange local buckling resistance Eq. 6.12.2.2.4d-1 provides a linear transition in Mn from Mp to 0.7FySxc. If λf exceeds λrf, then Mn is given by the elastic flange local buckling resistance Eq. 6.12.2.2.4d-2, as shown on this slide.

## Slide 87: Combined Loading - Example
flange local buckling does not apply.
    For tee stems subject to compression, Mn based on local buckling of the stem is taken as specified in AASHTO LRFD Article 6.12.2.2.4e (10th Edition). Since the tee stem is subject to tension in this case, local buckling of the stem does not apply.
(lateral-torsional buckling controls)
Notes: The flange slenderness, bf/2tf, of the tee section is computed to be 5.0 (bf and tf are taken from Slide 73 in this lesson). The limiting slenderness for a compact flange, λpf, is computed to be 9.15 for Fy equal to 50 ksi, which exceeds λf equal to 5.0; therefore, referring back to the preceding slide, flange local buckling does not apply.
For tee stems subject to compression, the nominal flexural resistance, Mn, based on local buckling of the stem is taken as specified in AASHTO LRFD Article 6.12.2.2.4e (10th Edition). Since the tee stem is subject to tension in this case, local buckling of the stem does not apply. For cases where the tee stem is subject to compression, refer to AASHTO LRFD Article 6.12.2.2.4e for the proper equations to compute Mn based on local buckling of the stem. Note also that slightly different equations are specified in AASHTO LRFD Article 6.12.2.2.4 to compute Mn for double angles, which are not covered in this course.
Since the computed nominal flexural resistance based on lateral-torsional buckling, Mn = 597.0 kip-in (Slide 85), is less that the computed nominal flexural resistance based on yielding, Mn = 621.6 kip-in. (Slide 83), Mn for the tee section is taken equal to 597.0 kip-in. The factored flexural resistance of the tee section about the x-axis, Mrx, is taken equal to the resistance factor for flexure, f = 1.0 (AASHTO LRFD Article 6.5.4.2), times Mn, or 597.0 kip-in.

## Slide 88: Combined Loading - Example
Eq. 6.9.2.2.1-1
Eq. 6.9.2.2.1-2
For members in which all the cross-section elements are defined as compact for flexure (Slide 69):
The WT8 x 28.5 tee-section member is satisfactory.
Notes: As discussed previously on Slide 70 in this lesson, tee stems in which the tip of the stem is in flexural tension are considered as compact elements; thus, the strength interaction Eqs. 6.9.2.2.1-1 and 6.9.2.2.1-2 shown on this slide (refer also to Slide 69 in this lesson) may be applied in this case to check for the effect of the combined axial compression and flexure on the member.
Since the ratio of Pu/Pr, which is equal to 0.43 in this case, is greater than 0.2, the second interaction Eq. 6.9.2.2.1-2 applies. Since Mrx is governed by lateral–torsional buckling, the largest value of Mux/Mrx associated with the unbraced length relevant to the lateral–torsional buckling resistance should be considered along with the cross-section-based value of Pu/Pr (Muy/Mry is not applicable in this case and is taken equal to zero). However, Mux is constant along the length of the member and so the preceding is not a consideration in this example. Substituting Pu along with the previously computed values of Pr, (Mux)2, and Mrx into this equation gives a value of 0.95, which is less than 1.0. Therefore, the WT8 x 28.5 tee-section member is satisfactory for combined axial compression and flexure..
Since the flange containing bolt holes in the end cross-sections of the tee-section member is not subject to tension under the combined effect of the axial compression and flexure on the member in this case, tension rupture under the combined loading (refer to Slides 34 and 35 in this lesson) does not need to be checked.

## Slide 89: COMPRESSION MEMBERS single-angle members
Notes: The next topic in this lesson will discuss special AASHTO LRFD provisions for the design of single-angle compression members. The discussion includes an example illustrating the application of these provisions to the design of a single-angle member serving as the bottom strut of a cross-frame in a horizontally curved I-girder bridge.

## Slide 90: Single-Angle Compression Members
Notes: Single-angle members, as shown in cross-section on this slide, are commonly used as cross-frame and lateral bracing members for steel bridges. Since in most practical applications, the angle is connected through one leg only, single-angle bracing members are typically subject to combined axial compression/tension and flexure, or moments about both principal axes due to the eccentricities of the applied axial load. The angle is also usually restrained by differing amounts about its geometric x- and y-axes. As a result, the prediction of the nominal resistance of these members under these conditions is difficult, particularly when the member is subject to compression.
As discussed previously on Slide 31 of this lesson, the condition of flexure due to eccentric axial tension for single angles at the strength limit state is typically addressed through the use of the shear lag coefficient, U, specified in AASHTO LRFD Article 6.8.2.2 (refer to Slides 12 through 15 of this lesson).
The condition of flexure due to eccentric axial compression is now efficiently handled through the use of an effective slenderness ratio, (K/r)eff, as specified in AASHTO LRFD Article 6.9.4.4. The use of the specified effective slenderness ratio allows single angles satisfying certain conditions that are subject to combined axial compression and flexure to be designed as pin-ended concentrically loaded compression members for flexural buckling only. Furthermore, when the effective slenderness ratio is used, single angles need not be checked for flexural-torsional buckling, and the calculation of the nominal flexural resistance, Mn, of a single-angle member is typically not required. These provisions are based on the provisions for the design of single-angle members used in latticed transmission towers.

## Slide 91: Single-Angle Compression Members Effective Slenderness Ratio
The provisions of AASHTO LRFD Article 6.9.4.4 permit the effects of all eccentricities in single-angle compression members to be neglected when these members are evaluated as pin-ended concentrically loaded compression members for flexural buckling (FB) only using an appropriate effective slenderness ratio, (K/r)eff.
Furthermore, when the effective slenderness ratio is used, single angles need not be checked for flexural-torsional buckling (FTB).
The member must satisfy all the following conditions in order to use (K/r)eff :
  The end connections are to a single leg;
  The member is loaded at the ends in compression through the same leg;
  The end connections are welded or use a minimum of two bolts;
  The member is not subjected to any intermediate transverse loads; and
  When used as web members in trusses, all adjacent web members are attached to the same side of the gusset plate or chord.
Notes: The provisions of AASHTO LRFD Article 6.9.4.4 permit the effects of all eccentricities in single-angle compression members to be neglected when these members are evaluated as pin-ended concentrically loaded compression members for flexural buckling (FB) only using an appropriate effective slenderness ratio, (K/r)eff. The effective slenderness ratio indirectly accounts for the bending in the angles due to the eccentricity of the loading allowing the member to be proportioned as if it were a pinned-end concentrically loaded compression member. Furthermore, when the effective slenderness ratio is used, single angles need not be checked for flexural-torsional buckling (FTB). The member must satisfy all of the conditions listed on this slide, which are typically satisfied by members used in cross-frames and lateral bracing in steel-bridge applications, in order to use the effective slenderness ratio.

## Slide 92: Single-Angle Compression Members Effective Slenderness Ratio
The equations for the effective slenderness ratio presume significant end rotational restraint about the y-axis, or the axis perpendicular to the connected leg and gusset plate.
As a result, the angle tends to buckle primarily about the x-axis due to the eccentricity of the load about the x-axis coupled with the high degree of restraint about the y-axis.
Thus, the radius of gyration in the effective slenderness ratio equations is taken as rx, or the radius of gyration about the geometric axis parallel to the connected leg.
Notes: The equations for the effective slenderness ratio presume significant end rotational restraint about the y-axis, or the axis perpendicular to the connected leg and gusset plate, as shown for the equal-leg and unequal-leg angles on this slide. As a result, as shown in various tests, the angle tends to buckle primarily about the x-axis due to the eccentricity of the load about the x-axis coupled with the high degree of restraint about the y-axis. Thus, the radius of gyration in the effective slenderness ratio equations is taken as rx, or the radius of gyration about the geometric axis parallel to the connected leg, as opposed to the minimum radius of gyration about the minor principal axis of the angle, rz (refer to Slide 90 in this lesson). When an angle has significant rotational restraint about the y-axis, the stress along the connected leg will be approximately uniform. A separate set of equations presented in the AISC Specification, which assume a higher degree of x-axis rotational restraint and thus are intended for application only to single angles used as web members in box or space trusses, is not provided in the AASHTO LRFD Specifications.
The illustration on the right-hand side of this slide shows a single angle loaded through one leg with the ends assumed clamped and unable to rotate. Actual gusset / connection plates have some flexibility and would not provide a truly fixed condition. The illustration shows the effects of loading through a leg as opposed to through the centroid of the cross-section, a moment is induced.

## Slide 93: Single-Angle Compression Members Effective Slenderness Ratio
If , then:
Eq. 6.9.4.4-1
If , then:
Eq. 6.9.4.4-2
where:
 = distance between the work points of the joints measured along the length of the angle (in.)
rx = radius of gyration about the geometric axis of the angle parallel to the connected leg (in.)
Notes: The equations for the effective slenderness ratio, (K/r)eff, for the case of equal-leg angles and unequal-leg angles connected through the longer leg are given on this slide. In the equations, it is important to note that  is not the physical length of the single-angle member but is instead to be taken as the distance between the work points of the joints (Lesson 11) at each end of the member measured along the length of the angle. Also, rx in the equations should be taken as the smaller value about the angle geometric axes, which is typically listed as ry for unequal-leg rolled angle shapes connected through the longer leg.
Single-angle members are often employed in X-type configurations in cross-frames. Since the necessary rotational restraint about the y-axis assumed in the effective slenderness ratio equations may not be present at the crossover point of the diagonals (e.g., if the members are only connected with a single bolt at that point), it is currently recommended in AASHTO LRFD Article C6.9.4.4 that the full length of the diagonal between the connection work points be used for  in applying the effective slenderness ratio equations. Section 2.3.2 of Chapter 13 of the NSBA SBDH on Bracing System Design presents a different viewpoint on this issue for consideration.
Buckling of the angle when loaded through one leg is shown in the graphic on the right-hand side of this slide. There are deflections about the two geometric axes and some twisting. The use of the equations on this slide allows for this complex behavior to be modeled through an equivalent slenderness approach.

## Slide 94: Single-Angle Compression Members Effective Slenderness Ratio
If , then:
Eq. 6.9.4.4-3
If , then:
Eq. 6.9.4.4-4
where:
b = length of the longer leg of an unequal-leg angle (in.)
bs = length of the shorter leg of an unequal-leg angle (in.)
rz = radius of gyration about the minor principal axis of the angle (in.)
Notes: The equations for the effective slenderness ratio, (K/r)eff, for the case of unequal-leg angles connected through the shorter leg and with ratios of leg lengths, (b/bs), less than 1.7 are given on this slide. b is the length of the longer leg and bs is the length of the shorter leg.
The limited available test data for this case give lower capacities for comparable /rx values than equal-leg angles. Stiffening the shorter leg rotationally tends to force the buckling axis of the angle away from the x-axis and closer to the z-axis, or minor principal axis of the angle. Thus, the effective slenderness ratio equations for this case are modified by adding an additional term based on the ratio of the leg lengths, along with a governing slenderness limit based on /rz for slender unequal-leg angles. The upper limit on (b/bs) of 1.7 is based on the limits of the available physical tests.
Single-angle compression members not meeting one or more of the specified conditions summarized on Slide 91 of this lesson, or with (b/bs) greater than or equal to 1.7, should instead be explicitly evaluated for combined axial load and flexure as beam-columns according to Section H2 of the AISC Specification. Refer to AASHTO LRFD Article C6.9.4.4 for further information on the suggested procedure to follow in the unlikely event that this would be required. It is recommended herein that should (b/bs) be greater than or equal to 1.7, that a different single-angle member size with (b/bs) less than 1.7 be chosen in lieu of following this procedure.

## Slide 95: Single-Angle Compression Members
Elastic critical buckling resistance, Pe:
Check for slender cross-section elements (i.e., the angle legs) and calculate Pn accordingly (Slides 54 through 62).
Check the actual maximum slenderness ratio (vs. the effective slenderness ratio) against the appropriate limiting slenderness (Slide 66).
Flexural buckling (FB)
Notes: Once the proper effective slenderness ratio, (K/r)eff, is calculated from one of the equations shown on the previous two slides, the ratio is substituted into the equation for the elastic critical buckling resistance, Pe, for flexural buckling (FB), as shown at the top of this slide. As mentioned previously, flexural-torsional buckling (FTB) need not be checked when the effective slenderness ratio is used in the calculation of Pe. The effects of all eccentricities can also be neglected so that the member need not be checked for combined loading (i.e., combined axial compression and flexure). With Pe determined, the nominal compressive resistance, Pn, can then be calculated from the appropriate equation shown on Slide 52 in this lesson. However, a check of the angle legs should first be made to see if they are slender cross-section elements subject to potential local buckling. The angle legs are both classified as elements supported along one longitudinal edge for this check. If so, Pn must be calculated accordingly to account for the effects of local buckling as discussed previously on Slides 54 through 62 in this lesson.
Finally, it is important to note that AASHTO LRFD Article 6.9.4.4 specifies that the actual maximum slenderness ratio of the angle, as opposed to (K/r)eff, is not to exceed the applicable limiting slenderness ratio specified in AASHTO LRFD Article 6.9.3 (refer to Slide 66 in this lesson). Thus, if the actual maximum slenderness ratio of the angle (which is typically based on the actual physical length of the angle and the radius of gyration about the minor principal axis, rz) exceeds the limiting ratio, a larger angle must be selected until the ratio is satisfied. If (K/r)eff exceeds the limiting ratio, but the actual maximum slenderness ratio of the angle does not, the design is satisfactory.
Another view of the buckled angle from the preceding slides is shown on this slide. Note a twist and sweep deformation are apparent.

## Slide 96: Single-Angle Compression Members - Example
Example – Determine the suitability of a L6 x 6 x 3/8 single-angle member for use as the bottom strut in a cross-frame of a horizontally curved I-girder bridge. The length of the member is 8′-0”.
Assume the cross-frame is arranged in an X-type configuration, and that the work points of the bolted connections at each end of the member are located 6 inches from the centerline of the girder webs. The girder spacing is 11′-0”.
Assume the structural steel for the angle is ASTM A709 Grade 50.
The factored compressive force, Pu, due to the Strength I load combination is
-70.0 kips.
L6 x 6 x 3/8
Ag = 4.36 in.2
rx = 1.87 in.
rz = 1.19 in.
Notes: To illustrate the application of these provisions, this example will determine the suitability of a L6 x 6 x 3/8 single-angle member for use as the bottom strut in a cross-frame of a horizontally curved I-girder bridge. The length of the member is 8′-0”. Note that the thickness of the angle legs exceeds the minimum permissible thickness of 5/16 specified for structural steel in AASHTO LRFD Article 6.7.3. Due to availability concerns, fabricators prefer that angle sizes with thicknesses specified in 1/16ths be avoided. Assume the cross-frame is arranged in an X-type configuration, and that the work points of the bolted connections at each end of the member are located 6 inches from the centerline of the girder webs. The girder spacing is 11′-0”. Assume the structural steel for the angle is ASTM A709 Grade 50. The factored compressive force, Pu, due to the Strength I load combination is -70.0 kips. The gross cross-sectional area of the member, Ag, along with the radii of gyration about the x- and z-axes, rx and rz, respectively, are shown on this slide.

## Slide 97: Single-Angle Compression Members - Example
Calculate the elastic critical buckling resistance, Pe, of the single-angle member:
  Determine the effective slenderness ratio, (K/r)eff:
(Slide 93)
(Slide 95)
Notes: First, calculate the elastic critical buckling resistance, Pe, of the single-angle member. Determine the effective slenderness ratio, (K/r)eff. As discussed previously, in the computation of the effective slenderness ratio,  is to be taken as the distance between the work points of the joints at each end of the member measured along the length of the angle in lieu of the actual physical length of the angle. Assume that the angle serving as the bottom strut of an X-type cross-frame is welded to gusset plates, which are assumed bolted to the cross-frame connection plates in the field. The work points of the connection at each end of the member are assumed to be located 6 inches from the centerline of the girder webs. The girder spacing is 11′-0”. Thus, as shown at the top of this slide,  is computed to be 10.0 feet.
The ratio of /rx for this member is computed to be 64.2 which is less than 80. Therefore, for equal-leg angles with /rx less than 80, the equation shown in the middle of this slide taken from Slide 93 in this lesson is to be used to compute (K/r)eff. Substituting /rx of 64.2 into this equation gives (K/r)eff of 120.2.
Since the effective slenderness ratio is being used, the member can be treated as a pin-ended concentrically loaded compression member to be checked for flexural buckling (FB) only. The flexural buckling equation used to calculate Pe is taken from Slide 95 in this lesson. Substituting in (K/r)eff of 120.2 and the gross cross-sectional area of the member, Ag, equal to 4.36 in.2 gives Pe of 86.4 kips.

## Slide 98: Single-Angle Compression Members - Example
Next, check for slender cross-section elements:
  Check if the angle legs are slender cross-section elements:
Table 6.9.4.2.1-1 (Slide 55)
The angle legs are slender cross-section elements.
Notes: Next, check the single-angle member for any slender cross-section elements. Check if the angle legs are slender cross-section elements. As discussed previously on Slide 57 in this lesson, a slender cross-section element is a longitudinally unstiffened plate element within the cross-section of a member having a slenderness large enough such that nominal local buckling of the element may occur and may have an impact on its resistance in uniform axial compression prior to developing its full nominal yield strength. Slender cross-section elements have a b/t exceeding the limiting width-to-thickness ratio, λr, given in AASHTO LRFD Table 6.9.4.2.1-1. λr for the outstanding legs of single angles is given by the equation shown on this slide (refer to Slide 55 in this lesson), which is computed to be 10.8 for Fy equal to 50 ksi. For this section, b/t of the legs is computed to be 16.0, which exceeds λr. Therefore, the angle legs are slender cross-section elements and the potential effects of local buckling of these elements on the overall resistance of the member in uniform axial compression must be considered.

## Slide 99: Single-Angle Compression Members - Example
(Slide 58)
Pcr = nominal compressive resistance of the member calculated from Eq. 6.9.4.1.1-1 or 6.9.4.1.1-2, as applicable, using Ag (Slide 52) (kips)
Po = nominal yield resistance = FyAg = (50)(4.36) = 218.0 kips
(Slide 52)
(Slide 52)
Notes: For compression members containing one or more slender longitudinally unstiffened cross-section elements, Pn is to be determined using the equation shown at the top of this slide (refer to Slide 58 in this lesson). In this equation, Fcr is taken as the nominal compressive resistance, Pcr, which is equal to Pn calculated from AASHTO LRFD Eq. 6.9.4.1.1-1 or 6.9.4.1.1-2 (Slide 52), as applicable, using the total gross cross-sectional area of the member, Ag, divided by Ag. The calculated value of Fcr is then multiplied by the effective area of the cross-section, Aeff, to give the nominal compressive resistance of the member, Pn.
To calculate Pcr, first compute the nominal yield resistance, Po, which is equal to FyAg or 218.0 kips (refer to Slide 52 in this lesson). Next, calculate the ratio of Po/Pe. Substituting in the value of Pe equal to 86.4 kips taken from Slide 97, the ratio of Po/Pe is computed to be 2.52, which is greater than 2.25. Therefore, Equation 6.9.4.1.1-2 (elastic column buckling – refer to Slides 52 and 53 in this lesson) controls. Substituting the value Pe into this equation gives Pcr = Pn = 75.8 kips. Dividing Pcr by Ag gives Fcr equal to 17.4 ksi.

## Slide 100: Single-Angle Compression Members - Example
  Calculate the effective width, be, of the angle legs:
(Slide 61)
(Slide 59)
0
(Slide 43)
Notes: Calculate the effective width, be, of the angle legs. As discussed previously on Slide 61 of this lesson, if the stress level at overall member buckling, Fcr, is small enough relative to Fy, a slender cross-section element will not exhibit any significant local buckling effects prior to the member reaching its axial compressive resistance. This behavioral attribute is accounted for by checking the element width-to-thickness ratio, b/t, versus the modified limit . If b/t is less then or equal to this limit, no significant local buckling effects occur prior to the member reaching its axial compressive resistance and the effective width of the slender cross-section element is taken equal to the full element width, b. Substituting the value of Fcr equal to 17.4 ksi from the preceding slide, and the value of λr for the angle legs of 10.8 taken from Slide 98, into the top equation on this slide gives a modified limit of 18.3. The b/t value of 16.0 for the angle legs is less than the modified limit of 18.3; therefore, be for the angle legs is taken equal to the full element width, b.
From Slide 59 in this lesson, for rolled sections containing slender elements, the effective area, Aeff, is given by the equation shown in the middle of this slide. Since be is equal to b for both angle legs, the second term in the equation is equal to zero, and Aeff is equal to the gross area of the single-angle member, Ag. The nominal compressive resistance, Pn, for members containing slender elements is equal to FcrAeff (Slide 99) or 75.8 kips. The factored compressive resistance of the member, Pr, is taken equal to the resistance factor for axial compression (c = 0.95 for noncomposite members – Slide 43) times the nominal compressive resistance, Pn, or 72.0 kips. Pr exceeds the absolute value of the factored compressive force, Pu, which is equal to 70.0 kips (Slide 96); therefore, the single-angle member is satisfactory for compression.
Calculate the effective width, be, of the angle legs. As discussed previously on Slide 61 of this lesson, if the stress level at overall member buckling, Fcr, is small enough relative to Fy, a slender cross-section element will not exhibit any significant local buckling effects prior to the member reaching its axial compressive resistance. This behavioral attribute is accounted for by checking the element width-to-thickness ratio, b/t, versus the modified limit 𝜆_𝑟=√(𝐹_𝑦∕𝐹_𝑐𝑟 ). If b/t is less then or equal to this limit, no significant local buckling effects occur prior to the member reaching its axial compressive resistance and the effective width of the slender cross-section element is taken equal to the full element width, b. Substituting the value of Fcr equal to 17.4 ksi from the preceding slide, and the value of λr for the angle legs of 10.8 taken from Slide 98, into the top equation on this slide gives a modified limit of 18.3. The b/t value of 16.0 for the angle legs is less than the modified limit of 18.3; therefore, be for the angle legs is taken equal to the full element width, b.
From Slide 59 in this lesson, for rolled sections containing slender elements, the effective area, Aeff, is given by the equation shown in the middle of this slide. Since be is equal to b for both angle legs, the second term in the equation is equal to zero, and Aeff is equal to the gross area of the single-angle member, Ag. The nominal compressive resistance, Pn, for members containing slender elements is equal to FcrAeff (Slide 99) or 75.8 kips. The factored compressive resistance of the member, Pr, is taken equal to the resistance factor for axial compression (c = 0.95 for noncomposite members – Slide 43) times the nominal compressive resistance, Pn, or 72.0 kips. Pr exceeds the absolute value of the factored compressive force, Pu, which is equal to 70.0 kips (Slide 96); therefore, the single-angle member is satisfactory for compression.

## Slide 101: Single-Angle Compression Members - Example
Lastly, check the actual maximum slenderness ratio of the member against the appropriate limiting slenderness ratio:
  For single angles, K = 1.0 regardless of the end connection (Slide 48).
The maximum slenderness ratio is satisfactory.
Notes: Lastly, check the actual maximum slenderness ratio (vs. the effective slenderness ratio) of the single-angle member against the appropriate limiting slenderness ratio. The effective length factor, K, is taken as 1.0 for single-angle members regardless of the end connection, as specified AASHTO LRFD Article 4.6.2.5 (refer to Slide 48 in this lesson). Using the physical length of the angle (8′-0” - Slide 96) to represent the unbraced length of the bottom strut in this case, the maximum slenderness ratio is computed using the minimum radius of gyration of the angle about the minor principal axis, rz. Substituting in the value of rz of 1.19 in. (Slide 96), the maximum slenderness ratio is computed to be 80.7, which is less than the limiting slenderness ratio of 120 specified for a primary compression member (Slide 66). AASHTO LRFD Table 6.6.2.1-1 indicates that cross-frame members in horizontally curved I-girder bridges are to be classified as primary members. The maximum slenderness ratio is satisfactory.

## Slide 102: COMPRESSION MEMBERS Built-up members
Notes: The last topic in this lesson will cover the AASHTO LRFD design provisions for built-up compression members.

## Slide 103: Built-up Compression Members
Built-up compression members typically consist of two or more steel shapes, either:
  Closely spaced shapes (e.g., angles or channels) interconnected at intervals using welds or bolts/rivets or by intermittent bolted/riveted or welded filler/stay plates; or
  Widely spaced shapes or plates connected by lacing (i.e., flat bars, angles, channels, or other shapes), tie plates (also referred to as batten or stay plates), solid plates, or perforated cover plates (Slides 5 and 41). Solid plates and perforated plates are most commonly used in modern steel bridges; lacing and tie plates are now less commonly used.
Along the length of the built-up member between the end connections, the maximum longitudinal spacing or pitch of bolts must satisfy the spacing requirements for stitch bolts specified in AASHTO LRFD Article 6.13.2.6.3 (Lesson 11). At the ends of built-up compression members, bolts must also satisfy the maximum pitch requirements specified for the ends of these members in AASHTO LRFD Article 6.13.2.6.4.
Notes: As discussed previously for built-up tension members, built-up compression members also typically consist of two or more steel shapes, either: 1) closely spaced shapes (e.g., angles or channels) interconnected at intervals by intermittent bolted/riveted or welded filler/stay plates, or 2) widely spaced shapes or plates connected by lacing (i.e., flat bars, angles, channels, or other shapes), tie plates (also referred to as batten or stay plates), solid plates, or perforated cover plates. Illustrations of perforated cover plates, batten plates and lacing were shown previously on Slide 5 in this lesson. Solid plates and perforated cover plates are most commonly used to connect widely spaced shapes or plates in modern steel bridges; lacing and tie plates are now less commonly used. AASHTO LRFD Article C6.8.5.1 contains references where some limiting design proportions for batten plates and lacing bars may be found. AASHTO LRFD Article C6.9.4.3.1 also gives a reference for determining section properties (e.g., the moment of inertia and torsional constant) of latticed built-up members. Special design requirements for members composed of perforated plates in built-up compression members are discussed on Slide 108 of this lesson.
The design of built-up compression members is covered in AASHTO LRFD Article 6.9.4.3. In addition to other bolt spacing requirements specified in AASHTO LRFD Article 6.13.6.2 (i.e., minimum and maximum spacing, clear distance, and sealing requirements), the maximum longitudinal spacing or pitch of bolts along the length of the member between the end connections must satisfy the spacing requirements for stitch bolts specified in AASHTO LRFD Article 6.13.2.6.3 (Lesson 11). These maximum pitch requirements are intended to ensure that the individual components of the member act as a unit to transfer the required forces without buckling of the member. Note that the maximum pitch must also not exceed the maximum pitch for sealing specified in AASHTO LRFD Article 6.13.2.6.2. Consideration may be given to also applying the specified maximum pitch requirements to the spacing of intermittent welds used to connect built-up compression members. Built-up compression members should also satisfy the appropriate maximum slenderness ratio limit discussed previously on Slide 66 in this lesson (see also Slide 107 in this lesson).
As indicated in the Commentary to Section E6 of the AISC Specification, the ends of the member should be connected rigidly by welding or full-tension bolting, or by using end tie plates. Section E6 suggests designing bolted end connections of built-up compression members for the full compressive load as a bearing-type connection, with the bolts fully pretensioned and a Class A or B faying surface provided (Lesson 11). The Class A or B surface is not recommended to develop slip resistance in the bolts, but to help prevent relative moment between the components at the end as the member takes a curved shape (note that the shear is highest at the ends of the member where the slope of the buckled member is the greatest). At the ends of built-up compression members, bolts must also satisfy the maximum pitch requirements specified for the ends of these members in AASHTO LRFD Article 6.13.2.6.4 (Lesson 11).
The built-up compression rib in the historic Strawberry Mansion bridge is shown along with other built-up truss members.
Photo credit: Russo Structural Services

## Slide 104: Built-up Compression Members Nominal Compressive Resistance, Pn
The nominal compressive resistance, Pn, of built-up compression members is to be determined according to the provisions of AASHTO LRFD Article 6.9.4.1 (Slides 44 to 53).
For built-up compression members with cross-sections containing any slender cross-section elements (as defined on Slide 57), Pn is to be determined according to the provisions of AASHTO LRFD Article 6.9.4.2.2 to account for the effects of potential local buckling of the elements on the overall compressive resistance (Slides 54 to 64).
For built-up compression members with cross sections containing any longitudinally stiffened plates, Pn is to be determined according to the provisions of AASHTO LRFD Article E6.1.1 (Appendix E6).
For built-up compression members composed of two or more shapes, the effect of any relative deformation between the shapes that produces shear forces in the connectors between the individual shapes on the compressive resistance must be considered (next two slides).
Notes: The nominal compressive resistance, Pn, of built-up compression members is to be determined according to the provisions of AASHTO LRFD Article 6.9.4.1, as discussed previously on Slides 44 to 53 of this lesson. For built-up compression members with cross sections containing any slender cross-section elements, as defined previously on Slide 57 of this lesson, i.e., longitudinally unstiffened elements not satisfying the corresponding width-to-thickness or slenderness ratio limits specified in AASHTO LRFD Table 6.9.4.2.1-1 (or b/t > λr), Pn is to be determined according to the provisions of AASHTO LRFD Article 6.9.4.2.2 to account for the effects of potential local buckling of the elements on the overall compressive resistance, as discussed previously on Slides 54 to 64 of this lesson. For compression members with cross-sections containing any longitudinally stiffened plates, Pn is to be determined according to the provisions of AASHTO LRFD Article E6.1.1 (Appendix E6) to account for the action of the longitudinal stiffeners and their tributary plate widths acting as stiffener struts including any local buckling effects in slender longitudinally stiffened plate panels. These provisions are considered outside the scope of this course. Members composed of solid and/or perforated plates that are determined to be slender cross-section elements must also satisfy the provisions of AASHTO LRFD Article 6.9.4.5 (refer to Slides 63 and 64 of this lesson).
For built-up compression members composed of two or more shapes, the effect of any relative deformation between the shapes that produces shear forces in the connectors between the individual shapes on the compressive resistance must be considered, as discussed on the next two slides. Shear in a compression member can result due to lateral loads, end eccentricity of the axial load, and/or by the slope of the member with respect to the line of thrust of the axial load caused by bending during buckling or any unintended initial curvature. Shear has an insignificant effect on reducing the compressive resistance of sections with solid webs, and on box-section members built-up using perforated cover plates. However, the effect of shear on the compressive resistance for built-up compression members composed of two or more shapes should not be neglected.

## Slide 105: Built-up Compression Members Nominal Compressive Resistance, Pn
For built-up compression members composed of two or more shapes where the intermediate connectors between the shapes are welded or fully-tensioned bolted, the shear effect can be accounted for by using the following modified slenderness ratio, (K/r)m:
Eq. 6.9.4.3.1-1
where:
(K/r)o = slenderness ratio of the built-up member (with shear deformation neglected) acting as a unit in the buckling direction being considered
 = separation ratio = h/2rib
a = distance (center-to-center) between connectors (in.)
rib = radius of gyration of an individual component shape relative to its centroidal axis parallel to the member axis of buckling (in.)
h = distance between centroids of individual component shapes perpendicular to the member axis of buckling (in.)
Notes: The shear effect discussed on the preceding slide can be accounted for by an adjustment to the effective length of the member. AASHTO LRFD Article 6.9.4.3 specifies the following modified slenderness ratio, (K/r)m, for built-up members composed of two or more shapes where the buckling mode involves relative deformation that produces shear forces in connectors between the individual shapes. This modified ratio applies when the intermediate connectors between the shapes are welded or fully-tensioned bolted.
For example, for a built-up back-to-back double-angle or double-channel compression member interconnected at intervals along its length in the plane defined by the y-axis of the cross-section, (K/r)m would be used in place of (K/r)y for flexural buckling (FB) about the y-axis to account for the effect of the shear displacements between the shapes. Flexural buckling (FB) about the x-axis would be checked in conventional fashion, as shear effects would have no effect on buckling about the x-axis. Similarly, for the case of the same singly-symmetric back-to-back double-angle compression member with the y-axis defined as the plane of symmetry, Pey calculated using the modified (K/r)m in place of (K/r)y, would be used in the flexural-torsional buckling (FTB) equation given on Slide 50 of this lesson. The nominal compressive resistance in this case would then be computed as the smaller value based on either flexural buckling (FB) about the x-axis or flexural-torsional buckling (FTB), which involves torsion of the member in combination with flexure about the y-axis.

## Slide 106: Built-up Compression Members Nominal Compressive Resistance, Pn
For built-up compression members composed of two or more shapes that are built-up using other types of intermediate connectors, including those members on existing structures that are interconnected with rivets, the shear effect should be accounted for by using the following modified slenderness ratio, (K/r)m:
Eq. C6.9.4.3.1-1
where:
(K/r)o = slenderness ratio of the built-up member (with shear deformation neglected) acting as a unit in the buckling direction being considered
a = distance (center-to-center) between connectors (in.)
ri = minimum radius of gyration of an individual component shape (in.)
Notes: AASHTO LRFD Article C6.9.4.3.1 gives the alternate equation for (K/r)m shown on this slide assumed applicable to compression members, for which shear-force effects are a concern, that are built-up using two or more shapes with other types of intermediate connectors, including those members on existing structures that are interconnected with rivets. This equation is based on the equation given in Section E6 of the AISC Specification for application to built-up compression members in which the intermediate connectors are snug-tight bolted.
As mentioned in AASHTO LRFD Article C6.9.4.3.1, the connectors in built-up compression members must be designed to resist the shear forces that develop in the buckled member whenever the equation on this slide or on the preceding slide are employed, but no additional guidance is offered. It is suggested in Chapter 4 of the NSBA SBDH that the additional transverse shear force due to stability effects, given on Slide 108 of this lesson, might be used to design the connectors in such cases.

## Slide 107: Built-up Compression Members Nominal Compressive Resistance, Pn
For built-up compression members composed of two or more shapes interconnected at intervals, the slenderness ratio of each component shape between connecting fasteners or welds must not exceed 75 percent of the governing slenderness ratio of the built-up member (AASHTO LRFD Article 6.9.4.3.1).
Lacing members and/or tie plates are to be spaced such that the slenderness ratio of each component shape between the lacing and/or tie-plate connection points does not exceed 75 percent of the governing slenderness ratio of the built-up member.
The least radius of gyration is to be used in computing the slenderness ratio of each component shape between the connectors or connection points.
Notes: In addition, AASHTO LRFD Article 6.9.4.3.1 specifies that for built-up compression members composed of two or more shapes interconnected at intervals, the slenderness ratio of each component shape between connecting fasteners or welds (i.e., the maximum value of a/rib or a/ri for each shape, as applicable) must not exceed 75 percent of the governing slenderness ratio of the built-up member. Also, lacing members and/or tie plates are to be spaced such that the slenderness ratio of each component shape between the lacing and/or tie-plate connection points does not exceed 75 percent of the governing slenderness ratio of the built-up member. In each case, the least radius of gyration is to be used in computing the slenderness ratio of each component shape between the connectors or connection points. Formulas giving approximate radii of gyration for various potential configurations of built-up members are provided in Table A1 of Salmon and Johnson Steel Structures – Design and Behavior. This requirement is intended to mitigate the possibility of so-called compound buckling, or the interaction between global buckling of the built-up member and local buckling of the individual components between intermediate connectors or lacing and/or tie-plate connection points.
Built-up laced columns supporting the approach spans of the Strawberry Mansion Bridge are shown in the photo on this slide.
Photo credit: Russo Structural Services

## Slide 108: Built-up Compression Members Nominal Compressive Resistance, Pn
Design requirements for perforated cover plates used in built-up compression members are given in AASHTO LRFD Article 6.8.5.2 (Slide 39).
In addition, for built-up compression members utilizing perforated cover plates, AASHTO LRFD Article 6.9.4.3.2 specifies that the perforated plates must be designed for the sum of the shear force due to the factored loads and an additional transverse shear force, V, due to stability effects assumed divided equally to each plane containing a perforated plate, taken as:
Eq. C6.9.4.3.2-1
where:
Pr = factored compressive resistance (kips)
 = member length (in.)
r = radius of gyration about an axis perpendicular to the plane of the perforated plate (in.)
Notes: As mentioned previously, perforated cover plates are more likely to be used for built-up members in new bridge construction than laced or battened compression members. Specific design requirements for perforated cover plates used in built-up compression members are given in AASHTO LRFD Article 6.8.5.2, as summarized previously on Slide 39 in this lesson. Also, when checking for slender cross-section elements, λr in the first row of AASHTO LRFD Table 6.9.4.2.1-1 under elements supported along two longitudinal edges (refer to Slide 56 in this lesson) should be checked taking b as the distance between the edge supports of the perforated plate. Should it be determined that the perforated plate is a slender cross-section element according to this check, the provisions of AASHTO LRFD Article 6.9.4.5 should also be satisfied (refer to Slides 63 and 64 in this lesson). A separate check should also be made of λr in the last row of AASHTO LRFD Table 6.9.4.2.1-1 under elements supported along one longitudinal edge (refer to Slide 55 in this lesson) taking b as the projecting width from the edge of the perforation to a single edge support.
In addition, for built-up compression members utilizing perforated cover plates, AASHTO LRFD Article 6.9.4.3.2 specifies that the perforated plates must be designed for the sum of the shear force due to the factored loads (i.e., the shear due to self-weight of the member plus any additional applied force), and an additional transverse shear force, V (kips), due to stability effects, assumed divided equally to each plane containing a perforated plate, as given by the equation on this slide. Consideration should also be given to applying this equation to any built-up compression member design in which lacing might be used.

## Slide 109: Lesson 12 Summary – Tension and Compression Members
Tension Members
  Introduction
  Factored Tensile Resistance
  Limiting Slenderness Ratios
  Combined Loading
  Built-up Members
Compression Members
  Introduction
  Factored Compressive Resistance
  Limiting Slenderness Ratios
  Combined Loading
  Single-Angle Members
  Built-up Members
Notes: This slide summarizes the various topics that were covered in Lesson 12 on tension and compression members.
The topics that were covered on tension members in this lesson included an introduction to the different types of tension members that are typically utilized in steel-bridge structures, the calculation of the factored tensile resistance of these members using the AASHTO LRFD provisions (including illustrative examples), the limiting slenderness ratios that apply to these members, the design for combined loading on these members; i.e., loading consisting of any combination of axial tension, uniaxial or biaxial flexure, and flexural and/or torsional shear, and the design of built-up tension members.
The topics that were covered on compression members in this lesson included an introduction to the different types of compression members that are typically utilized in steel-bridge structures, the calculation of the factored compressive resistance of these members using the AASHTO LRFD provisions, the limiting slenderness ratios that apply to these members, the design for combined loading on these members; i.e., loading consisting of any combination of axial compression, uniaxial or biaxial flexure, and flexural and/or torsional shear (which included an example illustrating the application of the these provisions to the design of a tee-section top lateral bracing member in a straight tub-girder bridge), the special design requirements for single-angle compression members (which included an example illustrating the application of these provisions to the design of a single-angle member serving as the bottom strut of a cross-frame in a horizontally curved I-girder bridge), and the design of built-up compression members.

## Slide 110: END