## Slide 1
Combined Forces Design
THEORY SLIDES
Developed by Scott Civjan
University of Massachusetts, Amherst
Teaching Modules for
Steel Instruction

## Slide 2
2
Pa
Pb
Ma
Va
Mb
COMBINED FORCES:
Structural member subjected to axial load, bending and shear
Vb
Notes: 2

## Slide 3
Major Issues to Address:
Combination of multiple states of stress.
Second Order load effects.
COMBINED FORCES:
Direct analysis versus traditional K methods.

## Slide 4
Combination of multiple states of stress:
Bending about the major and minor axis will combine to provide maximum stresses in the corner of a W shape.
Axial load will provide uniform stresses across the member and add to other maximum stresses.
s1=Mxcy/Ix
s3=P/A
s2=Mycx/Iy
(elastic range)

## Slide 5
Combination of multiple states of stress
Bending in each direction occurs simultaneously with associated shear stresses.
For elastic analysis one can superimpose stresses and arrive at a maximum value.
Once behavior becomes inelastic the resulting stresses are very difficult to calculate.
Actual design may include inelastic behavior and needs to account for residual stresses.

## Slide 6
Combination of multiple states of stress
Design provisions are simplified and rely on the inherent ductility of steel to redistribute stresses throughout the section.
The basic principle for design is an interaction equation which combines axial and bending forces with shear being checked independently.
Modes of failure from all independent modes are analyzed independently of other modes and forces. This does not capture complete behavior, but is sufficiently accurate for design purposes.

## Slide 7
Second Order Effects
Equilibrium is based on DEFORMED GEOMETRY.
Initially, consider a member subjected to flexure only.

## Slide 8
d0
Second Order Effects
Equilibrium is based on DEFORMED GEOMETRY.
Initially, consider a member subjected to flexure only.
Application of load results in mid-span deflection d0,
from basic derivations.

## Slide 9
Second Order Effects
Equilibrium is based on DEFORMED GEOMETRY.
Now consider the same member with Axial load P.
P
P

## Slide 10
Second Order Effects
Equilibrium is based on DEFORMED GEOMETRY.
Axial force acting through deformations results in additional moment P(d0) at center of span.
d0
P
P

## Slide 11
Axial force acting through deformations results in additional moment P(d0) at center span.
Second Order Effects
Equilibrium is based on DEFORMED GEOMETRY.
Additional moment then results in displacement d’.
P
P
11
d0
d’
Notes: 11

## Slide 12
Axial force acting through deformations results in additional moment P(d0) at center span.
Second Order Effects
Equilibrium is based on DEFORMED GEOMETRY.
Additional moment then results in displacement d’.
P
P
12
d0
d’
Resulting in additional moment P(d’)
Notes: 12

## Slide 13
Axial force acting through deformations results in additional moment P(d0) at center span.
Second Order Effects
Equilibrium is based on DEFORMED GEOMETRY.
Additional moment then results in displacement d’.
P
P
13
d0
d’
Resulting in additional moment P(d’)
Notes: 13

## Slide 14
Second Order Effects
Equilibrium is based on DEFORMED GEOMETRY.
This either results in an incremental failure,or stabilizes.
d > d0 and M > M0
M = M0 + Pd
but d depends on M…
where d0 and M0 are first order results based on original geometry.

## Slide 15
Second Order Effects
When considering a frame with loads applied at joints the same principles can be applied.
In these cases, we define joint deflections as D, with D0 being the first order joint deflection.

## Slide 16
Second Order Effects
P
P

## Slide 17
17
P
P
H
D0
Second Order Effects

## Slide 18
18
P
P
H
D0
D’
D
Second Order Effects

## Slide 19
Tension forces on a member tend to “straighten” the member. Usually, they do not introduce 2nd order effects.
Multiple states of stress are still present and need to be accounted for.
Tension in a member can also make lateral torsional buckling less likely to occur.
Tension forces and Flexure
Second Order Effects

## Slide 20
INDIVIDUAL MEMBERS
2nd Order Analysis Theory
Second Order Effects

## Slide 21
D0
H
Mmax= HL
Moment Diagram
L
Assuming deflections are in the shape of a sine curve
Second Order Effects

## Slide 22
D0
H
L
22
P
Mmax = HL + PD
D’
D
Assuming deflections are in the shape of a sine curve
Moment Diagram
Second Order Effects
Notes: 22

## Slide 23
D0
H
L
23
P
D’
D
, due to PD
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 23

## Slide 24
D0
H
L
24
P
D’
D
, due to PD
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 24

## Slide 25
D0
H
L
25
P
D’
D
, due to PD
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 25

## Slide 26
D0
H
L
26
P
D’
D
, due to PD
Since
, and
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 26

## Slide 27
D0
H
L
27
P
D’
D
, due to PD
Since
and
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 27

## Slide 28
Assuming deflections are in the shape of a sine curve
D0
H
L
28
P
D’
D
Mmax = HL + PD = M0 + PD
Second Order Effects
Notes: 28

## Slide 29
D0
H
L
29
P
D’
D
Mmax = HL + PD = M0 + PD
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 29

## Slide 30
D0
H
L
30
P
D’
D
Mmax = HL + PD = M0 + PD
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 30

## Slide 31
D0
H
L
31
P
D’
D
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 31

## Slide 32
D0
H
L
32
P
D’
D
Assuming deflections are in the shape of a sine curve
Second Order Effects
Notes: 32

## Slide 33
D0
H
L
33
P
D’
D
Assuming deflections are in the shape of a sine curve
For design Cm is usually taken equal to 1 for this condition (translation of member ends), calculated for the condition where deflections are within a member length (P-d).
Second Order Effects
Notes: 33

## Slide 34
H+PD/L
L
34
D
Note that the maximum moment is similar to this case:
Mmax = HL + PD
Moment Diagram
Second Order Effects
Notes: 34

## Slide 35
H+PD/L
L
35
D
Note that the maximum moment is similar to this case:
However, the shape of the moment diagram is slightly altered,
now assumed to be a straight line.
Previous case moment
Mmax = HL + PD
Moment Diagram
Second Order Effects
Notes: 35

## Slide 36
H+PD/L
L
36
D
Note that the maximum moment is similar to this case:
Second Order Effects
Notes: 36

## Slide 37
H+PD/L
L
37
D
Note that the maximum moment is similar to this case:
Second Order Effects
Notes: 37

## Slide 38
H+PD/L
L
38
D
Note that the maximum moment is similar to this case:
Second Order Effects
Notes: 38

## Slide 39
H+PD/L
L
39
D
Note that the maximum moment is similar to this case:
Second Order Effects
Notes: 39

## Slide 40
H+PD/L
L
40
D
Note that the maximum moment is similar to this case:
Second Order Effects
Notes: 40

## Slide 41
H+PD/L
L
41
D
Note that the maximum moment is similar to this case:
Second Order Effects
Notes: 41

## Slide 42
H+PD/L
L
42
D
Note that the maximum moment is similar to this case:
Second Order Effects
Notes: 42

## Slide 43
P
P
P
2H
H
H
D0
D’
D = (Amplification Factor)D0
The previous theory is applicable to deflections and moments within a single member.
General equations are similar.
43
D0
H
L
D’
D

## Slide 44
Amplification factors approach infinity as P approaches Pe
Axial Force, P
Amplification Factor
1.0
Pe
Second Order Effects

## Slide 45
Transverse Load on Beam
Mid Span Deflection, d
P = 0 No amplification of M or d
P1 > 0 Amplification of M and d
P2 = 2xP1 Amplification of M and d is GREATER than P1 results times 2
45
Therefore, can not superimpose results from different P values.
Second Order Effects
Notes: 45

## Slide 46
MEMBERS WITHIN STRUCTURE
Second Order Effects

## Slide 47
H
L
P4
P3
P2
P1
47
Note that in a full structure all displacements within a story are similar.
Second Order Effects
Notes: 47

## Slide 48
Note that in a full structure all displacements within a story are similar.
H
L
P4
P3
P2
P1
48
D
D
Second Order Effects
Notes: 48

## Slide 49
H
L
49
D
D
Note that in a full structure all displacements within a story are similar.
P4
P3
P2
P1
Second Order Effects
Notes: 49

## Slide 50
H
L
50
P4
P3
P2
P1
This concept is directly applicable to the case of “Leaner Columns” as discussed in the Compression Member module.
Second Order Effects
Notes: 50

## Slide 51
H
L
51
D
D
P4
P3
P2
P1
This concept is directly applicable to the case of “Leaner Columns” as discussed in the Compression Member module.
Second Order Effects
Notes: 51

## Slide 52
NOTIONAL LOADS

## Slide 53
Notional loads are a function of the gravity load being applied.
Notional loads are applied as a lateral load at each floor level in the direction that adds to the destabilizing effects of the load combination being considered.
Notional loads can account for geometric imperfections, inelasticity of members, and other non-ideal conditions.
Notional Loads
Notional loads can be thought of as representing an initial out-of-plumbness in each story of the structure of 1/500 times the story height.

## Slide 54
Recall that a vertical load acting through a displacement, D, is similar to the application of a horizontal load PD/L.
Therefore, a notional load can be considered the equivalent effect of an assumed geometric imperfection, D.
Notional Loads
H+PD/L
L
D
H
L
P
D

## Slide 55
DIRECT ANALYSIS

## Slide 56
DIRECT ANALYSIS METHOD
Analysis of entire structure interaction.
Additional lateral “Notional” loads.
No K values required.
Reduced stiffness of structure.
Notes: Alternatively, Direct Analysis Methods are more common in international codes and are now introduced in AISC publications, with the likelihood of being the dominant design method in the future. This method is also easier to program for analysis and design in typical software packages. In this method, all members are designed as beam-columns with a “K” factor of 1.0. However, to account for structure interaction a series of notional loads are applied to the structure to develop moments in all “columns”, and these combined forces are calibrated to column capacities with K=1. As will be shown in beam-column modules these loads are based on rational principles, but require a slight “leap of faith” from the students to accept their values. If this method is chosen for instruction, it may be preferable to skip to beam-column design directly after addressing single column behavior and design.

## Slide 57
Moment, M
Axial Force, P
Initially consider a “traditional” analysis
57
DIRECT ANALYSIS METHOD
Notes: 57

## Slide 58
Moment, M
Axial Force, P
Initially consider a “traditional” analysis
58
PnKL
Py
Axial strength is defined as PnKL which includes K factors (Py indicates crushing).
DIRECT ANALYSIS METHOD
Notes: 58

## Slide 59
Moment, M
Axial Force, P
Initially consider a “traditional” analysis
59
PnKL
Py
Axial strength is defined as PnKL which includes K factors (Py indicates crushing).
Bending Strength is defined as Mn, assumed here to be Mp for a laterally braced member.
Mp
DIRECT ANALYSIS METHOD
Notes: 59

## Slide 60
Moment, M
Axial Force, P
60
PnKL
Py
Mp
Pu
Mu
Elastic 2nd Order
Traditional design accounts for interaction by calibrating the member design to column curves.
DIRECT ANALYSIS METHOD
Notes: 60

## Slide 61
Moment, M
Axial Force, P
61
PnKL
Py
Mp
Pu
Mu
Elastic 2nd Order
Traditional design accounts for interaction by calibrating the member design to column curves.
Actual Response
Actual response produces a higher internal moment in the member. This is accounted for in calibrating the member check, but does not get transferred into adjacent members and connections.
DIRECT ANALYSIS METHOD
Notes: 61

## Slide 62
Moment, M
Axial Force, P
62
PnKL
Py
Mp
Pu
Mu
Elastic 2nd Order
Actual Response
DIRECT ANALYSIS METHOD
Notes: 62

## Slide 63
Moment, M
Axial Force, P
63
Now consider the “Direct” analysis
DIRECT ANALYSIS METHOD
Notes: 63

## Slide 64
Moment, M
Axial Force, P
64
Py
Now consider the “Direct” analysis
PnL
Axial strength is defined as PnL which assumes K=1 for all cases.
DIRECT ANALYSIS METHOD
Notes: 64

## Slide 65
Moment, M
Axial Force, P
65
Py
Now consider the “Direct” analysis
PnL
Axial strength is defined as PnL which assumes K=1 for all cases.
Mp
Bending strength is defined as Mn, assumed here to be Mp for a laterally braced member.
DIRECT ANALYSIS METHOD
Notes: 65

## Slide 66
Moment, M
Axial Force, P
66
Py
Now consider the “Direct” analysis
PnL
Axial strength is defined as PnL which assumes K=1 for all cases.
Mp
Bending strength is defined as Mn, assumed here to be Mp for a laterally braced member.
PnKL
Therefore, design curve is shifted upwards from traditional assumptions.
DIRECT ANALYSIS METHOD
Notes: 66

## Slide 67
Moment, M
Axial Force, P
67
Py
PnL
Mp
Pu
Mu
Elastic 2nd order (direct analysis includes notional loads and reduced stiffness).
Direct analysis accounts for interaction by including additional lateral “notional” loads and reducing the frame stiffness thus calibrating the member design to K = 1 analysis.
DIRECT ANALYSIS METHOD
Notes: 67

## Slide 68
Moment, M
Axial Force, P
68
Py
PnL
Mp
Pu
Mu
Elastic 2nd order (direct analysis includes notional loads and reduced stiffness).
Actual Response
Actual response then should match the internal moment, transferring this moment into adjacent members and connections during analysis.
DIRECT ANALYSIS METHOD
Direct analysis accounts for interaction by including additional lateral “notional” loads and reducing the frame stiffness thus calibrating the member design to K = 1 analysis.
Notes: 68

## Slide 69
Moment, M
Axial Force, P
DIRECT ANALYSIS METHOD
69
Py
PnL
Mp
Pu
Mu
Elastic 2nd order (direct analysis includes notional loads and reduced stiffness).
Actual Response
Notes: 69

## Slide 70
DIRECT ANALYSIS METHOD
Direct Analysis and Traditional methods are valid for design.
Each is reliant on calibration to match the response curves shown on previous slides.
The Direct Analysis method has been calibrated for typical building structures. Unusual structures (such as a cantilever with compression and bending) may require additional calibration.

## Slide 71
DIRECT ANALYSIS METHOD
Analysis and Calibration
With proper calibration design strength approaches the actual response.
Calibration consists of a combination of notional load values and reduction in member stiffness.
Analysis is referenced to K = 1 member capacities.

## Slide 72
MODELING ISSUES

## Slide 73
Second Order Effects
Final deflections and moments can be calculated in several different ways.
Closed form mathematical solutions:
Derivations exist for standard results, but very difficult, if not impossible, for a full structure.
Approximate Methods:
Amplification factor applied to first order displacement and moments by simple method
OR
approximate computer methods will provide results within a given tolerance.

## Slide 74
Amplified First Order Analysis
Computer Analysis
Exact Closed-Form Solution
2nd order analysis is any method that accounts for P-D and P-d effects.
Second Order Effects

## Slide 75
Exact solutions for P-d and P-D can be derived for simple structures.
Exact Closed-Form Solution
For full structures typically encountered in design the process is generally too tedious to perform.

## Slide 76
Most structural analysis programs will include some form of “second order” analysis.
Computer Analysis
To satisfy a “rigorous 2nd order analysis” a program must include both P-∆ and P-δ analysis, or the designer must verify that P-δ effects are minimal in the structure.
Computer software uses approximate solutions rather than exact closed form solutions, and iterate until a specified error tolerance is reached.

## Slide 77
Verify that load combinations include second order effects. Some programs analyze individual load cases only. Load case results are factored and summed to produce load combinations, but are not re-analyzed.
Designers must verify that second order effects are correctly handled by the programs being used.
Therefore, moments resulting from lateral loads in one load case may not be correctly amplified by axial load in a separate load case when combined in a load combination.
Computer Analysis

## Slide 78
Verify computer programs correctly analyze load combinations.
78
H
P
P
+
Load Case 2
Load Case 1
Computer Analysis

## Slide 79
Verify computer programs correctly analyze load combinations.
79
P
P
H
Compare 2nd order analysis from the load combination and load case 3. If results are identical, the program correctly includes 2nd order analysis in load combinations.
Load Combination (LC1+LC2)
OR
Load Case 3
H
P
P
+
Load Case 2
Load Case 1
Computer Analysis

## Slide 80
Designers must verify that second order effects are correctly handled by the programs being used.
80
Computer Analysis

## Slide 81
Most programs only include P-∆. If P-δ effects are significant the designer can use multiple elements to provide equivalent P-∆ effects within the original element.
Designers must verify that second order effects are correctly handled by the programs being used.
To determine the capabilities of a specific program compare first and second order analysis results for known load cases – typically a flagpole (P-∆) and simple beam (P-δ) with axial and lateral loads applied. (Figures C-C2-2 and C-C2-3)
Computer Analysis

## Slide 82
Computer Analysis
P
P
H
Some computer programs do not analyze P-d effects such as the case shown.
d

## Slide 83
83
P
P
H
Some computer programs do not analyze P-d effects such as the case shown.
d
P
P
H
Provide additional joints in the member.
Member shown is now made up of 4 shorter members.
Computer Analysis

## Slide 84
84
P
P
H
Some computer programs do not analyze P-d effects such as the case shown.
d
P
P
H
Provide additional joints in the member
(Member shown is now made up of 4 shorter members)
D1
D1
D2
P-d analysis of the overall member is now analyzed as P-D analysis of each individual member, which most programs will be able to analyze.
Such an analysis is only required for members which will have significant P-d effects
Computer Analysis

## Slide 85
Braced frames with pinned member connections:
If loads applied at the nodes, members are subjected to axial forces only.
Combined Forces
Beams and girders may be subjected to combined forces, but designers should take care in understanding whether analysis results represent compressive forces present in the steel section or carried by the floor slab.

## Slide 86
Moment frames with fixed member connections:
Most if not all members will be subjected to a combination of axial forces, flexure and shear.
Combined Forces